EFI Developer’s Guide

Version 0.99

May 4, 2000

THIS SPECIFICATION IS PROVIDED "AS IS" WITH NO WARRANTIES  WHATSOEVER, INCLUDING ANY WARRANTY OF MERCHANTABILITY,  FITNESS FOR ANY PARTICULAR PURPOSE, OR ANY WARRANTY OTHERWISE ARISING OUT OF ANY PROPOSAL, SPECIFICATION OR SAMPLE.

A license is hereby granted to copy and reproduce this specification for internal use only.

No other license, express or implied, by estoppel or otherwise, to any other intellectual property rights is granted herein.

Intel disclaims all liability, including liability for infringement of any proprietary rights, relating to implementation of information in this specification.  Intel does not warrant or represent that such implementation(s) will not infringe such rights.

† Third-party trademarks are the property of their respective owners.

|  | Copyright ( 1999. Intel Corporation, All Rights Reserved. |
| --- | --- |

Revision History

| Revision | Revision History | Date | Author |
| --- | --- | --- | --- |
| 0.1 | Initial review draft | 5/3/99 | Intel Corporation |
| 0.2 | Updated for the 0.91 Sample Implementation | 7/14/99 | Intel Corporation |
| 0.9 | Updated for the 0.91.009 Sample Implementation | 11/18/99 | Intel Corporation |
| 0.99 | Updated for the 0.99.12.20 Sample Implementation | 05/04/00 | Intel Corporation |

Table of Contents

1 Introduction	10

1.1	Organization of this Document	11

1.2	Goals	11

1.3	Target Audience	11

1.4	Prerequisite Specifications	11

1.5	Conventions Used in This Document	11

1.5.1	Typographic Conventions	12

2 EFI Shell	13

2.1	Invocation of the EFI Shell	13

2.2	EFI Shell Command Syntax	13

2.2.1	Variable Substitution	13

2.2.2	Wildcard Expansion	13

2.2.3	Output Redirection	14

2.2.4	Quoting	15

2.2.5	Execution of Batch Scripts	15

2.2.6	Error Handling in Batch Scripts	16

2.2.7	Comments in Script Files	16

2.3	EFI Shell Commands	17

2.3.1	help	19

2.3.2	guid	20

2.3.3	set	21

2.3.4	alias	22

2.3.5	dh	23

2.3.6	map	25

2.3.7	cd	27

2.3.8	echo	28

2.3.9	for	29

2.3.10	if	30

2.3.11	goto	31

2.3.12	pause	32

2.3.13	exit	33

2.3.14	attrib	34

2.3.15	bcfg	35

2.3.16	comp	37

2.3.17	cp	38

2.3.18	cls	39

2.3.19	date	40

2.3.20	edit	41

2.3.21	hexedit	42

2.3.22	load	43

2.3.23	ls	44

2.3.24	memmap	45

2.3.25	mkdir	47

2.3.26	mode	48

2.3.27	nshell	49

2.3.28	rm	50

2.3.29	time	51

2.3.30	type	52

2.3.31	ver	53

2.3.32	vol	54

2.3.33	dblk	55

2.3.34	dmem	57

2.3.35	dmpstore	59

2.3.36	err	61

2.3.37	getmtc	62

2.3.38	mm	63

2.3.39	mv	64

2.3.40	pci	65

2.3.41	reset	66

2.3.42	setsize	67

2.3.43	stall	68

2.3.44	touch	69

3 Writing EFI Shell Commands	70

3.1	Writing a Shell Command	70

3.2	Compiling a Shell Command	72

3.3	Adding Commands to the EFI Shell	74

3.4	Removing Commands from the EFI Shell	74

4 EFI Applications	75

4.1	Writing EFI Applications	75

4.2	Compiling EFI Applications	77

4.3	Writing EFI Applications with EFI Library Support	77

4.4	Running EFI Applications	79

5 EFI OS Loaders	80

5.1	Device Path and Image Information of the OS Loader	81

5.2	Accessing Files in the Device Path of the OS Loader	81

5.3	Finding the OS Partition	82

5.4	Getting the Current System Configuration	82

5.5	Getting the Current Memory Map	83

5.6	Getting Environment Variables	83

5.7	Transitioning to an OS Kernel	84

A EFI Boot Time Services	85

A.1	Event Services	85

A.2	Memory Allocation Services	86

A.3	Protocol Handler Services	86

A.4	Image Services	87

A.5	Miscellaneous Services	87

B EFI Run Time Services	88

B.1	Variable Services	88

B.2	Time Services	88

B.3	Virtual Memory Services	89

B.4	Miscellaneous Services	89

C EFI Protocol Interfaces	90

C.1	Device Path Protocol	90

C.2	Device I/O Protocol	91

C.3	Simple Input Protocol	91

C.4	Simple Text Output Protocol	92

C.5	Block I/O Protocol	92

C.6	Disk I/O Protocol	92

C.7	Simple File System Protocol	93

C.8	File System Protocol	93

C.9	Load File Protocol	93

C.10	Loaded Image Protocol	94

C.11	Serial I/O Protocol	94

C.12	Unicode Collation Protocol	94

C.13	PXE I/O Protocol	95

C.14	Simple Network Protocol	96

D EFI Library Functions and Macros	97

D.1	Initialization Functions	98

D.2	Linked List Support Macros	98

D.3	String Functions	99

D.4	Memory Support Functions	100

D.5	CRC Support Functions	100

D.6	Text I/O Functions	101

D.7	Math Functions	102

D.8	Spin Lock Functions	102

D.9	Handle and Protocol Support Functions	103

D.10	File I/O Support Functions	103

D.11	Device Path Support Functions	104

D.12	PCI Functions and Macros	105

D.13	Miscellaneous Functions and Macros	106

E Sample OS Loader Listing	107

F Sample OS Loader Output	115

Tables

Table 1-1.	Specification Organization and Contents	11

Table 2-1.	Wildcard Character Expansion	14

Table 2-2.	Output Redirection Syntax	15

Table 2-3.	List of Internal EFI Shell Commands	17

Table 2-4.	List of External EFI Shell Commands	17

Table 2-5.	List of Debug EFI Shell Commands	18

Table A-1.	Event Services	85

Table A-2.	Memory Allocation Services	86

Table A-3.	Protocol Handler Services	86

Table A-4.	Image Services	87

Table A-5.	Miscellaneous Services	87

Table B-1.	Variable Services	88

Table B-2.	Time Services	88

Table B-3.	Virtual Memory Services	89

Table B-4.	Miscellaneous Services	89

Table C-2.	Device I/O Protocol Interfaces	91

Table C-3.	Simple Input Protocol Interfaces	91

Table C-4.	Simple Text Output Protocol Interfaces	92

Table C-5.	Block I/O Protocol Interfaces	92

Table C-6.	Disk I/O Protocol Interfaces	92

Table C-7.	Simple File System Protocol Interfaces	93

Table C-8.	File System Protocol Interfaces	93

Table C-9.	Load File Protocol Interfaces	93

Table C-10.	Loaded Image Protocol Interfaces	94

Table C-11.	Serial I/O Protocol Interfaces	94

Table C-12.	Unicode Collation Protocol Interfaces	94

Table C-13.	PXE I/O Protocol Interfaces	95

Table C-14.	Simple Network Protocol Interfaces	96

Table D-1.	Initialization Functions	98

Table D-2.	Linked List Support Macros	98

Table D-3.	String Functions	99

Table D-4.	Memory Support Functions	100

Table D-5.	CRC Support Functions	100

Table D-6.	Text I/O Functions	101

Table D-7.	Math Functions	102

Table D-8.	Spin Lock Functions	102

Table D-9.	Handle and Protocol Support Functions	103

Table D-10.	File I/O Support Functions	103

Table D-11.	Device Path Support Functions	104

Table D-12.	Miscellaneous Functions and Macros	105

Table D-13.	Miscellaneous Functions and Macros	106

# Introduction

1The Extensible Firmware Interface (EFI) Specification describes a set of Application Program Interfaces (APIs) and data structures that are exported by a system’s firmware.  Software that takes advantage of these APIs and data structures may take one of many forms.  These include an EFI device driver, an EFI shell, an EFI system utility, an EFI system diagnostic, or an Operating System (OS)  loader.  In addition, the EFI Specification describes a set of run-time services that are available to an OS while the OS has full control of the system.

The sample implementation of the EFI Specification includes an EFI Shell.  An EFI Shell is a special type of EFI Application that allows other EFI Applications to be launched.  The combination of the EFI firmware and the EFI Shell provide an environment that can be modified to easily adapt to many different hardware configurations.  The EFI shell is a simple, interactive environment that allows EFI device drivers to be loaded, EFI applications to be launched, and operating systems to be booted.  In addition, the shell also provides a set of basic commands used to  manage files and the system environment variables.

An EFI application has access to the APIs and data structures exported by the EFI firmware.  An EFI application may be any number of things including a system utility, a system diagnostic, or an OS loader.  Many of the EFI Shell commands are implemented as EFI applications. An OS loader is a special type of EFI application because it typically will load a number of other files related to the OS  into memory, and then transfer control an OS kernel.  During this process, the OS loader may collect the system’s configuration information that is maintained by the EFI firmware and put it into a form that can be used by the OS kernel.

An EFI device driver provides a set of interfaces that allow communication with a hardware device.  The types of devices that are typically available in the EFI environment include keyboard, display, hard drive, network, CD-ROM, floppy, etc.  The EFI Specification provides mechanisms to add new types of device drivers to the base firmware so new types of devices can be accessed from the EFI environment and presented to the OS loader during the boot process.  These device drivers can be loaded from the system’s non-volatile storage, a PCI Option ROM, or any system device that is natively supported by the EFI environment.  Device drivers are very similar to EFI applications.  They have the same access to all the APIs and data structures.  The main difference is that they typically add a set of interfaces that provide access to a hardware device.  When the device driver exits, the EFI device driver stays resident in memory, so those interfaces may be used by other types of EFI applications to access the hardware device.

The sample implementation of the EFI firmware and the EFI shell includes a set of library functions and macros.  These functions and macros represent one possible minimal implementation of the EFI environment.  Together, the EFI APIs and EFI library functions, provide the functionality required for basic console I/O, basic disk I/O, memory management, and string manipulation.  The EFI library also provides functions for 64-bit math operations, CRC checks, spin locks, and helper functions to manage device handle, device protocol, and device paths.  The appendices in this document contain a complete list of the APIs, library functions, and library macros that are available to an EFI developer.  Please refer to the appropriate specification for complete details on all the APIs and macros.

## Organization of this Document

This specification is organized as follows:

Table 1-1.	Specification Organization and Contents

| Chapter | Description |
| --- | --- |
| Chapter 1: Introduction | Introduction to EFI Development. |
| Chapter 2: EFI Shell | Overview of EFI shell commands. |
| Chapter 3: Writing EFI Shell Commands | Describes how to write, compile, and run EFI Shell commands . |
| Chapter 4 : EFI Applications | Describes how to write, compile, and run EFI Applications. |
| Chapter 5: EFI OS Loaders | Describes how to write an EFI OS loader. |
| Appendix A: EFI Boot Time Services | List and high level description of EFI Boot Time Services. |
| Appendix B: EFI Run Time Services | List and high level description of EFI Run Time Services. |
| Appendix C: EFI Protocol Interfaces | List and high level description of EFI Protocol Interfaces. |
| Appendix D: EFI Library Overview | List and high level description of EFI Library functions. |
| Appendix E: Sample OS Loader Listing | C source code to OS Loader sample. |
| Appendix F: Sample OS Loader Output | Output from OS Loader sample. |

## Goals

The primary goal of  this document is to provide an overview of the EFI environment and its capabilities. This includes using the EFI shell, writing EFI applications, and writing EFI device drivers.

## Target Audience

This document is intended for the following readers:

- Developers who will be utilizing and writing applications, including tests and diagnostics, OS loaders, and device drivers for the EFI environment.

## Prerequisite Specifications

Extensible Firmware Interface Specification Version 0.9, Intel Corporation, 1999.

EFI Library Specification Version 0.9, Intel Corporation , 1999.

## Conventions Used in This Document

This document uses typographic and illustrative conventions described below.

### Typographic Conventions

The following typographic conventions are used in this document to illustrate programming concepts:

Prototype	This typeface is use to indicate prototype code.

Argument	This typeface is used to indicate arguments.

Name		This typeface is used to indicate actual code or a programming construct.

register		This typeface is used to indicate a processor register.

# EFI Shell

This section describes the features of the EFI Shell.  The EFI Shell supports a command line interface, batch scripting, a set of internal shell commands, and a set of external shell commands.

## Invocation of the EFI Shell

When the EFI Shell is invoked, it first looks for commands in the file startup.nsh on the execution path defined by the environment.  There is no requirement for a startup file to exist. Once the startup file commands are completed, the shell looks for commands from console input device.

## EFI Shell Command Syntax

The EFI Shell implements a programming language that provides control over the execution of individual commands.  When the shell scans its input, it always treats certain characters specially: (#, >, %, *, ?, [, ^, space, and newline). Care should be exercised in the use of these characters.

When a command contains a defined alias the shell replaces the alias with its definition (see alias command in this chapter).  If the argument is prefixed with the ^ character, however, the argument is treated as a literal argument and alias processing is not performed.

In interactive execution, the shell performs variable substitution, then expands wildcards before the command is executed.  In batch script execution, the shell performs argument substitution, then variable substitution, then expands wildcards before the command is executed.

### Variable Substitution

Environment variables can be set and viewed through the use of the set command (see set command in this chapter).  To access the value of an environment variable as an argument to a shell command, delimit the name of the variable with the % character before and after the variable name; for example, %myvariable%.

The shell maintains a special variable, named lasterror.  The variable contains the return code of the most recently executed shell command.

### Wildcard Expansion

The * , ? and [ characters can be used as wildcard characters in filename arguments to shell commands.  If an argument contains one or more of these characters, the shell processes the argument for file meta-arguments and expands the argument list to include all filenames matching the pattern.  These characters are part of patterns which represent file and directory names.

Table 2-1.	Wildcard Character Expansion

| Character Sequence | Meaning |
| --- | --- |
| "*" | Matches zero or more characters in a file name |
| "?" | Matches exactly one character of a file name |
| "[chars]" | Defines a set of characters; the pattern matches any single character in the set. Characters in the set are not separated. Ranges of characters can be specified by specifying the first character in a range, then the – character, then the last character in the range. Example: [a-zA-Z] |

### Output Redirection

Output of EFI Shell commands can be redirected to files. The syntax of this is as follows:

Command > unicode_output_file_pathname

Command >a ascii_output_file_pathname

Command 1> unicode_output_file_pathname

Command 1>a ascii_output_file_pathname

Command 2> unicode_output_file_pathname

Command 2>a ascii_output_file_pathname

Command >> unicode_output_file_pathname

Command >>a ascii_output_file_pathname

Command 1>> unicode_output_file_pathname

Command 1>>a ascii_output_file_pathname

The meanings of the special character sequences used to denote output redirection are shown in Table 2-1.

Table 2-2.	Output Redirection Syntax

| Character Sequence | Meaning |
| --- | --- |
| ">" | redirect standard output to a unicode file |
| ">a" | redirect standard output to an ascii file |
| "1>" | redirect standard output to a unicode file |
| "1>a" | redirect standard output to an ascii file |
| "2>" | redirect standard error to unicode file |
| "2>a" | redirect standard error to ascii file |
| ">>" | redirect standard output appended to a unicode file |
| ">>a" | redirect standard output appended to an ascii file |
| "1>>" | redirect standard output appended to a unicode file |
| "1>>a" | redirect standard output appended to an ascii file |

The shell will redirect standard output to a single file and standard error to a single file.  Redirecting both standard output and standard error to the same file is allowed.  Redirecting Standard output to more than one file on the same command is not supported.  Similarly, redirecting to multiple files is not supported for standard error.

### Quoting

Quotation marks in the EFI Shell are used for argument grouping. A quoted string is treated as a single argument to a command, and any whitespace characters included in the quoted string are just part of that single argument.  Quoting an environment variable does not have any effect on the de-referencing of that variable.  Double quotation marks “” are used to denote strings.  Single quotation marks are not treated specially by the shell in any way.  Empty strings are treated as valid command line arguments.

### Execution of Batch Scripts

The EFI Shell has the capability of executing commands from a file (batch script).  EFI Shell batch script files are named using the “.nsh” extension.  Batch script files can be either UNICODE or ASCII format files.  EFI Shell script files are invoked by entering the filename at the command prompt, with or without the filename extension.

Up to nine (9) positional arguments are supported for batch scripts.  Positional argument substitution is performed before the execution of each line in the script file.  Positional arguments are denoted by %n, where n is a digit between 0 and 9.  By convention, %0 is the name of the script file currently being executed.  In batch scripts, argument substitution is performed first, then variable substitution.  Thus, for a variable containing %2, the variable will be replaced with the literal string %2, not the second argument on the command line.

If no real argument is found to substitute for a positional argument, then the positional argument is ignored.

Script file execution can be nested; that is, script files may be executed from within other script files.  Recursion is allowed.

Output redirection is fully supported.  Output redirection on a command in a script file causes the output for that command to be redirected.  Output redirection on the invocation of a batch script causes the output for all commands executed from that batch script to be redirected to the file, with the output of each command appended to the end of the file.

By default, both the input and output for all commands executed from a batch script are echoed to the console.  Display of commands read from a batch file can be suppressed via the echo -off command (see echo).   If output for a command is redirected to a file, then that output is not displayed on the console.  Note that commands executed from a batch script are not saved by the shell for DOSkey history (up-arrow command recall).

### Error Handling in Batch Scripts

By default, if an error is encountered during the execution of a command in a batch script, the script will continue to execute.  The lasterror shell variable is provided allow batch scripts to test the results of the most recently executed command using the if command.  This variable is not an environment variable, but is a special variable maintained by the shell for the lifetime of that instance of the shell.

### Comments in Script Files

Comments can be embedded in batch scripts.  The # character on a line is used to denote that all characters on the same line and to the right of the # are to be ignored by the shell.  Comments are not echoed to the console.

## EFI Shell Commands

There are two types of commands available with the shell:  internal commands and external commands.  Internal commands are part of the EFI shell image, while external commands are stand-alone EFI applications.  Note: This allows users to add their own user-defined commands.

The user may also run an EFI application by entering the name of the application at the command prompt.  In addition, the active drive may be changed by entering the mapped name followed by a ‘:’ at the command prompt.

Table 2-3.	List of Internal EFI Shell Commands

| Command | Built-in | Description |
| --- | --- | --- |
| Help | YES | Displays the list of available commands |
| Guid | YES | Displays the list of Globally Unique Identifiers. |
| Set | YES | Displays, sets, or deletes environment variables. |
| Alias | YES | Define as alias for an EFI command or an EFI application. |
| Dh | YES | Displays information on the protocol handles. |
| Map | YES | Maps a user defined name to a protocol handle. |
| Cd | YES | Sets the working directory for the EFI shell environment. |
| Echo | YES | Toggle console output or write text to the console |
| For / endfor | YES | Control flow construct: Looping (script-only) |
| If / endif | YES | Control flow construct: Conditional execution (script-only) |
| Goto | YES | Control flow construct: Jump (script-only) |
| Pause | YES | Pause for keyboard input; exit on ‘q’ or ‘Q’ (script-only) |
| Exit | YES | Exit the shell |

Table 2-4.	List of External EFI Shell Commands

| Command | Built-in | Description |
| --- | --- | --- |
| Attrib | NO | Get/Set file attributes. |
| Bcfg | NO | Manage boot and driver environment variables. |
| Cls | NO | Clear the standard output device. |
| Comp | NO | Compare two files. |
| Cp | NO | Copy a file. |
| Date | NO | Get/Set the system's date. |
| Edit | NO | Unicode/ASCII text editor. |
| Hexedit | NO | Hex editor |
| Load | NO | Load an EFI Device Driver. |
| Ls | NO | Displays the contents of a directory. |
| Memmap | NO | Displays the memory map. |
| Mkdir | NO | Creates a new directory. |
| Mode | NO | Changes the display mode of the standard output device. |
| Mv | NO | Move a file from one location to another on a disk. |
| Nshell | NO | Invoke another EFI Shell. |
| Reset | NO | Reset the system. |
| Rm | NO | Deletes a file or a directory. |
| Type | NO | Displays contents of a text file. |
| Time | NO | Get/Set the system's time. |
| Ver | NO | Display version information on the EFI firmware. |
| Vol | NO | Get/Set volume information on a disk. |

Table 2-5.	List of Debug EFI Shell Commands

| Command | Built-in | Description |
| --- | --- | --- |
| Dblk | NO | Display a block from a block device. |
| Dmem | NO | Display the contents of memory. |
| Dmpstore | NO | Display all the environment variables and their values. |
| Err | YES | Set the current debug error level. |
| Getmtc | NO | Display the value of the monotonic counter |
| Mm | NO | Perform an PCI I/O, PCI Memory, PCI Configuration, or MMIO cycle. |
| Pci | NO | Display all the PCI devices in the system. |
| Setsize | NO | Set the size of a file. |
| Stall | NO | Stall the processor for a given number of microseconds. |
| Touch | NO | Set the date and time of a file to the current date and time. |

### help

help [-b]

[-b]     - Display one screen at a time

The help command displays the list of commands that are built into the EFI Shell.  The following example shows the output from this command.

Examples

Shell> help

help [internal command]        - Displays this help

guid [sname]                   - Dump known guid ids

set [-d] [sname] [value]       - Set/get environment variable

alias [-d] [sname] [value]     - Set/get alias settings

dh [-p prot_id] | [handle]     - Dump handle info

map [-dvr] [sname[:]] [handle] - Map shortname to device path

cd [path]                      - Updates the current directory

echo [[-on | -off] | [text]    - Echo text to stdout or toggle script echo

if [not] condition then        - Script-only: Condition is "string1 == string2"

or "exist file"

endif                          - Script-only: Terminate effect of if command

goto label                     - Script-only: Jump to label location in script

for var in <set>               - Script-only: loop construct

endfor                         - Script-only: delimiter for loop construct

pause                          - Script-only: prompt to quit or continue

Shell>

### guid

guid [-b]

[-b]     - Display one screen at a time

This command displays a list of all the GUIDs that have been registered with the EFI environment.  The following example shows the output from this command.

Examples

Shell> guid

DevIo           : AF6AC311-84C3-11D2-8E3C-00A0C969723B

diskio          : CE345171-BA0B-11D2-8E4F-00A0C969723B

blkio           : 964E5B21-6459-11D2-8E39-00A0C969723B  *

txtin           : 387477C1-69C7-11D2-8E39-00A0C969723B

txtout          : 387477C2-69C7-11D2-8E39-00A0C969723B  *

fs              : 964E5B22-6459-11D2-8E39-00A0C969723B

load            : 56EC3091-954C-11D2-8E3F-00A0C969723B

image           : 5B1B31A1-9562-11D2-8E3F-00A0C969723B  *

varstore        : F088CD91-A046-11D2-8E42-00A0C969723B

dpath           : 09576E91-6D3F-11D2-8E39-00A0C969723B  *

unicode         : 1D85CD7F-F43D-11D2-9A0C-0090273FC14D

pxe             : 01949C4C-9496-11D2-85E1-00A0C93EC93B

ShellInt        : 47C7B223-C42A-11D2-8E57-00A0C969723B

SEnv            : 47C7B224-C42A-11D2-8E57-00A0C969723B

ShellProtId     : 47C7B226-C42A-11D2-8E57-00A0C969723B

ShellDevPathMap : 47C7B225-C42A-11D2-8E57-00A0C969723B

ShellAlias      : 47C7B227-C42A-11D2-8E57-00A0C969723B

G0              : 00000000-0000-0000-0000-000000000000

Efi             : 8BE4DF61-93CA-11D2-AA0D-00E098032B8C

GenFileInfo     : 09576E92-6D3F-11D2-8E39-00A0C969723B

FileSysInfo     : 09576E93-6D3F-11D2-8E39-00A0C969723B

PcAnsi          : E0C14753-F9BE-11D2-9A0C-0090273FC14D

Unknown Device  : CF31FAC5-C24E-11D2-85F3-00A0C93EC93B

g1              : 43D66E51-AD78-11D2-8E4B-00A0C969723B

g2              : 386F4BBC-7782-11D2-85D6-00A0C93EC93B

g3              : EFE309D1-ACA9-11D2-85E2-00A0C93EC93B

Shell>

### set

set [-d] [-b] [sname] [value]

[-d]     - Delete the environment variable

[-b]     - Display one screen at a time

[sname]  - Environment variable name

[value]  - Environment variable value

This command is used maintain the environment variables that are available from the EFI environment.  This command can display the environment variables, create new environment variables, change the value of existing environment variables, or delete environment variables.  The set command will set the environment variable specified by sname to value.  This form of the command can be used to create a new environment variable, or to modify an existing environment variable.  If the set command is used without any parameters, then all the environment variables are displayed.  If the set command is used with the –d option, then the environment variable specified by sname will be deleted.  The following examples show how this command can be used to create, modify, and delete the environment variable DiagnosticPath.

Examples

Shell> set

path : fs0:\efi\tools;fs0:\;.

Shell> set DiagnosticPath fs0:\efi\diag

Shell> set

path           : fs0:\efi\tools;fs0:\;.

DiagnosticPath : fs0:\efi\diag

Shell> set DiagnosticPath fs0:\efi\diag;fs1:\efi\diag

Shell> set

path           : fs0:\efi\tools;fs0:\;.

DiagnosticPath : fs0:\efi\diag;fs1:\efi\diag

Shell> set –d DiagnosticPath

Shell> set

path : fs0:\efi\tools;fs0:\;.

Shell>

### alias

alias [-d] [-b] [sname] [value]

[-d]     - Delete the alias

[-b]     - Display one screen at a time

[sname]  - Alias name

[value]  - EFI command or EFI application

This command displays, creates, or deletes aliases in the EFI shell environment.  An alias provides a new name for an existing EFI shell command or an EFI application.  Once the alias is created, it can be used to run the command or launch the EFI application.  There are some aliases that are predefined in the EFI shell environment.  These aliases provide the DOS and UNIX equivalent names for the file manipulation commands. The examples below show the default aliases available in the EFI shell environment, and an example of how to create and delete a new alias for the guid command.

Examples

Shell> alias

dir  : ls

md   : mkdir

rd   : rm

del  : rm

copy : cp

Shell> alias myguid guid

Shell> alias

dir    : ls

md     : mkdir

rd     : rm

del    : rm

copy   : cp

myguid : guid

Shell> alias –d myguid

Shell> alias

dir  : ls

md   : mkdir

rd   : rm

del  : rm

copy : cp

### dh

dh [-p prot_id] [-b] | [handle]

[-p prot_id]  - Protocol to dump

[-b]          - Display one screen at a time

[handle]      - Handle number to dump

This command displays the device handles in the EFI environment.  When the dh command is used without any parameters, a list of all the device handles in the EFI environment is displayed.  A single device handle can contain one or more protocol instances.  If the dh command is used with a specific handle number, the details of all the protocols associated with that device handle are displayed.  If the –p option is used, the list of device handles containing a specific protocol will be displayed.  The following examples show how the dh command can be used.  The first example displays all the device handles in a system.  The second example displays all the device handles with a file system protocol, and the third example displays the details of the device handle for the floppy drive.

Examples

Shell> dh

1: varstore

2: varstore

3: Image(dskio)

4: Image(pblkio)

5: Image(fat)

6: DevIo DevPath()

7: unicode

8: txtin DevPath(..,0)/Pci(0|0)/Acpi(PNP0303,0))

9: txtout DevPath(Acpi(PNP0A03,0)/Pci(3|0))

A: diskio blkio fs DevPath(..,0)/Pci(0|0)/Acpi(PNP0604,0))

B: diskio blkio DevPath(VenHw(Unknown Device:80))

C: diskio blkio fs DevPath(..vice:80)/HD(Part1,Sig1-F4A3))

D: diskio blkio DevPath(..vice:80)/HD(Part2,Sig1-F4A3))

E: diskio blkio fs DevPath(..,Sig1-F4A3)/HD(Part1,Sig1-0))

F: diskio blkio DevPath(..,Sig1-F4A3)/HD(Part2,Sig1-0))

10: diskio blkio fs DevPath(..rt2,Sig1-0)/HD(Part1,Sig1-0))

11: varstore DevPath(..0|0)/Acpi(PNP0604,0)/BootStr)

12: Image(ramdisk)

13: diskio blkio DevPath(VenMsg(g1))

14: Image(bootmgr)

15: Image(shellenv.efi)

16: Image(nshell) ShellInt

Shell> dh –p fs

A: diskio blkio fs DevPath(..,0)/Pci(0|0)/Acpi(PNP0604,0))

C: diskio blkio fs DevPath(..vice:80)/HD(Part1,Sig1-F4A3))

E: diskio blkio fs DevPath(..,Sig1-F4A3)/HD(Part1,Sig1-0))

10: diskio blkio fs DevPath(..rt2,Sig1-0)/HD(Part1,Sig1-0))

Shell> dh A

Handle 0A (07FC6E08)

diskio

blkio Fixed MId:1 bsize 200, lblock B40 (1,474,560), raw rw cached

fs

dpath

PNP Device Path for PnP

HID A0341D0, UID 0

Hardware Device Path for PCI

PNP Device Path for PnP

HID 60441D0, UID 0

AsStr: 'Acpi(PNP0A03,0)/Pci(0|0)/Acpi(PNP0604,0)'

Shell>

### map

map [-dvrb] [sname] [handle]

[-d]      - Delete a mapping

[-v]      - Verbose listing of mappings

[-r]      - Reset to default mappings

[-b]      - Display one screen at a time

[sname]   - A user defined name for the mapping

[handle]  - The handle number from the dh command

This command is used to define a mapping between a user defined name and a device handle.  The most common use of this command is to assign drive letters to device handles that support a file system protocol.  Once these mappings are created, the drive letters can be used with all the file manipulation commands.  The EFI shell environment creates default mappings for all the device handles that support a recognized file systems.  The floppy drive is typically fs0, and hard drive partitions with recognized file systems are typically fs1, fs2, …, fsn.  This command can be used to create additional mappings, or it can be used to delete an existing mapping with the  -d option.  If the map command is used without any parameters, all the current mappings will be listed.  If the –v option is used, the mappings will be shown with additional information on each mapped handle.  The -r option is used to regenerate all the mappings in a system.  This is useful if the system configuration has changed since the last boot.  The following examples show how to create a new mapping of D: for the first hard drive partition that supports the file system protocol  Please refer to the list of handles in the example for the dh command.

Examples

Shell> map

Device mapping table

fs0  : Acpi(PNP0A03,0)/Pci(0|0)/Acpi(PNP0604,0)

blk0 : Acpi(PNP0A03,0)/Pci(0|0)/Acpi(PNP0604,0)

blk1 : VenHw(Unknown Device:80)

blk2 : VenHw(Unknown Device:80)/HD(Part1,Sig1-B3C8)

blk3 : VenHw(Unknown Device:80)/HD(Part2,Sig1-B3C8)

blk4 : VenHw(Unknown Device:80)/HD(Part3,Sig1-B3C8)

blk5 : VenMsg(g1)

fs1  : VenHw(Unknown Device:80)/HD(Part1,Sig1-F4A3)

fs2  : VenHw(Unknown Device:80)/HD(Part2,Sig1-F4A3)/HD(Part1,Sig1-0)

fs3  : VenHw(Unknown Device:80)/HD(Part2,Sig1-F4A3)/HD(Part2,Sig1-0)/HD(Part1,Sig1-0)

Shell> map D C

Shell> map

Device mapping table

fs0  : Acpi(PNP0A03,0)/Pci(0|0)/Acpi(PNP0604,0)

blk0 : Acpi(PNP0A03,0)/Pci(0|0)/Acpi(PNP0604,0)

blk1 : VenHw(Unknown Device:80)

blk2 : VenHw(Unknown Device:80)/HD(Part1,Sig1-B3C8)

blk3 : VenHw(Unknown Device:80)/HD(Part2,Sig1-B3C8)

blk4 : VenHw(Unknown Device:80)/HD(Part3,Sig1-B3C8)

blk5 : VenMsg(g1)

fs1  : VenHw(Unknown Device:80)/HD(Part1,Sig1-F4A3)

fs2  : VenHw(Unknown Device:80)/HD(Part2,Sig1-F4A3)/HD(Part1,Sig1-0)

fs3  : VenHw(Unknown Device:80)/HD(Part2,Sig1-F4A3)/HD(Part2,Sig1-0)/HD(Part1,Sig1-0)

D    : VenHw(Unknown Device:80)/HD(Part1,Sig1-F4A3)

Shell> map –v D

D    : VenHw(Unknown Device:80)/HD(Part1,Sig1-F4A3)

= Handle  C: diskio blkio fs

> \

Shell> map –d D

Shell> map

Device mapping table

fs0  : Acpi(PNP0A03,0)/Pci(0|0)/Acpi(PNP0604,0)

blk0 : Acpi(PNP0A03,0)/Pci(0|0)/Acpi(PNP0604,0)

blk1 : VenHw(Unknown Device:80)

blk2 : VenHw(Unknown Device:80)/HD(Part1,Sig1-B3C8)

blk3 : VenHw(Unknown Device:80)/HD(Part2,Sig1-B3C8)

blk4 : VenHw(Unknown Device:80)/HD(Part3,Sig1-B3C8)

blk5 : VenMsg(g1)

fs1  : VenHw(Unknown Device:80)/HD(Part1,Sig1-F4A3)

fs2  : VenHw(Unknown Device:80)/HD(Part2,Sig1-F4A3)/HD(Part1,Sig1-0)

fs3  : VenHw(Unknown Device:80)/HD(Part2,Sig1-F4A3)/HD(Part2,Sig1-0)/HD(Part1,Sig1-0)

### cd

cd [path]

This command changes the current working directory used by the EFI shell environment.  The following example shows how to move between the directories on a floppy drive containing an EFI directory, and a TOOLS subdirectory below the EFI directory.  The EFI shell environment uses the directory name “.” to refer to the current directory, and the directory name “..” to refer to the directory’s parent.

Examples

Shell> fs0:

fs0:\> cd efi

fs0:\efi\> cd ..

fs0:\> cd efi\tools

fs0:\efi\tools\> cd \

fs0:>

### echo

echo [-on | -off]

echo [text]

The first form of the echo command controls whether or not batch commands are displayed as they are read from the batch file.  If no argument is given the current “on” or “off” status is displayed. The second form prints the given message to the display.  Wildcard substitution is performed on the second form of the command.

Examples

Shell> echo

Echo is on.

Shell> echo –off

Shell> echo Hello world

Hello world

Shell> echo Loop count is %c for this iteration

Loop count is 42 for this iteration

Shell>

### for

for %indexvar in set

command [arguments]

[command [arguments]]

…

endfor

The for command executes one or more commands for each item in a set of items. The set may be text strings or filenames or a mixture of both, separated by spaces. Wildcards in filenames are expanded before command is executed. Indexvar is any single printable character, but it should not be a digit (0-9) because %digit will be interpreted as a positional argument (see “Execution of Batch Scripts”).  The namespace for index variables is separate from that for environment variables, so if indexvar has the same name as an existing environment variable, the environment variable will remain unchanged by the for loop.  Each command is executed once for each item in the set, with any occurrence of %indexvar in the command replaced with the current item.

The for command is available only in batch scripts.

Examples

#

#  Sample for loop – type contents of all .txt files

#

for %a in *.txt

type %a

echo ===== %a done =====

endfor

### if

if [not] exist filename then

command [arguments]

endif

if [not] string1 == string2 then

command [arguments]

[command [arguments]]

…

endif

The if command executes one or more commands if the specified condition is true, unless the not keyword is given, in which case the command is executed if the condition is false. The exist condition is true if filename exists. The filename argument may include device and path information.  Wildcard expansion is supported for the exist form of the command.  If more than one file matches the wildcard pattern, the condition evaluates to TRUE.  The string1 == string2 condition is true if the two strings are identical.

The if command is available only in batch scripts.

Examples

#

#  Example script for “if” command

#

if exist fs0:\myscript.sc then

myscript myarg1 myarg2

endif

if %myvar% == runboth then

myscript1

myscript2

endif

### goto

goto label

The goto command directs batch file execution to the line in the batch file after the given label. The command is not supported from the interactive shell.  A label is a line beginning with a colon (:). The search for label is done forward in the batch file. If the end of the file is reached, the search resumes at the top of the file and continues until label is found or the starting point is reached. If label is not found, the batch process terminates and an error message is displayed. When not searching for the target of a goto command, the shell reads label lines and ignores them.

The goto command is available only in batch scripts.

The following example shows the use of this command.

Examples

# This is a batch script

goto Done

…

:Done

cleanup.nsh

### pause

pause

The pause command prints a message to the display and then suspends batch file execution and waits for keyboard input. Pressing any key resumes execution, except for q or Q.  If q or Q is pressed, batch processing terminates; otherwise execution continues with the next line after the pause command.

The pause command is available only in batch scripts.

The following example shows the use of this command.

Examples

+script.nsh> pause

Hit ‘q’ to quit, any other key to continue:

Q

fs0:>

### exit

exit

This command exits the EFI Shell environment and returns control to the EFI application that launched the EFI Shell.

Examples

Shell> exit

### attrib

attrib [+a|-a] [+s|-s] [+h|-h] [+r|-r] [-b] file

[+a|-a]    - Set or clear the archive attribue

[+s|-s]    - Set or clear the system attribute

[+h|-h]    - Set or clear the hidden attribute

[+r|-r]    - Set or clear the read only attribute

[-b]       - Display one screen at a time

Displays or sets file attributes.  There are four attribute types that are supported for the EFI File System.  These are archive[A], system[S], hidden[H], and read only[R].  If a file is a directory, then it is also shown to have the attribute [D].

Examples

Shell> attrib fs0:\

DA SH  fs0:\efi

A     fs0:\cp.efi

A     fs0:\date.efi

A     fs0:\dblk.efi

Shell> attrib -a +r fs0:\cp.efi

R fs0:\cp.efi

Shell> attrib fs0:\

DA SH  fs0:\efi

R fs0:\cp.efi

A     fs0:\date.efi

A     fs0:\dblk.efi

### bcfg

bcfg driver|boot [dump [-v]] [add # file “desc”] [rm #] [mv # #]

driver	selects boot driver list

boot		selects boot option list

dump		dump selected list

v		dumps verbose including load options

add		add ‘file’ with ‘desc’ at position #

rm		remove #

mv		move # to #

Manages the boot and driver options stored in NVRAM.  This command can display the Boot#### or Driver#### environment variables by using the dump option.  The add option can be used to add a new Boot#### or Driver#### environment variable.  The rm option can be used to delete a Boot#### or Driver#### environment variable, and finally, then mv option can be used to reorder the Boot#### and Driver#### environment variables.  The add, rm, and mv options also update the BootOrder or DriverOrder environment variables as appropriate.

Examples

Shell> bcfg boot dump

The boot option list is:

Shell> bcfg driver dump

The boot driver list is:

Shell> fs0:

fs0:\> bcfg boot add 1 osloader.efi “EFI OS Loader”

fs0:\> bcfg boot add 2 foo.efi “Foo”

fs0:\> bcfg boot add 3 bar.efi “Bar”

fs0:\> bcfg boot dump

The boot option list is:

- Acpi(PNP0700,0)/\osloader.efi “EFI OS Loader”

- Acpi(PNP0700,0)/\foo.efi “Foo”

- Acpi(PNP0700,0)/\bar.efi “Bar”

fs0:\> bcfg boot mv 1 4

fs0:\> bcfg boot dump

The boot option list is:

- Acpi(PNP0700,0)/\foo.efi “Foo”

- Acpi(PNP0700,0)/\bar.efi “Bar”

- Acpi(PNP0700,0)/\osloader.efi “EFI OS Loader”

fs0:\> bcfg boot rm 1

fs0:\> bcfg boot rm 1

fs0:\> bcfg boot rm 1

fs0:\> bcfg boot dump

The boot option list is:

### comp

comp file1 file2

Compares the contents of file1 to file2.  The first 10 differences are shown before the compare operation is terminated.

Examples

Shell> comp fs0:\a.txt fs0:\a.txt

Compare fs0:\a.txt to fs0:\a.txt

[ok]

Shell> comp fs0:\a.txt fs0:\b.txt

Compare fs0:\a.txt to fs0:\b.txt

Miscompare #1 File1: fs0:\a.txt

00000914: 20                                               * *

File2: fs0:\b.txt

00000914: 42                                               *B*

Miscompare #2 File1: fs0:\a.txt

00000916: 42                                               *B*

File2: fs0:\b.txt

00000916: 53                                               *S*

Miscompare #3 File1: fs0:\a.txt

00000918: 53                                               *S*

File2: fs0:\b.txt

00000918: 5F                                               *_*

### cp

cp file [file] … [dest]

This command copies one or more files from one location to another location.  The following example shows how to copy the file MEMMAP.EFI in the TOOLS directory on the floppy drive to the file MM.EFI.

Examples

Shell> fs0:

fs0:\> cd efi

fs0:\efi\> cd tools

fs0:\efi\tools\> cp memmap.efi mm.efi

fs0:\efi\tools\>

### cls

cls [color]

color		- new background color

This command clears the standard output device with an optional background color attribute.  If color is not specified, then the background is cleared to black.

Examples

Shell> cls

Shell> cls 1

### date

date [mm/dd/yyyy]

This command displays to sets the current date for the system.  If not parameters are used, it shows the current date.  If a valid month, day, and year are provided, then the system's date will be updated.

Examples

Shell> date

07/14/1999

Shell> date 07/12/1999

Shell>

### edit

edit [file]

This command allows a file to be edited using a full screen editor.  The editor supports both Unicode and ASCII file types.

Examples

fs0:\> edit

fs0:\> edit foo.txt

### hexedit

hexedit

This command allows a file, block device, or memory region to be edited.  The region being edited is displayed as hexidecimal bytes, and the contents can be modified and saved

Examples

fs0:\> hexedit

### load

load file

This command loads an EFI driver.

Examples

Shell> load serial.efi

### ls

ls [-b] [dir] [dir] …

[-b]      - Display one screen at a time

This command lists all the files and subdirectories present in a directory.  If the ls command is used without any parameters, then the contents of the current working directory are displayed.  If a parameter is used, then that parameter is interpreted as a file path, and the contents of the directory specified by the file path are displayed.  The following examples show how the ls command can be used.  The first example lists the files in the current working directory fs0:\.  The second example lists the files in the EFI subdirectory.  The third example lists the files in the root directory of the first hard drive partition containing a recognized file system.

Examples

Shell> fs0:

fs0:\> ls

Directory of fs0:\

01/22/99  10:11p <DIR>            512  EFI

05/05/99  05:41p               36,924  TEST.EFI

05/06/99  01:48p               41,024  OSLOADER.EFI

05/06/99  11:00a               41,024  OSKERNEL.BIN

3 Files      118,972 bytes

1 Dirs           512 bytes

fs0:\> ls efi

Directory of fs0:\EFI

00/00/80  12:00a <DIR>            512  .

00/00/83  12:00a <DIR>              0  ..

00/00/80  12:00a               32,768  BOOTSTR

1 File        32,768 bytes

2 Dirs           512 bytes

fs0:\> ls fs1:\

Directory of fs1:\

.

.

.

fs0:\>

### memmap

memmap [-b]

[-b]      - Display one screen at a time

This command displays the memory map that is maintained by the EFI environment.  The EFI environment keeps track all the physical memory in the system and how it is currently being used.  The EFI Specification defines a set of Memory Type Descriptors.  Please see the EFI Specification for a description of how each of these memory types is used.

Examples

Shell> memmap

Type       Start            End               # Pages          Attributes

BS_data    0000000000000000-0000000000000FFF  0000000000000001 0000000000000008

available  0000000000001000-000000000001FFFF  000000000000001F 0000000000000008

BS_data    0000000000020000-0000000000021FFF  0000000000000002 0000000000000008

available  0000000000022000-0000000000089FFF  0000000000000068 0000000000000008

BS_data    000000000008A000-000000000009AFFF  0000000000000011 0000000000000008

BS_code    000000000009B000-000000000009EFFF  0000000000000004 0000000000000008

BS_data    000000000009F000-000000000009FFFF  0000000000000001 0000000000000008

BS_data    00000000000F0000-00000000000FFFFF  0000000000000010 0000000000000008

available  0000000000100000-00000000001DFFFF  00000000000000E0 0000000000000008

BS_data    00000000001E0000-00000000001FFFFF  0000000000000020 0000000000000008

available  0000000000200000-0000000000200FFF  0000000000000001 0000000000000008

BS_code    0000000000201000-0000000000215FFF  0000000000000015 0000000000000008

RT_code    0000000000216000-0000000000218FFF  0000000000000003 8000000000000008

BS_data    0000000000219000-000000000021BFFF  0000000000000003 0000000000000008

RT_data    000000000021C000-000000000021CFFF  0000000000000001 8000000000000008

BS_data    000000000021D000-000000000021DFFF  0000000000000001 0000000000000008

available  000000000021E000-0000000007E61FFF  0000000000007C44 0000000000000008

LoaderData 0000000007E62000-0000000007E62FFF  0000000000000001 0000000000000008

LoaderCode 0000000007E63000-0000000007E65FFF  0000000000000003 0000000000000008

LoaderData 0000000007E66000-0000000007E69FFF  0000000000000004 0000000000000008

available  0000000007E6A000-0000000007E6EFFF  0000000000000005 0000000000000008

LoaderData 0000000007E6F000-0000000007E6FFFF  0000000000000001 0000000000000008

BS_data    0000000007E70000-0000000007E70FFF  0000000000000001 0000000000000008

LoaderData 0000000007E71000-0000000007E75FFF  0000000000000005 0000000000000008

BS_data    0000000007E76000-0000000007E77FFF  0000000000000002 0000000000000008

LoaderData 0000000007E78000-0000000007E79FFF  0000000000000002 0000000000000008

BS_data    0000000007E7A000-0000000007E7AFFF  0000000000000001 0000000000000008

LoaderData 0000000007E7B000-0000000007E7BFFF  0000000000000001 0000000000000008

BS_data    0000000007E7C000-0000000007E85FFF  000000000000000A 0000000000000008

RT_data    0000000007E86000-0000000007E86FFF  0000000000000001 8000000000000008

BS_data    0000000007E87000-0000000007E87FFF  0000000000000001 0000000000000008

BS_code    0000000007E88000-0000000007E93FFF  000000000000000C 0000000000000008

BS_data    0000000007E94000-0000000007E99FFF  0000000000000006 0000000000000008

LoaderData 0000000007E9A000-0000000007E9BFFF  0000000000000002 0000000000000008

BS_data    0000000007E9C000-0000000007E9CFFF  0000000000000001 0000000000000008

LoaderData 0000000007E9D000-0000000007E9DFFF  0000000000000001 0000000000000008

LoaderCode 0000000007E9E000-0000000007EA1FFF  0000000000000004 0000000000000008

LoaderData 0000000007EA2000-0000000007EA4FFF  0000000000000003 0000000000000008

BS_data    0000000007EA5000-0000000007FC6FFF  0000000000000122 0000000000000008

RT_data    0000000007FC7000-0000000007FC8FFF  0000000000000002 8000000000000008

BS_data    0000000007FC9000-0000000007FCEFFF  0000000000000006 0000000000000008

RT_data    0000000007FCF000-0000000007FCFFFF  0000000000000001 8000000000000008

BS_data    0000000007FD0000-0000000007FFFFFF  0000000000000030 0000000000000008

BS_data    00000000FFFE0000-00000000FFFFFFFF  0000000000000020 0000000000000008

LoaderCode:       7 pages (28,672)

LoaderData:      20 pages (81,920)

BS_code   :      37 pages (151,552)

BS_data   :     471 pages (1,929,216)

RT_code   :       3 pages (12,288)

RT_data   :       5 pages (20,480)

available :  32,177 pages (131,796,992)

Shell>

### mkdir

mkdir dir [dir] …

This command creates a new directory on a file system.  The following example shows how to create the directory DIAGS below the directory EFI on the floppy drive.

Examples

Shell> fs0:

fs0:\> cd efi

fs0:\efi\> mkdir diags

fs0:\efi\> cd diags

fs0:\efi\diags\>

### mode

mode [row col]

This command is used to change the display mode for the console output device.  When this command is used without any parameters, it shows the list of modes that the standard output device currently supports.  The mode command can then be used with the row and col parameter to change the number of rows and columns on the standard output device.  The following examples show how the mode command can be used.  The first example lists all modes that are currently available, and the current selected mode is indicated by an ‘*’.  The second example changes the mode to an 80 X 50 text mode display.  The display is cleared every time the mode command is used to change the currently selected display mode.

Examples

Shell> mode

Available modes on standard output

col  80 row  25  *

col  80 row  50

col  80 row  43

col 100 row 100

col 100 row 999

Shell> mode 80 50

Shell>

### nshell

nshell

This command launches another copy of the EFI Shell.  This new shell inherits the environment variables of the parent shell along with the standard input device, standard output device, and the standard error device.

Examples

Shell> nshell

### rm

rm file|dir [file|dir] …

This command deletes one or more files or directories.  The following examples show how to delete the directory created in the mkdir command example, and the file copied in the cp command example.

Examples

Shell> fs0:

fs0:\> cd efi

fs0:\efi\> rm diags

fs0:\efi\> cd tools

fs0:\efi\tools\> rm mm.efi

fs0:\efi\tools\>

### time

date [hh:mm:ss]

This command displays to sets the current time for the system.  If not parameters are used, it shows the current time.  If valid hours, minutes, and seconds are provided, then the system's time will be updated.

Examples

Shell> time

15:09:57

Shell> time 15:10:00

Shell>

### type

type [-a] [-u] [-b] file

[-a]  - Display the file as ASCII characters.

[-u]  - Display the file as Unicode characters.

[-b]  - Display one screen at a time

This command sends the contents of a file to the standard output device.  If no options are used, then the file type is auto-detected and sent to the standard output device. If the –a option is used, the file is sent to the standard output device as a stream of ASCII characters. If the –u option is used, the file is sent to the standard output device as a stream of Unicode characters.  The following example shows how to send the ASCII file README.TXT on the floppy drive to the standard output device and the Unicode file READMEU.TXT on the floppy drive to the standard output device.

Examples

Shell> fs0:

fs0:\> type readme.txt

fs0:\> type –a readme.txt

fs0:\> type readmeu.txt

fs0:\> type –u readmeu.txt

fs0:\>

### ver

ver

Displays the version information for this EFI Firmware.  This information is retrieved through the EFI System Table.

Examples

Shell> ver

EFI Specification Revision 0.91

EFI Vendor      = INTEL

EFI Revision    = 00000009

Shell>

### vol

vol fs [Volume Label]

fs            - The name of the file system to use

Volume Label  – New volume label

Displays volume information for the file system specified by fs.  If Volume Label is specified, then the volume label for fs will be set to Volume Label.  The maximum length for Volume Label is 11 characters.

Examples

Shell> vol fs0

Shell> vol fs0 New Volume

### dblk

dblk BlockDeviceName [LBA] [# Blocks]

BlockDeviceName  The name of the block device to display

[LBA]            The block number to display

[# Blocks]       The number of block to display

Displays the contents of one or more blocks from a block device.   If [LBA] is not specified or it greater than the last block on that block device, then block #0 is displayed.  If [# Blocks] is not specified, then on1y 1 block will be displayed.  The maximum number of blocks that can be displayed at one time is 0x10.

Examples

Shell> dblk blk0

LBA 0x0000000000000000 Size 0x00000200 bytes BlkIo 0x07FCD350

00000000: EB 3C 90 28 25 5A 69 59-49 48 43 00 02 01 01 00  *.<.INTEL   .....*

00000010: 02 E0 00 40 0B F0 09 00-12 00 02 00 00 00 00 00  *...@............*

00000020: 00 00 00 00 00 01 29 20-20 20 20 45 46 49 20 46  *......)    EFI F*

00000030: 4C 4F 50 50 59 20 46 41-54 31 32 20 20 20 8C C8  *LOPPY FAT12   ..*

00000040: 8E D0 05 00 10 8E D8 BC-00 7C 8B EC B4 08 B2 00  *................*

00000050: CD 13 33 C0 8A C6 24 3F-FE C0 50 8A C1 24 3F 50  *..3...$?..P..$?P*

00000060: 81 BE FE 01 55 AA 0F 85-6F 01 80 BE 00 00 EB 0F  *....U...o.......*

00000070: 85 66 01 81 BE 0B 00 00-02 0F 85 5C 01 80 BE 0D  *.f.........\....*

00000080: 00 00 0F 84 53 01 83 BE-11 00 00 0F 84 4A 01 8B  *....S........J..*

00000090: 86 0E 00 3B 86 13 00 0F-8F 3E 01 33 C9 8D 36 03  *...;.....>.3..6.*

000000A0: 00 B1 08 E8 25 01 8D 36-2B 00 B1 0B E8 1C 01 81  *....%..6+.......*

000000B0: BE 36 00 46 41 0F 85 20-01 81 BE 38 00 54 31 0F  *.6.FA.. ...8.T1.*

000000C0: 85 16 01 B8 20 20 39 86-3B 00 0F 85 0B 01 39 86  *....  9.;.....9.*

000000D0: 3C 00 0F 85 03 01 80 BE-3A 00 32 74 0C 80 BE 3A  *<.......:.2t...:*

000000E0: 00 36 0F 84 F3 00 E9 F0-00 8B 8E 11 00 C1 E1 05  *.6..............*

000000F0: 8B D9 81 E3 FF 01 0F 85-DF 00 8B D9 C1 EB 09 BF  *................*

00000100: 00 00 8A 86 10 00 32 E4-F7 A6 16 00 03 86 0E 00  *......2.........*

00000110: 1E 07 E8 6D 00 03 C3 89-46 00 81 3D 45 46 75 27  *...m....F..=EFu'*

00000120: 81 7D 02 49 4C 75 20 81-7D 04 44 52 75 19 B8 20  *...ILu ...DRu.. *

00000130: 20 39 45 06 75 11 39 45-08 75 0C 39 45 09 75 07  * 9E.u.9E.u.9E.u.*

00000140: 8A 45 0B 24 58 74 0B 83-C7 20 83 E9 20 75 CB E9  *.E.$Xt... .. u..*

00000150: 87 00 8B 4D 1A 8C C8 05-00 20 8E C0 33 FF 8B C1  *...M..... ..3...*

00000160: 83 E8 02 32 FF 8A 9E 0D-00 F7 E3 03 46 00 32 FF  *...2........F.2.*

00000170: 8A 9E 0D 00 06 E8 0A 00-58 89 86 80 01 EA 00 00  *........X.......*

00000180: 00 20 60 8B F0 8B CB BD-FC 7B 8B C6 33 D2 F7 76  *. `.........3..v*

00000190: 00 42 8B 5E 00 2B DA 43-3B CB 7F 02 8B D9 51 8A  *.B.^.+.C;.....Q.*

000001A0: CA 33 D2 F7 76 02 53 8A-F2 B2 00 8A E8 8A C3 B4  *.3..v.S.........*

000001B0: 02 8B DF CD 13 5B 59 03-F3 2B CB 8C C0 C1 E3 05  *.....[Y..+......*

000001C0: 03 C3 8E C0 83 F9 00 75-BE 61 C3 80 3A 7F 7F 09  *.......u.a..:...*

000001D0: 80 3A 20 7C 04 46 E2 F3-C3 CC EB FD 00 00 00 00  *.: ..F..........*

000001E0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

000001F0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 55 AA  *..............U.*

Fat 12 BPB  FatLabel: 'EFI FLOPPY '  SystemId: 'FAT12   ' OemId: 'INTEL   '

SectorSize 0x200  SectorsPerCluster 1 ReservedSectors 1  # Fats 2

Root Entries 0xE0  Media 0xF0  Sectors 0xB40  SectorsPerFat 0x9

SectorsPerTrack 0x12 Heads 2

### dmem

dmem [Address] [Size] [;MMIO]

[Address]  Start address

[Size]     Number of bytes to display

[;MMIO]    Use DEVICE_IO protocol to access memory

Displays the contents of system memory or device memory.  If Address is not specified, then the contents of the EFI System Table are displayed.  Otherwise, memory starting at Address is displayed.  Size specifies the number of bytes to display.  If Size is not specified, then this command defaults to 512 bytes.  If MMIO is not specified, then main system memory is displayed.  Otherwise, device memory is displayed through the use of the DEVICE_IO protocol.

Examples

Shell> dmem

Memory Address 000000000012FB60 200 Bytes

0012FB60: 49 42 49 20 53 59 53 54-5B 00 00 00 48 00 00 00  *IBI SYST[...H...*

0012FB70: 66 78 20 E5 00 00 00 00-88 08 82 01 09 00 00 00  *fx .............*

0012FB80: 08 0A 82 01 68 1C 82 01-08 0A 82 01 28 1C 82 01  *....h.......(...*

0012FB90: 88 E3 82 01 28 1F 82 01-58 50 42 00 E8 F6 41 00  *....(...XPB...A.*

0012FBA0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FBB0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FBC0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FBD0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FBE0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FBF0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FC00: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FC10: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FC20: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FC30: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FC40: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FC50: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FC60: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FC70: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FC80: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FC90: 00 00 00 00 A8 FC 12 00-96 59 A3 01 88 50 81 01  *.........Y...P..*

0012FCA0: C0 FC 12 00 01 FC 12 00-C8 FE 12 00 F8 14 A3 01  *................*

0012FCB0: 88 50 81 01 C0 FC 12 00-01 00 00 00 08 CE 82 01  *.P..............*

0012FCC0: 64 00 6D 00 65 00 6D 00-00 00 00 00 00 00 00 00  *d.m.e.m.........*

0012FCD0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FCE0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FCF0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FD00: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FD10: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FD20: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FD30: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FD40: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

0012FD50: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

Valid EFI Header at Address 000000000012FB60

--------------------------------------------

System: Table Structure size 00000048 revision 0000005B

ConIn (0x01820A08) ConOut (0x01820A08) StdErr (0x0182E388)

Console In on  VenHw(g3)

Console Out on VenHw(g3)

Std Error on   VenHw(g3)

Runtime Services 0x0000000000425058

Boot Services    0x000000000041F6E8

Shell> dmem 01820a08 18

Memory Address 0000000001820A08 18 Bytes

01820A08: 68 6E 64 6C 8C 07 82 01-0C 0D 82 01 10 09 82 01  *hndl............*

01820A18: 90 0A 82 01 57 00 00 00-                         *....W...*

### dmpstore

dmpstore

Displays all the environment variables being managed by EFI.

Examples

Shell> dmpstore

Dump NVRAM

Variable RT+BS 'Efi:LangCodes' DataSize = 3

00000000: 65 6E 67                                         *eng*

Variable NV+RT+BS 'Efi:Lang' DataSize = 3

00000000: 65 6E 67                                         *eng*

Variable NV+RT+BS 'ShellProtId:DevIo' DataSize = 10

00000000: 11 C3 6A AF C3 84 D2 11-8E 3C 00 A0 C9 69 72 3B  *..j......<...ir;*

Variable NV+RT+BS 'ShellProtId:fs' DataSize = 10

00000000: 22 5B 4E 96 59 64 D2 11-8E 39 00 A0 C9 69 72 3B  *"[N.Yd...9...ir;*

Variable NV+RT+BS 'ShellProtId:diskio' DataSize = 10

00000000: 71 51 34 CE 0B BA D2 11-8E 4F 00 A0 C9 69 72 3B  *qQ4......O...ir;*

Variable NV+RT+BS 'ShellProtId:blkio' DataSize = 10

00000000: 21 5B 4E 96 59 64 D2 11-8E 39 00 A0 C9 69 72 3B  *![N.Yd...9...ir;*

Variable NV+RT+BS 'ShellProtId:txtin' DataSize = 10

00000000: C1 77 74 38 C7 69 D2 11-8E 39 00 A0 C9 69 72 3B  *.wt8.i...9...ir;*

Variable NV+RT+BS 'ShellProtId:txtout' DataSize = 10

00000000: C2 77 74 38 C7 69 D2 11-8E 39 00 A0 C9 69 72 3B  *.wt8.i...9...ir;*

Variable NV+RT+BS 'ShellProtId:load' DataSize = 10

00000000: 91 30 EC 56 4C 95 D2 11-8E 3F 00 A0 C9 69 72 3B  *.0.VL....?...ir;*

Variable NV+RT+BS 'ShellProtId:image' DataSize = 10

00000000: A1 31 1B 5B 62 95 D2 11-8E 3F 00 A0 C9 69 72 3B  *.1.[b....?...ir;*

Variable NV+RT+BS 'ShellProtId:varstore' DataSize = 10

00000000: 91 CD 88 F0 46 A0 D2 11-8E 42 00 A0 C9 69 72 3B  *....F....B...ir;*

Variable NV+RT+BS 'ShellProtId:unicode' DataSize = 10

00000000: 7F CD 85 1D 3D F4 D2 11-9A 0C 00 90 27 3F C1 4D  *....=.......'?.M*

Variable NV+RT+BS 'ShellProtId:LegacyBoot' DataSize = 10

00000000: B2 5E 6E 37 E4 30 D3 11-BA E5 00 80 C7 3C 88 81  *.^n7.0.......<..*

Variable NV+RT+BS 'ShellProtId:serialio' DataSize = 10

00000000: 6F CF 25 BB D4 F1 D2 11-9A 0C 00 90 27 3F C1 FD  *o.%.........'?..*

Variable NV+RT+BS 'ShellProtId:pxe' DataSize = 10

00000000: 4C 9C 94 01 96 94 D2 11-85 E1 00 A0 C9 3E C9 3B  *L............>.;*

Variable NV+RT+BS 'ShellProtId:dpath' DataSize = 10

00000000: 91 6E 57 09 3F 6D D2 11-8E 39 00 A0 C9 69 72 3B  *.nW.?m...9...ir;*

Variable NV+RT+BS 'ShellProtId:VgaClass' DataSize = 10

00000000: 10 63 3D 0E E4 6F D3 11-BB 81 00 80 C7 3C 88 81  *.c=..o.......<..*

Variable NV+RT+BS 'ShellProtId:TxtOutSplit' DataSize = 10

00000000: A0 30 D8 56 7A 7E D3 11-BB A0 00 A0 C9 69 72 3B  *.0.Vz........ir;*

Variable NV+RT+BS 'ShellProtId:TxtInSplit' DataSize = 10

00000000: 50 C5 A3 F9 B5 7F D3 11-BB A0 00 A0 C9 69 72 3B  *P............ir;*

Variable NV+RT+BS 'ShellProtId:ShellInt' DataSize = 10

00000000: 23 B2 C7 47 2A C4 D2 11-8E 57 00 A0 C9 69 72 3B  *#..G*....W...ir;*

Variable NV+RT+BS 'ShellProtId:SEnv' DataSize = 10

00000000: 24 B2 C7 47 2A C4 D2 11-8E 57 00 A0 C9 69 72 3B  *$..G*....W...ir;*

Variable NV+RT+BS 'ShellProtId:ShellProtId' DataSize = 10

00000000: 26 B2 C7 47 2A C4 D2 11-8E 57 00 A0 C9 69 72 3B  *&..G*....W...ir;*

Variable NV+RT+BS 'ShellProtId:ShellDevPathMap' DataSize = 10

00000000: 25 B2 C7 47 2A C4 D2 11-8E 57 00 A0 C9 69 72 3B  *%..G*....W...ir;*

Variable NV+RT+BS 'ShellProtId:ShellAlias' DataSize = 10

00000000: 27 B2 C7 47 2A C4 D2 11-8E 57 00 A0 C9 69 72 3B  *'..G*....W...ir;*

Variable NV+RT+BS 'ShellProtId:G0' DataSize = 10

00000000: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

Variable NV+RT+BS 'ShellProtId:Efi' DataSize = 10

00000000: 61 DF E4 8B CA 93 D2 11-AA 0D 00 E0 98 03 2B 8C  *a.............+.*

Variable NV+RT+BS 'ShellProtId:GenFileInfo' DataSize = 10

00000000: 92 6E 57 09 3F 6D D2 11-8E 39 00 A0 C9 69 72 3B  *.nW.?m...9...ir;*

Variable NV+RT+BS 'ShellProtId:FileSysInfo' DataSize = 10

00000000: 93 6E 57 09 3F 6D D2 11-8E 39 00 A0 C9 69 72 3B  *.nW.?m...9...ir;*

Variable NV+RT+BS 'ShellProtId:Unknown Device' DataSize = 10

00000000: C5 FA 31 CF 4E C2 D2 11-85 F3 00 A0 C9 3E C9 3B  *..1.N........>.;*

Variable NV+RT+BS 'SEnv:path' DataSize = 2E

00000000: 66 00 73 00 30 00 3A 00-5C 00 65 00 66 00 69 00  *f.s.0.:.\.e.f.i.*

00000010: 5C 00 74 00 6F 00 6F 00-6C 00 73 00 3B 00 66 00  *\.t.o.o.l.s.;.f.*

00000020: 73 00 30 00 3A 00 5C 00-3B 00 2E 00 00 00        *s.0.:.\.;.....*

Variable NV+RT+BS 'ShellAlias:dir' DataSize = 6

00000000: 6C 00 73 00 00 00                                *l.s...*

Variable NV+RT+BS 'ShellAlias:md' DataSize = C

00000000: 6D 00 6B 00 64 00 69 00-72 00 00 00              *m.k.d.i.r...*

Variable NV+RT+BS 'ShellAlias:rd' DataSize = 6

00000000: 72 00 6D 00 00 00                                *r.m...*

Variable NV+RT+BS 'ShellAlias:del' DataSize = 6

00000000: 72 00 6D 00 00 00                                *r.m...*

Variable NV+RT+BS 'ShellAlias:copy' DataSize = 6

00000000: 63 00 70 00 00 00                                *c.p...*

Variable NV+RT+BS 'g4:MTC' DataSize = 4

00000000: 07 00 00 00                                      *....*

Variable NV+RT+BS 'ShellDevPathMap:fs0' DataSize = 18

00000000: 01 04 14 00 51 6E D6 43-78 AD D2 11 8E 4B 00 A0  *....Qn.Cx....K..*

00000010: C9 69 72 3B 7F FF 04 00-                         *.ir;....*

Variable NV+RT+BS 'ShellDevPathMap:blk0' DataSize = 2C

00000000: 01 04 14 00 BC 4B 6F 38-82 77 D2 11 85 D6 00 A0  *.....Ko8.w......*

00000010: C9 3E C9 3B 01 04 14 00-BC 4B 6F 38 82 77 D2 11  *.>.;.....Ko8.w..*

00000020: 85 D6 00 A0 C9 3E C9 3B-7F FF 04 00              *.....>.;....*

### err

err [Error Level]

[Error Level]  – New error level bit mask.

This command sets the current debug error level in the system.  This commands only works if the EFI Shell and the ERR command are built into the core firmware.  Error Level is a bit mask for different types of error messages.  The following is the list of definitions for the bit mask.

#define D_INIT        0x00000001          // Initialization style messages

#define D_WARN        0x00000002          // Warnings

#define D_LOAD        0x00000004          // Load events

#define D_FS          0x00000008          // EFI File system

#define D_POOL        0x00000010          // Alloc & Free's

#define D_PAGE        0x00000020          // Alloc & Free's

#define D_INFO        0x00000040          // Verbose

#define D_VAR         0x00000100          // Variable

#define D_PARSE       0x00000200          // Command parsing

#define D_BM          0x00000400          // Boot manager

#define D_BLKIO       0x00001000          // BlkIo Driver

#define D_BLKIO_ULTRA 0x00002000          // BlkIo Driver

#define D_ERROR       0x80000000          // Error

Examples

Shell> err

EFI ERROR 0000000080001007

Shell> err 80003007

EFI ERROR 80003007

### getmtc

getmtc

This command displays the current monotonic counter value.  The lower 32 bits increment every time this command is executed.  Every time the system is reset, the upper 32 bits will be incremented, and the lower 32 bits will be reset to 0.

Examples

Shell> getmtc

Monotinic count = 700000000

Shell> getmtc

Monotonic count = 700000001

### mm

mm Address [Width 1|2|4|8] [;MMIO | ;MEM | ;IO | ;PCI] [:Value] [-n]

Address – Start address

Width   - Size access in bytes.  Default is 1 byte.

MEM     - Memory Address 0 - 0xffffffff_ffffffff

MMIO    - Memory Mapped IO Address 0 - 0xffffffff_ffffffff

IO      - IO Address 0 - 0xffff

PCI     - PCI Config Address 0x000000ssbbddffrr

ss-> _SEG  bb-> bus  dd-> Device  ff-> Func  rr-> Register

Value   - The value to write

[-n]    - Nonintewractive mode

Allows the user to display and/or modify I/O register, memory contents, or PCI configuration space.  The user can specify the start address and the access size they wish to perform using the Address and Width parameters.  MEM accesses system memory, MMIO accesses device memory, IO accesses device I/O ports, and PCI accesses PCI Configuration Space.  When this command is executed, the current contents of Address are displayed, and the user has the option of modifying the contents by typing in a hex value.  When the user pressed [ENTER], then next address is displayed.  This is continued until the user enter ‘q’.

Examples

Shell> mm 80 1 ;IO

IO  0x0000000000000080 : 0x0E > aa

IO  0x0000000000000081 : 0x00 >

IO  0x0000000000000082 : 0x00 > q

Shell>

### mv

mv file1 file2

This command moves a file from the path specified by file1 to the path specified by file2.  This command can be used to rename file, or move a file from one directory into another directory.

Examples

Shell> mv fs0:\a.txt fs0:\b.txt

mv: fs0:\a.txt -> fs0:\b.txt [ok]

Shell> mv fs0:\a.txt fs0:\efi\a.txt

mv: fs0:\a.txt -> fs0:\efi\a.txt [ok]

### pci

pci

Displays all the PCI devices found in the system.

Examples

Shell> pci

Bus  Dev  Func

---  ---  ----

0    0     0 ==> PCI Bridge Device - Host

Vendor 0x8086 Device 0x7192 Prog Interface 0

0    2     0 ==> PCI Bridge Device - CardBus

Vendor 0x104C Device 0xAC16 Prog Interface 0

0    2     1 ==> PCI Bridge Device - CardBus

Vendor 0x104C Device 0xAC16 Prog Interface 0

0    3     0 ==> Display Controller - VGA

Vendor 0x10C8 Device 0x0004 Prog Interface 0

0    7     0 ==> PCI Bridge Device -

Vendor 0x8086 Device 0x7110 Prog Interface 0

0    7     1 ==> Mass Storage Controller - IDE

Vendor 0x8086 Device 0x7111 Prog Interface 80

0    7     2 ==> Serial Bus Controller - USB

Vendor 0x8086 Device 0x7112 Prog Interface 0

0    7     3 ==> PCI Bridge Device -

Vendor 0x8086 Device 0x7113 Prog Interface 0

### reset

reset [/warm] [reset string]

[/warm]         - Perform a warm reset

[reset string]  – String to pass to reset API.

Resets the system.  The default is to perform a cold reset unless the /warm parameter is specified.  If reset string is specified, then it is passed into the Reset() function, so the system can know the reason for the system reset.

Examples

Shell> reset

Shell> reset /warm

Shell>

### setsize

setsize newsize filename

newsize  – The new size of the file in bytes.

filename – The file path of the file to resize.

This command sets the size of the file specified by filename to newsize bytes.  This command can be used to either shrink or grow and existing file.

Examples

Shell> setsize fs0:\a.txt 100

setsize: fs0:\a.txt 100

Shell> setsize fs0:\a.txt 0

setsize: fs0:\a.txt 0

Shell>

### stall

stall microseconds

microseconds  - Time to stal in microseconds

This command stalls the processor for the number of microseconds specified by microseconds.

Examples

Shell> stall 1000000

Stall for 1000000 uS

Shell>

### touch

touch filename

This command updates the time and date on file specified by filename to the current time and date.

Examples

Shell> touch fs0:\a.txt

touch: fs0:\a.txt [ok]

Shell>

# Writing EFI Shell Commands

This section describes how to write, compile, and modify the set of commands available from the EFI Shell environment.  The EFI Shell is provided as part of the EFI Application Toolkit.  The EFI Shell can either be built as a stand alone set of applications from the EFI Application Toolkit, or they can be integrated into the EFI Sample Implementation.  This section describes how to write EFI Shell commands that are built as part of the EFI Sample Implementation.  Please see the release notes for the EFI Sample Implementation for directions on how to import the EFI Shell from the EFI Application Toolkit.

## Writing a Shell Command

EFI Shell commands can be added to the EFI source tree.  It is recommended that the EFI Shell commands be placed below the \efi\shell directory.  To add a new shell command to the build environment, a new subdirectory needs to be created, and a make.inf file along with the command’s source code needs to be placed in that subdirectory.  There are two types of shell commands that can be written.  One is an internal shell command, and the other is an external shell command.  Internal shell commands are built into the EFI Shell itself.  This means that the image for the shell command is resident in memory along with the rest of the EFI Shell.  External shell commands reside on a storage device, and they are loaded into memory from the storage device each time they are executed.  For this example, the files for an internal EFI Shell command that displays all of the command line arguments are placed in the directory itestcmd, and their contents are listed below.  The make.inf file specifies a list of source files, the path to the include directories, the path of the library directories, the entry point for the application, and the name of the executable EFI Shell command.  The contents of make.inf are listed below.

[sources]

itestcmd.c

[includes]

.

..\inc

$(EFI_SOURCE)\inc

[libraries]

$(EFI_SOURCE)\lib

$(EFI_SOURCE)\shell\lib

[nmake]

IMAGE_ENTRY_POINT=InitializeInternalTestCommand

TARGET_APP=itestcmd

The source to the EFI Shell command itestcmd listed below is a shell command that displays the list of command line parameters on the console out device.  It makes use of some EFI Library calls, and some EFI Shell support functions.  The call to InstallInternalShellCommand() registers the command with the shell as an internal command, so the command can be executed without loading it from a storage device.  It also provides the EFI Shell with the information required to display help on the command’s usage.

/*++

Copyright (c) 1998  Intel Corporation

Module Name:

itestcmd.c

Abstract:

Shell app "itestcmd"

Author:

Revision History

--*/

#include "shell.h"

EFI_STATUS

InitializeInternalTestCommand (

IN EFI_HANDLE           ImageHandle,

IN EFI_SYSTEM_TABLE     *SystemTable

);

EFI_DRIVER_ENTRY_POINT(InitializeInternalTestCommand)

EFI_STATUS

InitializeInternalTestCommand (

IN EFI_HANDLE           ImageHandle,

IN EFI_SYSTEM_TABLE     *SystemTable

)

{

CHAR16 **Argv;

UINTN  Argc;

UINTN  i;

//

// Check to see if the app is to be installed as a "internal command"

// to the shell

//

InstallInternalShellCommand (

ImageHandle,   SystemTable,   InitializeInternalTestCommand,

L"itestcmd",                    // command

L"itestcmd",                    // command syntax

L"Displays argc/argv list",     // 1 line descriptor

NULL                            // command help page

);

//

// We are not being installed as an internal command driver, initialize

// as an nshell app and run

//

InitializeShellApplication (ImageHandle, SystemTable);

//

// Get Argc and Argv.

//

Argv = SI->Argv;

Argc = SI->Argc;

//

// Display list of argumnents.

//

for(i=0;i<Argc;i++) {

Print(L"Argv[%d] = %s\n",i,Argv[i]);

}

return EFI_SUCCESS;

}

## Compiling a Shell Command

EFI Shell commands are PE/COFF images with a modified header signature.  The modified header helps distinguish EFI images from PE/COFF images.  Please refer to the EFI Specification for details on EFI images.

Before the EFI image type is integrated into the standard commercial tool chain, a utility for converting PE/COFF images to 64-bit EFI images is available. This will be provided with the initial release of the EFI Sample Implementation.

Before a new EFI Shell command can be compiled, the makefile for each build tip need to be modified.  These files include:

\efi\build\nt32\makefile

\efi\build\sal64\makefile

\efi\build\bios32\makefile

\efi\build\ia-32emb\makefile

In each of these files, there are two sections that need to be updated.  These are the list of EFI Shell command libraries, and the list of EFI Shell command makefiles.  A line needs to be added to each of these section for each EFI Shell command that is added.  An example for the itestcmd EFI Shell command is shown below:

!IF "$(EFI_BOOTSHELL)" == "YES"

EFI_LIBS = $(EFI_LIBS)  \

output\shell\newshell\newshell.lib                  \

output\shell\shellenv\shellenv.lib                  \

output\shell\lib\lib.lib                            \

output\shell\rm\rm.lib                              \

. . .

output\shell\edit\edit.lib                          \

output\shell\itestcmd\itestcmd.lib                  \

!ENDIF

. . .

makemaker:

. . .

$(MAKE) -f output\shell\err\makefile                          all

$(MAKE) -f output\shell\vol\makefile                          all

$(MAKE) -f output\shell\bcfg\makefile                         all

$(MAKE) -f output\shell\cls\makefile                          all

$(MAKE) -f output\shell\edit\makefile                         all

$(MAKE) -f output\shell\itestcmd\makefile                     all

!ENDIF

If an EFI Shell command is going to be an internal command, one more file need to be updated.  This is \efi\corefw\fw\inc\plshell.h.  This file must declare the entry point to the new command.  For this example, this entry point is InitializeInternalTestCommand().  The other change to this file is to the declaration of the PlLoadShellTools() define.  This define must be appended with a call to LOAD_INTENAL_DRIVER() for the itestcmd command.  A portion of the modified version of plshell.h is shown below.  Please refer to the sample code for a complete listing of this file.

EFI_STATUS

InitializeInternalTestCommand (

IN EFI_HANDLE           ImageHandle,

IN EFI_SYSTEM_TABLE     *SystemTable

);

#define PlLoadShellTools()                          \

\

LOAD_INTERNAL_DRIVER(                           \

FW,                                         \

IMAGE_SUBSYSTEM_EFI_BOOT_SERVICE_DRIVER,    \

L"shellenv",                                \

InitializeShellEnviroment                   \

);                                          \

\

LOAD_INTERNAL_DRIVER(                           \

FW,                                         \

IMAGE_SUBSYSTEM_EFI_BOOT_SERVICE_DRIVER,    \

L"ls",                                      \

InitializeLS                                \

);                                          \

\

.

.

.

\

LOAD_INTERNAL_DRIVER(                           \

FW,                                         \

IMAGE_SUBSYSTEM_EFI_BOOT_SERVICE_DRIVER,    \

L"itestcmd",                                \

InitializeInternalTestCommand               \

);                                          \

Once all of these changes have been made to the EFI build environment the code can be built as normal from one of the build tips.  If an internal EFI shell command has been added, then the new command will be available from the EFI Shell, and the command should be listed when the help command is executed.  If a new EFI Shell command is not an internal shell command, then the image for the new command will have to be placed on a storage device where the EFI Shell can find it.  The new EFI Shell command can then be loaded and executed.

## Adding Commands to the EFI Shell

The following is a summary of the steps required to add a new standard EFI Shell command to the EFI Shell.

- Create a new directory for the command below \efi\shell\

- Place make.inf and the source files to the new command in the new directory.

- Update the makefile in each of the build tips to include the new command.

If the new EFI Shell command is going to be an internal command, then the following three steps also need to be performed.

- Add a declaration to the entry point of the new command to \efi\corefw\fw\inc\plshell.h.

- Add a call to LOAD_INTERNAL_DRIVER for the new command to #define PlLoadShellTools in the file \efi\corefw\fw\inc\plshell.h.

## Removing Commands from the EFI Shell

If a command needs to be removed from the EFI shell, then undo the steps listed in previous section.

# EFI Applications

This section describes how to write, compile, and run applications in the sample implementation of the EFI environment.  Building applications in the sample implementation is described for illustration purposes.

## Writing EFI Applications

EFI Applications can be added to the EFI source tree.  It is recommended that all stand alone EFI Applications be placed below the \efi\apps directory.  This recommendation is not strictly required.  However, it does provide a convenient build environment.  To add a new application to the build environment, a new subdirectory needs to be created, and a make.inf file along with the source code needs to be placed in that subdirectory.  For this example, the files for a simple test application are placed in the directory hello, and their contents are listed below.  The make.inf file specifies a list of source files, the path to the include directories, the path the library directories, the entry point for the application, and the name of the executable EFI Application image.  The contents of make.inf are listed below.

[sources]

hello.c

[includes]

$(EFI_SOURCE)\inc

[libraries]

$(EFI_SOURCE)\lib

[nmake]

IMAGE_ENTRY_POINT=InitializeHelloApplication

TARGET_APP=hello

The test application listed below is the simplest possible application that can be written.  It does not depend upon any EFI Library functions, so the EFI Library is not linked into the executable that is generated.  This test application uses the SystemTable that is passed into the entry point to get access to the EFI console devices.  The console output device is used to display a message using the OutputString() function of the SIMPLE_TEXT_OUTPUT_INTERFACE protocol, and the application waits for a keystroke from the user on the console input device using the WaitForEvent() service with the WaitForKey event in the SIMPLE_INPUT_INTERFACE protocol.  Once a key is pressed, the application exits.

/*++

Copyright (c) 1998  Intel Corporation

Module Name:

hello.c

Abstract:

Author:

Revision History

--*/

#include "efi.h"

EFI_STATUS

InitializeHelloApplication (

IN EFI_HANDLE           ImageHandle,

IN EFI_SYSTEM_TABLE     *SystemTable

)

{

UINTN Index;

//

// Send a message to the ConsoleOut device.

//

SystemTable->ConOut->OutputString(SystemTable->ConOut,

L"Hello application started\n\r");

//

// Wait for the user to press a key.

//

SystemTable->ConOut->OutputString(SystemTable->ConOut,

L"\n\r\n\r\n\rHit any key to exit\n\r");

SystemTable->BootServices->WaitForEvent (1,

&(SystemTable->ConIn->WaitForKey),

&Index);

SystemTable->ConOut->OutputString(SystemTable->ConOut,L"\n\r\n\r");

//

// Exit the application.

//

return EFI_SUCCESS;

}

## Compiling EFI Applications

EFI applications are PE/COFF images with a modified header signature.  The modified header helps distinguish EFI images from PE/COFF images.  Please refer to the EFI Specification for details on EFI images.

Before the EFI image type is integrated into the standard commercial tool chain, a utility for converting PE/COFF images to 64-bit EFI images is available. This will be provided with the initial release of the EFI sample implementation.

Before a new EFI application can be compiled, the makefile for each build tip need to be modified.  These files include:

\efi\build\ntdbg32\makefile

\efi\build\sal64\makefile

\efi\build\saldbg64\makefile

\efi\build\bios32\makefile

\efi\build\biosdbg32\makefile

In each of these files, there is a section labeled "makemaker".  Add a line to the end of this section for each new EFI application.  The section of a makefile that supports two test applications is listed below.  Once these changes have been made, the new application will be compiled when nmake is run from a build tip.

makemaker:

. . .

!IF "$(EFI_BOOTSHELL)" == "YES"

. . .

!ENDIF

$(MAKE) -f output\apps\hello\makefile                       all

$(MAKE) -f output\apps\hellolib\makefile                    all

## Writing EFI Applications with EFI Library Support

If an EFI Application wants to use the EFI Library functions, then the file efilib.h needs to be included, and a call to InitializeLib() needs to be added.  The following is a listing of the EFI application hellolib.c.  This application makes use of the EFI Library to print text to the console output device.  It also uses the global variable ST instead of SystemTable to make the standard EFI API calls.

/*++

Copyright (c) 1999  Intel Corporation

Module Name: hellolib.c

Abstract: This is an example EFI program

Author:

Revision History: 1.0

--*/

#include "efi.h"

#include "efilib.h"

EFI_STATUS

InitializeHelloLibApplication (

IN EFI_HANDLE           ImageHandle,

IN EFI_SYSTEM_TABLE     *SystemTable

)

{

//

// Initialize the Library. Set BS, RT, &ST globals

//  BS = Boot Services

//  RT = RunTime Services

//  ST = System Table

//

InitializeLib (ImageHandle, SystemTable);

//

// Print a message to the console device using a library function.

//

Print(L"HelloLib application started\n");

//

// Wait for a key to be pressed on the console device.

//

Print(L"\n\n\nHit any key to exit this image\n");

WaitForSingleEvent (ST->ConIn->WaitForKey, 0);

//

// Print a message to the console device using a protocol interface.

//

ST->ConOut->OutputString (ST->ConOut, L"\n\n");

//

// Return control to the Shell.

//

return EFI_SUCCESS;

}

## Running EFI Applications

An EFI application may be executed by typing the program’s name at the EFI shell command line.  The following examples show how to run the test applications described in the sections above from the EFI Shell.  Both applications wait for the user to press a key before they will return to the EFI Shell prompt.  It is assumed that hello.efi and hellolib.efi are in the search path of the EFI Shell environment.

Examples

Shell> hello

Hello application started

Hit any key to exit this image

Shell> hellolib

HelloLib application started

Hit any key to exit this image

Shell>

# EFI OS Loaders

This section discusses the special considerations required when writing an OS loader.  An OS loader is a special type of EFI Application.  It is responsible for transitioning a system from a firmware environment into an Operating System environment.  To accomplish this task, several important steps must be taken.

- The OS loader must determine where it was loaded from.  This will allow an OS loader to retrieve additional files from the same location.

- The OS loader must determine where in the system the OS exists.  Typically, the OS will reside on a partition of a hard drive.  However, the partition where the OS exists may not use a file system that is recognized by the EFI environment.  In this case, the OS loader can only access the partition as a block device using only block I/O operations.  The OS loader will then be required to implement or load the file system driver to access files on the OS partition.

- The OS loader must build a memory map of the physical memory resources so that the OS kernel can know what memory to manage.  Some of the physical memory in the system must remain untouched by the OS kernel, so the OS loader must use the EFI APIs to retrieve the system’s current memory map.

- An OS has the option of storing boot paths and boot options in non-volatile storage in the form of environment variables.  The OS loader may need to use some of the environment variables stored in non-volatile storage.  In addition, the OS loader may be required to pass some of the environment variables to the OS kernel.

- The next step is to call ExitBootServices().  This can be done from either the OS loader, or from the OS kernel.  Special care must be taken to guarantee that the most current memory map has been retrieved prior to making this call.  Once ExitBootServices() had been called, no more EFI Boot Time Service calls can be made.  At some point, either just prior to calling ExitBootServices() or just after, the OS loader will transfer control to the OS kernel.

- Finally, after ExitBootServices() has been called, the EFI Boot Service calls are no longer available.  This means that once an OS kernel has taken control of the system, the OS kernel may only make EFI Run Time Service calls.

A complete listing of the an OS Loader sample application can be found in Appendix E, and the output from the OS loader sample can be found in Appendix F. The code fragments in the following sections do not perform any error checking.  The code listing in Appendix E has similar code sections, but all the return status codes are checked.  Also, the OS Loader sample application makes use of several EFI Library functions to simplify the implementation.

The output shown in Appendix F shows the OS loader sample going through the steps listed above.  It starts by printing out the device path and the file path of the OS loader itself.  It also shows where in memory the OS loader resides, and how many bytes it is using.  Next, it loads the file OSKERNEL.BIN into memory.  The file OSKERNEL.BIN was retrieved from the same directory as the image of the OS loader sample.

The next section of the output shows the first block of several block devices.  The first one is the first block of floppy drive with a FAT12 file system.  The second one is the Master Boot Record from the hard drive.  The third one is the first block of a large FAT32 partition on the same hard drive, and the fourth one is the first block of a smaller FAT16 partition on the same hard drive.

The next section shows the pointers to all the system configuration tables, the system’s current memory map, and a list of all the system’s environment variables.  The very last step shown is the OS loader calling ExitBootServices().

## Device Path and Image Information of the OS Loader

The following code fragment shows the steps required to get the device path and file path to the OS loader itself.  The first call to HandleProtocol() gets the LOADED_IMAGE_PROTOCOL interface from the ImageHandle that was passed into the OS loader application.  The second call to HandleProtocol() gets the DEVICE_PATH_PROTOCOL interface to the device handle of the OS loader image.  With these two calls, the device path of the OS loader image is known, and the file path along with other image information is known about the OS loader.

BS->HandleProtocol(ImageHandle, &LoadedImageProtocol, LoadedImage);

BS->HandleProtocol(LoadedImage->DeviceHandle, &DevicePathProtocol, &DevicePath);

Print (L"Image device : %s\n", DevicePathToStr (DevicePath));

Print (L"Image file   : %s\n", DevicePathToStr (LoadedImage->FilePath));

Print (L"Image Base   : %X\n", LoadedImage->ImageBase);

Print (L"Image Size   : %X\n", LoadedImage->ImageSize);

## Accessing Files in the Device Path of the OS Loader

Section 5.1 shows how to retrieve the device path and the image path of the OS loader image.  The following code fragment shows how to use this information to open another file called OSKERNEL.BIN that resides in the same directory as the OS loader itself.  The first step is to use HandleProtocol() to get the FILE_SYSTEM_PROTOCOL interface to the device handle retrieved in the previous section.  Then, the disk volume can be opened so file access calls can be made.  The end result is that the variable CurDir is a file handle to the same partition that the OS loader resides.

BS->HandleProtocol(LoadedImage->DeviceHandle, &FileSystemProtocol, &Vol);

Vol->OpenVolume (Vol, &RootFs);

CurDir = RootFs;

The next step is to build a file path to OSKERNEL.BIN that exists in the same directory as the OS loader image.  Once the path is built, the file handle CurDir can be used to perform Open, Close, Read, and Write calls on the OSKERNEL.BIN file.  The following code fragment builds a file path, opens the file, reads it into an allocated buffer, and closes the file.

StrCpy(FileName,DevicePathToStr(LoadedImage->FilePath));

for(i=StrLen(FileName);i>=0 && FileName[i]!='\\';i--);

FileName[i] = 0;

StrCat(FileName,L"\\OSKERNEL.BIN");

CurDir->Open (CurDir, &FileHandle, FileName, EFI_FILE_MODE_READ, 0);

Size = 0x00100000;

BS->AllocatePool(EfiLoaderData, Size, &OsKernelBuffer);

FileHandle->Read(FileHandle, &Size, OsKernelBuffer);

FileHandle->Close(FileHandle);

## Finding the OS Partition

The EFI sample environment materializes a BLOCK_IO_PROTOCOL instance for every partition found in a system.  An OS loader can search for OS partitions by looking at all the BLOCK_IO devices.  The following code fragment uses LibLocateHandle() to get a list of BLOCK_IO device handles.  These handles are then used to retrieve the first block from each one of these BLOCK_IO devices.  The HandleProtocol() API is used to get the DEVICE_PATH_PROTOCOL and the BLOCK_IO_PROTOCOL instances for each of the BLOCK_IO devices.  The variable BlkIo is a handle to the BLOCK_IO device using the BLOCK_IO_PROTOCOL interface.  At this point, a ReaddBlocks() call can be used to read the first block of a device.  The sample OS loader just dumps the contents of the block to the display.  A real OS loader would have to test each block read to see if it is a recognized partition.  If a recognized partition is found, then the OS loader can implement a simple file system driver using the EFI API ReadBlocks() to load additional data from that partition.

NoHandles = 0;

HandleBuffer = NULL;

LibLocateHandle(ByProtocol, &BlockIoProtocol, NULL, &NoHandles, &HandleBuffer);

for(i=0;i<NoHandles;i++) {

BS->HandleProtocol (HandleBuffer[i], &DevicePathProtocol, &DevicePath);

BS->HandleProtocol (HandleBuffer[i], &BlockIoProtocol, &BlkIo);

Block = AllocatePool (BlkIo->BlockSize);

MediaId = BlkIo->MediaId;

BlkIo->ReadBlocks(BlkIo, MediaId, (EFI_LBA)0, BlkIo->BlockSize, Block);

Print(L"\nBlock #0 of device %s\n",DevicePathToStr(DevicePath));

DumpHex(0,0,BlkIo->BlockSize,Block);

}

## Getting the Current System Configuration

All the system configuration is available through the SystemTable data structure that is passed into the OS loader.  There are five tables available, and their structure and contents are described in the appropriate specifications.

LibGetSystemConfigurationTable(&AcpiTableGuid,&AcpiTable);

LibGetSystemConfigurationTable(&SMBIOSTableGuid,&SMBIOSTable);

LibGetSystemConfigurationTable(&SalSystemTableGuid,&SalSystemTable);

LibGetSystemConfigurationTable(&MpsTableGuid,&MpsTable);

Print(L"  ACPI Table is at address                   : %X\n",AcpiTable);

Print(L"  SMBIOS Table is at address                 : %X\n",SMBIOSTable);

Print(L"  Sal System Table is at address             : %X\n",SalSystemTable);

Print(L"  MPS Table is at address                    : %X\n",MpsTable);

## Getting the Current Memory Map

There is one EFI Library function that can retrieve the memory map maintained by the EFI environment.  The following code fragment shows the use of this library function, and it displays the contents of memory map.  An OS loader must pay special attention to the MapKey parameter.  Every time that the EFI environment modifies the memory map that is maintains, the MapKey is incremented.  An OS loader needs to pass to current memory map to the OS kernel.  Depending on what functions the OS loader calls between the time the memory map is retrieved and the time that ExitBootServices() is called, the memory map may be modified.  In general, the OS loader should retrieve the memory map just before the call to ExitBootServices().  If ExitBootServices() fails because the MapKey does not match, then the OS loader must get a new copy of the memory map and try again.

MemoryMap = LibMemoryMap(&NoEntries,&MapKey,&DescriptorSize,&DescriptorVersion);

Print(L"Memory Descriptor List:\n\n");

Print(L"  Type        Start Address     End Address       Attributes      \n");

Print(L"  ==========  ================  ================  ================\n");

MemoryMapEntry = MemoryMap;

for(i=0;i<NoEntries;i++) {

Print(L"  %s  %lX  %lX  %lX\n",

OsLoaderMemoryTypeDesc[MemoryMapEntry->Type],

MemoryMapEntry->PhysicalStart,

MemoryMapEntry->PhysicalStart +

LShiftU64(MemoryMapEntry->NumberOfPages,PAGE_SHIFT)-1,

MemoryMapEntry->Attribute);

MemoryMapEntry = NextMemoryDescriptor(MemoryMapEntry, DescriptorSize);

}

## Getting Environment Variables

The following code fragment shows how to extract all the environment variables maintained by the EFI environment.  It uses the GetNextVariableName() API to walk the entire list.

VariableName[0] = 0x0000;

VendorGuid = NullGuid;

Print(L"GUID                                Variable Name        Value\n");

Print(L"=================================== ==================== ========\n");

do {

VariableNameSize = 256;

Status = RT-GetNextVariableName(&VariableNameSize,VariableName,&VendorGuid);

if (Status == EFI_SUCCESS) {

VariableValue = LibGetVariable(VariableName,&VendorGuid);

Print(L"%.-35g %.-20s %X\n",&VendorGuid,VariableName,VariableValue);

}

} while (Status == EFI_SUCCESS);

## Transitioning to an OS Kernel

A single call to ExitBootServices() terminates all the Boot Time Services that the EFI environment provides.  From that point on, only the EFI Run Time Services may be used.  Once this call is made, the OS loader needs to prepare for the transition to the OS kernel.  It is assumed that the OS kernel has full control of the system, and that only a few firmware functions are required by the OS kernel.  These functions are the EFI Run Time Services.  The OS loader must pass the SystemTable to the OS kernel, so the OS kernel can make the Run Time Service calls.  The exact mechanism used to transition from the OS loader to the OS kernel is implementation dependent.  It is important to note that the OS loader could transition to the OS kernel prior to calling ExitBootServices().  In this case, the OS kernel is responsible for calling ExitBootServices() before taking full control of the system.

EFI Boot Time Services

A high level description of the EFI Boot Time Services are described in this section. These services are APIs exported by the EFI environment, and they are only available at boot time before an operating system takes control of the system.  Once a call to ExitBootServices() is made, the EFI Boot Time Service APIs may no longer be used.   The EFI Boot Time Services are organized into the following groups.

- Event Services

- Memory Allocation Services

- Protocol Handler Services

- Image Services

- Miscellaneous Services

Event Services

Table A-1 lists the functions used to manage events.

Table A-1.	Event Services

| Name | Description |
| --- | --- |
| CreateEvent | Creates a general-purpose event structure. |
| CloseEvent | Closes and frees an event structure. |
| CheckEvent | Checks whether an event is in the signaled state. |
| SignalEvent | Signals an event. |
| RaiseTPL | Raises the task priority level. |
| RestoreTPL | Restores/lowers the task priority level. |
| SetTimer | Sets an event to be signaled at a particular time. |
| WaitForEvent | Waits for an event to be signaled. |

Memory Allocation Services

Table A-2 lists the functions used to allocate and free memory.

Table A-2.	Memory Allocation Services

| Name | Description |
| --- | --- |
| AllocatePages | Allocates memory pages of a particular type. |
| FreePages | Frees memory pages. |
| GetMemoryMap | Returns the current boot services memory map and memory map key. |
| AllocatePool | Allocates pool of a particular type. |
| FreePool | Frees allocated pool. |

Protocol Handler Services

Table A-3 lists the functions used to manage protocol handles.

Table A-3.	Protocol Handler Services

| Name | Description |
| --- | --- |
| InstallProtocolInterface | Adds protocol handler onto an existing or new device handle. |
| UninstallProtocolInterface | Removes a protocol handler from a device handle. |
| ReinstallProtocolInterface | Replaces a protocol interface. |
| HandleProtocol | Queries the list of protocol handlers on a device handle for the requested Protocol Interface. |
| RegisterProtocolNotify | Registers for protocol interface installation notifications |
| LocateHandle | Locates the handle(s) that support the specified protocol. |
| LocateDevicePath | Locates the closest handle that supports the specified protocol on the specified device path. |

Image Services

Table A-4 lists the functions used load, execute, and exit EFI images.

Table A-4.	Image Services

| Name | Description |
| --- | --- |
| LoadImage | Function to dynamically load another EFI Image. |
| StartImage | Function to transfer control to the Image’s entry point. |
| EFI_IMAGE_ENTRY_POINT | Prototype of an EFI Image’s entry point. |
| Exit | Exits the image’s entry point. |
| UnloadImage | Unloads an image loaded with LoadImage. |
| ExitBootServices | Terminates boot services. |

Miscellaneous Services

Table A-5.	Miscellaneous Services

| Name | Description |
| --- | --- |
| SetWatchdogTimer | Resets and sets the system’s watchdog timer. |
| Stall | Stall the processor for a specified number of microseconds. |
| GetNextMonotonicCount | Returns a monotonically increasing count for the platform. |
| InstallConfigurationTable | Adds, updates, or removes a configuration table from the EFI System Table |

EFI Run Time Services

A high level description of the EFI Run Time Services are described in this section. These services are APIs exported by the EFI environment, and they are always available.  The EFI Run Time Services are organized into the following groups.

- Variable Services

- Time Services

- Virtual Memory Services

- Miscellaneous Services

Variable Services

The Variable Services are used to maintain environment variables in non-volatile storage.  Table B-1 lists the functions available for retrieving, creating, modifying, and deleting environment variables in non-volatile storage.

Table B-1.	Variable Services

| Name | Description |
| --- | --- |
| GetVariable | Returns the value of the specified variable |
| GetNextVariableName | Enumerates the current variables names |
| SetVariable | Sets the value of the specified variable. |

Time Services

Table B-2 lists the functions available to access the system’s Real Time Clock (RTC) and timer hardware.

Table B-2.	Time Services

| Name | Description |
| --- | --- |
| GetTime | Returns the current time and date information. |
| SetTime | Sets the current time and date. |
| GetWakeupTime | Returns the current wakeup alarm clock setting. |
| SetWakeupTime | Sets the current wakeup alarm clock setting. |

Virtual Memory Services

Table B-3 lists the functions used transition the firmware from flat physical  mode to virtual runtime mode.

Table B-3.	Virtual Memory Services

| Name | Description |
| --- | --- |
| SetVirtualAddressMap | Used by an OS loader to convert from physical addressing to virtual addressing. |
| ConvertPointer | Used by EFI components to convert internal pointers when switching to virtual addressing. |

Miscellaneous Services

Table B-4 lists the miscellaneous runtime services.

Table B-4.	Miscellaneous Services

| Name | Description |
| --- | --- |
| GetNextHighMonotonicCount | Subsumes the platform’s monotonic counter functionality. |
| ResetSystem | Resets all processors and devices and reboots the system. |

EFI Protocol Interfaces

A high level description of the EFI Protocol Interfaces are described in this section. These services are APIs exported by the EFI environment through GUID based protocol handles.  The standard set of protocol interfaces are listed here.  Additional protocol interfaces may be added to a system by an EFI device driver.  The EFI Protocol Interfaces are organized into the following groups.

- Device Path Protocol

- Device I/O Protocol

- Simple Input Protocol

- Simple Text Output Protocol

- Block I/O Protocol

- Disk I/O Protocol

- File System Protocol

- Load File Protocol

- Loaded Image Protocol

- Serial I/O Protocol

- Unicode Collation Protocol

- PXI I/O Protocol

- Simple Network Protocol

Device Path Protocol

This protocol does not contain any interfaces.  It simply returns a pointer to the device path for the protocol instance.

Device I/O Protocol

Table C-2 lists the functions used by device drivers to access hardware devices in a bus specific manner.

Table C-2.	Device I/O Protocol Interfaces

| Name | Description |
| --- | --- |
| Mem.Read | Reads from memory on a bus. |
| Mem.Write | Writes to memory on a bus. |
| Io.Read | Reads from I/O ports on a bus. |
| Io.Write | Writes to I/O ports on a bus. |
| Pci.Read | Reads from PCI Configuration Space. |
| Pci.Write | Writes to PCI Configuration Space. |
| PciDevicePath | Provides an EFI Device Path for a PCI device with the given PCI configuration space address. |
| Map | Provides the device specific addresses needed to access host memory for DMA. |
| Unmap | Releases any resources allocated with Map() |
| AllocateBuffer | Allocates pages that are suitable for a common buffer mapping. |
| Flush | Flushes any posted write data to the device. |
| FreeBuffer | Frees pages that were allocated with AllocateBuffer() |

Simple Input Protocol

Table C-3 lists the functions used to access a simple input hardware device.

Table C-3.	Simple Input Protocol Interfaces

| Name | Description |
| --- | --- |
| Reset | Resets a simple input device. |
| ReadKeyStroke | Read a keystroke from a simple input device. |

Simple Text Output Protocol

Table C-4 lists the functions used to access the standard output device, the standard error device, or any other text based output device.

Table C-4.	Simple Text Output Protocol Interfaces

| Name | Description |
| --- | --- |
| Reset | Reset the ConsoleOut device. |
| OutputString | Displays the Unicode string on the device at the current cursor location. |
| TestString | Test to see if the ConsoleOut device supports this Unicode string. |
| QueryMode | Queries information concerning the output device’s supported text mode. |
| SetMode | Sets the current mode of the output device. |
| SetAttribute | Sets the foreground and background color of the text that is output. |
| ClearScreen | Clears the screen with the currently set background color. |
| SetCursorPosition | Sets the current cursor position. |
| EnableCursor | Turns on/off the visibility of the cursor. |

Block I/O Protocol

Table C-5 lists the functions used to access a block based I/O device.

Table C-5.	Block I/O Protocol Interfaces

| Name | Description |
| --- | --- |
| Reset | Resets the block device hardware. |
| ReadBlocks | Reads the requested number of blocks from the device. |
| WriteBlocks | Writes the requested number of blocks to the device. |
| FlushBlocks | Flushes any cached blocks. |

Disk I/O Protocol

Table C-6 lists the functions used to access a block based I/O device as a byte stream device.

Table C-6.	Disk I/O Protocol Interfaces

| Name | Description |
| --- | --- |
| ReadDisk | Reads data from the disk. |
| WriteDisk | Writes data to the disk. |

Simple File System Protocol

Table C-7 lists the functions used to open a partition for file access.

Table C-7.	Simple File System Protocol Interfaces

| Name | Description |
| --- | --- |
| OpenVolume | Opens the volume for file I/O access. |

File System Protocol

Table C-8 lists the functions used to maintain files in a partition containing a supported file system.

Table C-8.	File System Protocol Interfaces

| Name | Description |
| --- | --- |
| Open | Opens or creates a new file. |
| Close | Closes the current file handle. |
| Delete | Deletes a file. |
| Read | Reads bytes from the file. |
| Write | Writes bytes to the file. |
| SetPosition | Sets the current file position. |
| GetPosition | Returns the current file position. |
| GetInfo | Gets the requested file or volume information. |
| SetInfo | Sets the requested file information. |
| Flush | Flushes all modified data associated with the file to the device. |

Load File Protocol

Table C-9 lists the functions used to load drivers from sources other than a file system.

Table C-9.	Load File Protocol Interfaces

| Name | Description |
| --- | --- |
| LoadFile | Causes the driver to load the requested file. |

Loaded Image Protocol

Table C-10 lists the functions used to load drivers from sources other than a file system.

Table C-10.	Loaded Image Protocol Interfaces

| Name | Description |
| --- | --- |
| Unload | Requests an image to unload. |

Serial I/O Protocol

Table C-11 lists the functions used to access a serial I/O device.

Table C-11.	Serial I/O Protocol Interfaces

| Name | Description |
| --- | --- |
| Reset | Resets the hardware device. |
| SetAttributes | Sets communication parameters for a serial device. These include the baud rate, receive FIFO depth, transmit/receive time out, parity, data bits, and stop bit attributes. |
| SetControl | Set the control bits on a serial device. These include Request to Send and Data Terminal Ready. |
| GetControl | Read the status of the control bits on a serial device. These include Clear to Send, Data Set Ready, Ring Indicator, and Carrier Detect. |
| Write | Send a buffer of characters to a serial device. |
| Read | Receive a buffer of characters from a serial device. |

Unicode Collation Protocol

Table C-12 lists the functions used to perform case insensitive Unicode string comparisons.

Table C-12.	Unicode Collation Protocol Interfaces

| Name | Description |
| --- | --- |
| StriColl | Performs a case insensitive comparison between two Unicode strings. |
| MetaiMatch | Performs a case insensitive comparison between aUnicode pattern string and a Unicode string. The pattern string can use the ‘?’ wildcard for match any character, and the ‘*’ wildcard for match any substring. |
| StrLwr | Converts characters in a Unicode string to upper case characters. |
| StrUpr | Converts characters in a Unicode string to lower case characters. |
| FatToStr | Converts a FAT 8.3 file name to a Unicode string |
| StrToFat | Converts a Unicode string to a FAT 8.3 file name. |

PXE I/O Protocol

Table C-13 lists the functions used to access a network device.

Table C-13.	PXE I/O Protocol Interfaces

| Name | Description |
| --- | --- |
| Arp | Uses the ARP protocol to resolve a MAC address. |
| Dhcp | Attempts to complete a DHCPv4 D.O.R.A. (discover / offer / request / acknowledge) or DHCPv6 S.A.R.R (solicit / advertise / request / reply) sequence. |
| Discover | Attempts to complete the PXE Boot Server and/or boot image discovery sequence. |
| EFI_PXE_BASE_CODE _CALLBACK | Callback function that is invoked when the PXE Base Code Protocol is waiting for an event. |
| Mtftp | Is used to perform TFTP and MTFTP services. |
| SetIpFilter | Updates the IP receive filters of a network device and enables software filtering. |
| SetPackets | Updates the contents of the cached DHCP and Discover packets. |
| SetParameters | Updates the parameters that affect the operation of the PXE Base Code Protocol. |
| SetStationIp | Updates the station IP address and/or subnet mask values. |
| Start | Enables the use of PXE Base Code Protocol functions. |
| Stop | Disables the use of PXE Base Code Protocol functions. |
| UdpRead | Reads a UDP packet from a network interface. |
| UdpWrite | Writes a UDP packet to a network interface. |

Simple Network Protocol

Table C-14 lists the functions used to access a network device.

Table C-14.	Simple Network Protocol Interfaces

| Name | Description |
| --- | --- |
| GetStatus | Reads the current interrupt status and recycled transmit buffer status from the network interface. |
| Initialize | Resets the network adapter and allocates the transmit and receive buffers required by the network interface; also optionally allows space for additional transmit and receive buffers to be allocated |
| MCastIPtoMAC | Allows a multicast IP address to be mapped to a multicast HW MAC address. |
| NVData | Allows read and writes to the NVRAM device attached to a network interface. |
| Receive | Receives a packet from the network interface. |
| Reset | Resets the network adapter, and re-initializes it with the parameters that were provided in the previous call to Initialize(). |
| Shutdown | Resets the network adapter and leaves it in a state safe for another driver to initialize. |
| Start | Changes the network interface from the stopped state to the started state. |
| StationAddress | Allows the station address of the network interface to be modified. |
| Statistics | Allows the statistics on the network interface to be reset and/or collected. |
| Stop | Changes the network interface from the started state to the stopped state. |
| Transmit | Places a packet in the transmit queue of the network interface. |

EFI Library Functions and Macros

A high level description of the EFI library functions and macros are described in this section. These library functions are complementary to the APIs described in the EFI specification.

EFI library functions and macros are organized into the following groups.

- Initialization Functions

- Linked List Support Macros

- String Functions

- Memory Support Functions

- CRC Support Functions

- Text I/O Functions

- Math Functions

- Spin Lock Functions

- Handle and Protocol Functions

- File I/O Support Functions

- Device Path Support Functions

- Miscellaneous Functions

Initialization Functions

The initialization functions in the EFI Library are used to initialize the execution environment so that other EFI Library function may be used.  Table D-1 lists the initialization support.

Table D-1.	Initialization Functions

| Name | Description |
| --- | --- |
| InitializeLib | Initializes the EFI Library. |
| InitializeUnicodeSupport | Initializes the use of language dependant Unicode library functions. |

Linked List Support Macros

The EFI Library supplies a set of macros that allow doubly linked lists to be created and maintained.  Table D-2 contains the list of macros.

Table D-2.	Linked List Support Macros

| Name | Description |
| --- | --- |
| InitializeListHead | Initializes the head node of a doubly linked list. |
| IsListEmpty | Determines if a doubly linked list is empty. |
| RemoveEntryList | Removes a node from a doubly linked list. |
| InsertTailList | Adds a node to the end of a double linked list. |
| InsertHeadList | Adds a node to the beginning of a doubly linked list. |

String Functions

The string functions in the EFI Library perform operations on Unicode and ASCII string.  Table D-3 contains the list of string support functions.

Table D-3.	String Functions

| Name | Description |
| --- | --- |
| StrCmp | Compares two Unicode strings. |
| StrnCmp | Compares a portion of two Unicode strings. |
| StriCmp | Performs a case insensitive comparison of two Unicode strings. |
| StrCpy | Copies one Unicode string to another Unicode string. |
| StrCat | Concatenates two Unicode strings. |
| StrLen | Determines the length of a Unicode string. |
| StrSize | Determines the size of a Unicode string in bytes. |
| StrDuplicate | Creates a duplicate of a Unicode string. |
| StrLwr | Converts characters in a Unicode string to upper case characters. |
| StrUpr | Converts characters in a Unicode string to lower case characters. |
| strlena | Determines the length of an ASCII string. |
| strcmpa | Compares two ASCII strings. |
| strncmpa | Compares a portion of two ASCII strings. |
| xtoi | Converts a hexidecimal formatted Unicode string to an integer. |
| Atoi | Converts a decimal formatted Unicode string to an integer. |
| MetaMatch | Checks to see if a Unicode string matches a given pattern. |
| MetaiMatch | Performs a case insensitive comparison of a Unicode pattern string and a Unicode string. |
| ValueToString | Converts an integer to a decimal formatted Unicode string. |
| ValueToHex | Converts an integer to a hexidecimal formatted Unicode string. |
| TimeToString | Converts a data structure containing the time and date into a Unicode string. |
| GuidToString | Converts a 128 bit GUID into a Unicode string. |
| StatusToString | Converts an EFI_STATUS value into a Unicode string. |
| DevicePathToStr | Converts a device path data structure into a Unicode string. |

Memory Support Functions

The EFI Library provides a set of functions that operating on buffers in memory.  Buffers can either be allocated on the stack, as global variables, or from the memory pool Table D-4 contains the list of memory support functions.

Table D-4.	Memory Support Functions

| Name | Description |
| --- | --- |
| ZeroMem | Fills a buffer with zeros. |
| SetMem | Fills a buffer with a value.. |
| CopyMem | Copies the contents of one buffer to another buffer. |
| CompareMem | Compares the contents of two buffers. |
| AllocatePool | Allocates a buffer from pool. |
| AllocateZeroPool | Allocates a buffer from pool and fills it with zeros. |
| ReallocatePool | Adjusts the size of a previously allocated buffer. |
| FreePool | Frees a previously allocated buffer. |
| GrowBuffer | Allocates a new buffer or grows the size of a previously allocated buffer. |
| LibMemoryMap | Retrieves the system’s current memory map. |

CRC Support Functions

The EFI Library provides a set of functions that are used to compute and verify CRC32 values..  Table D-5 contains the list of CRC support functions.

Table D-5.	CRC Support Functions

| Name | Description |
| --- | --- |
| SetCrc | Computes and updates the CRC32 value for a table header. |
| SetCrcAltSize | Computes and updates the CRC32 value for a portion of a table header. |
| CheckCrc | Verifies the CRC32 value for a table header. |
| CheckCrcAltSize | Verifies the CRC32 value for a portion of a table header. |
| CalculateCrc | Computes the CRC32 value. |

Text I/O Functions

The Text I/O functions in the EFI Library provide a simple means to get input and output from a console device. Table D-6 lists the text I/O functions.

Table D-6.	Text I/O Functions

| Name | Description |
| --- | --- |
| Input | Input a Unicode string at the current cursor location using the console in and console out device. |
| IInput | Input a Unicode string at the current cursor location using the specified input and output devices. |
| Output | Send a Unicode string to the console out device at the current cursor location. |
| Print | Sends a formatted Unicode string to the console out device at the current cursor location.. |
| PrintAt | Sends a formatted Unicode string to the specified location on the console out device. |
| IPrint | Sends a formatted Unicode string to the specified output device. |
| IPrintAt | Sends a formatted Unicode string to the specified location of the specified console device. |
| Aprint | Sends a formatted Unicode string to the console out device using an ASCII format string. |
| Sprint | Sends a formatted Unicode string to the specified buffer. |
| PoolPrint | Sends a formatted Unicode string to a buffer allocated from pool. |
| CatPrint | Concatenates a formatted Unicode string to a string allocated from pool. |
| DumpHex | Prints the contents of a buffer in hexidecimal format. |
| LibIsValidTextGraphics | Determines if a character is a legal Unicode box drawing character. |
| IsValidAscii | Determines if a character is a legal ASCII character. |
| IsValidEfiCntlChar | Determines if a character is a legal EFI control character. |

Math Functions

The EFI Library provides a few math functions to operate on 64-bit operands.  These include shift operations, multiplication, and division.  Table D-7 lists the set of 64-bit math functions.

Table D-7.	Math Functions

| Name | Description |
| --- | --- |
| LshiftU64 | Shift a 64 bit integer left between 0 and 63 bits. |
| RshiftU64 | Shift a 64 bit integer right between 0 and 63 bits. |
| MultU64x32 | Multiply a 64 bit unsigned integer by a 32 bit unsigned integer and generate a 64 bit unsigned result. |
| DivU64x32 | Divide a 64 bit unsigned integer by a 32 bit unsigned integer and generate a 64 bit unsigned result with an optional 32 bit unsigned remainder. |

Spin Lock Functions

Spin locks are used to protect data structures that may be updated by more than one processor at a time, or a single processor that may update the same data structure while running a several different priority levels.  Table D-8 lists the support functions for creating and maintaining spin locks.

Table D-8.	Spin Lock Functions

| Name | Description |
| --- | --- |
| InitializeLock | Initialize a spin lock. |
| AcquireLock | Acquire a spin lock. |
| ReleaseLock | Release a spin lock. |

Handle and Protocol Support Functions

The EFI Library contains a set of functions that help drivers maintain the protocol interfaces in the boot services environment.  Table D-9 lists the set of helper functions.

Table D-9.	Handle and Protocol Support Functions

| Name | Description |
| --- | --- |
| LibLocateHandle | Finds all device handles that match the specified search criteria. |
| LibLocateHandleByDiskSignature | Finds all device handles that support the Block I/O protocol and have a disk with a matching disk signature. |
| LibLocateProtocol | Finds the first protocol instance that matches a given protocol. |
| LibInstallProtocolInterfaces | Installs one or more protocol interfaces into the boot services environment.. |
| LibUninstallProtocolInterfaces | Removes one or more protocol interfaces from the boot services environment. |
| LinReinstallProtocolInterfaces | Reinstalls one or more protocol interfaces into the boot services environment. |

File I/O Support Functions

Table D-10 lists the set of file I/O support functions.

Table D-10.	File I/O Support Functions

| Name | Description |
| --- | --- |
| LibOpenRoot | Opens and returns a file handle to a root directory of a volume. |
| LibFileInfo | Retrieves the file information on an open file handle. |
| LibFileSystemInfo | Retrieves the file system information on an open file handle. |
| LibFileSystemVolumeLabelInfo | Retrieves the volume label from an open file handle. |
| ValidMBR | Determines if a hard drive’s Master Boot Record is valid. |
| OpenSimpleReadFile | Opens a file from several possible sources and returns a file handle. |
| ReadSimpleReadFile | Read from a file opened with OpenSimpleReadFile. |
| CloseSimpleReadFile | Close a file opened with OpenSimpleReadFile. |

Device Path Support Functions

Table D-11 lists the support functions for creating and maintaining device path data structures.

Table D-11.	Device Path Support Functions

| Name | Description |
| --- | --- |
| DevicePathFromHandle | Retrieves the device path from a specified handle. |
| DevicePathInstance | Retrieves the next device path instance from a device path. |
| DevicePathInstanceCount | Returns the number of device path instances in a device path. |
| AppendDevicePath | Appends a device path to all the instances of another device path. |
| AppendDevicePathNode | Appends a device path node to all the instances of a device path. |
| AppendDevicePathInstance | Appends a device path instance to a device path. |
| AllocateAndAppendDevicePathNode | Allocates and appends a device path node to all the instances of a device path. |
| FileDevicePath | Appends a file path to a device path. |
| DevicePathSize | Returns the size of a device path in bytes. |
| DuplicateDevicePath | Creates a new copy of a device path. |
| LibDevicePathToInterface | Retrieves a protocol interface for a device. |
| UnpackDevicePath | Naturally aligns all the nodes in a device path. |
| LibMatchDevicePaths | Reports membership of a single-instance device path in a possible multi-instance device path. |
| LibDuplicateDevicePathInstance | Creates a second corresponding instance of a given device path. |

PCI Functions and Macros

Table D-12 lists some miscellaneous helper functions that are described in the following sections.

Table D-12.	Miscellaneous Functions and Macros

| Name | Description |
| --- | --- |
| PciFindDeviceClass | Finds a PCI device that matches the PCI BaseClass and SubClass. |
| PciFindDevice | Finds the first PCI device with the specified Device ID and Vendor ID. |
| InitializeGlobalIoDevice | Retrieves the DEVICE_IO protocol instance for a given device. |
| ReadPort | Reads an I/O port. |
| WritePort | Writes to an I/O port. |
| ReadPciConfig | Reads an I/O port. |
| WritePciConfig | Writes to an I/O port. |
| inp | Read an 8 bit value from an I/O port. |
| outp | Write an 8 bit value to an I/O port. |
| inpw | Read a 16 bit value from an I/O port. |
| outpw | Write a 16 bit value to an I/O port. |
| inpd | Read a 32 bit value from an I/O port. |
| outpw | Write a 32 bit value to an I/O port. |
| readpci8 | Read an 8 bit value from PCI Configuration Space. |
| writepci8 | Write an 8 bit value to PCI Configuration Space. |
| readpci16 | Read a 16 bit value from PCI Configuration Space. |
| writepci16 | Write a 16 bit value to PCI Configuration Space. |
| readpci32 | Read a 32 bit value from PCI Configuration Space. |
| writepci32 | Write a 32 bit value to PCI Configuration Space. |

Miscellaneous Functions and Macros

Table D-13 lists some miscellaneous helper functions that are described in the following sections.

Table D-13.	Miscellaneous Functions and Macros

| Name | Description |
| --- | --- |
| LibGetVariable | Retrieves and environment variables value. |
| LibGetVariableAndSIze | Retrieves and environment variables value and its size in bytes. |
| CompareGuid | Compares two 128 bit GUID. |
| CR | Returns a pointer to a elements containing record. |
| DecimaltoBCD | Converts a decimal value to a BCD value. |
| BCDtoDecimal | Converts a BCD value to a decimal value. |
| LibCreateProtocolNotifyEvent | Creates a notification event that fires every time a specific protocol instance type is created. |
| WaitForSingleEvent | Waits for an event to fire or a timeout to expire. |
| WaitForEventWithTimeout | Waits for either a SIMPLE_INPUT event or a timeout to occur. |
| RtLibEnableVirtualMappings | Converts internal library pointers to virtual runtime pointers. |
| RtConvertList | Converts pointers in a linked list to virtual runtime pointers. |
| LibGetSystemConfigurationTable | Retrieves a system configuration table from the EFI System Table. |

Sample OS Loader Listing

/*++

Copyright (c) 1998  Intel Corporation

Module Name:

osloader.c

Abstract:

Author:

Revision History

--*/

#include "efi.h"

#include "efilib.h"

static CHAR16  *OsLoaderMemoryTypeDesc[EfiMaxMemoryType]  = {

L"reserved  ",

L"LoaderCode",

L"LoaderData",

L"BS_code   ",

L"BS_data   ",

L"RT_code   ",

L"RT_data   ",

L"available ",

L"Unusable  ",

L"ACPI_recl ",

L"ACPI_NVS  ",

L"MemMapIO  ",

L"MemPortIO ",

L"PAL_code  "

};

EFI_STATUS

InitializeOSLoader (

IN EFI_HANDLE           ImageHandle,

IN EFI_SYSTEM_TABLE     *SystemTable

)

{

EFI_STATUS              Status;

UINT16                  InputString[20];

EFI_TIME                Time;

CHAR16                  *DevicePathAsString;

EFI_LOADED_IMAGE        *LoadedImage;

EFI_DEVICE_PATH         *DevicePath;

EFI_FILE_IO_INTERFACE   *Vol;

EFI_FILE_HANDLE         RootFs;

EFI_FILE_HANDLE         CurDir;

EFI_FILE_HANDLE         FileHandle;

CHAR16                  FileName[100];

UINTN                   i;

UINTN                   Size;

VOID                    *OsKernelBuffer;

UINTN                   NoHandles;

EFI_HANDLE              *HandleBuffer;

EFI_BLOCK_IO            *BlkIo;

EFI_BLOCK_IO_MEDIA      *Media;

UINT8                   *Block;

UINT32                  MediaId;

VOID                    *AcpiTable              = NULL;

VOID                    *SMBIOSTable            = NULL;

VOID                    *SalSystemTable         = NULL;

VOID                    *MpsTable               = NULL;

EFI_MEMORY_DESCRIPTOR   *MemoryMap;

EFI_MEMORY_DESCRIPTOR   *MemoryMapEntry;

UINTN                   NoEntries;

UINTN                   MapKey;

UINTN                   DescriptorSize;

UINT32                  DescriptorVersion;

UINTN                   VariableNameSize;

CHAR16                  VariableName[256];

EFI_GUID                VendorGuid;

UINT8                   *VariableValue;

//

// Initialize the Library. Set BS, RT, &ST globals

//  BS = Boot Services RT = RunTime Services

//  ST = System Table

//

InitializeLib (ImageHandle, SystemTable);

//

// Print a message to the console output device.

//

Print(L"OS Loader application started\n");

//

// Print Date and Time

//

Status = RT->GetTime(&Time,NULL);

if (!EFI_ERROR(Status)) {

Print(L"Date : %02d/%02d/%04d  Time : %02d:%02d:%02d\n",

Time.Month,Time.Day,Time.Year,Time.Hour,Time.Minute,Time.Second);

}

//

// Get the device handle and file path to the EFI OS Loader itself.

//

Status = BS->HandleProtocol (ImageHandle,

&LoadedImageProtocol,

&LoadedImage

);

if (EFI_ERROR(Status)) {

Print(L"Can not retrieve a LoadedImageProtocol handle for ImageHandle\n");

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

Status = BS->HandleProtocol (LoadedImage->DeviceHandle,

&DevicePathProtocol,

&DevicePath

);

if (EFI_ERROR(Status) || DevicePath==NULL) {

Print(L"Can not find a DevicePath handle for LoadedImage->DeviceHandle\n");

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

DevicePathAsString = DevicePathToStr(DevicePath);

if (DevicePathAsString != NULL) {

Print (L"Image device : %s\n", DevicePathAsString);

FreePool(DevicePathAsString);

}

DevicePathAsString = DevicePathToStr(LoadedImage->FilePath);

if (DevicePathAsString != NULL) {

Print (L"Image file   : %s\n", DevicePathToStr (LoadedImage->FilePath));

FreePool(DevicePathAsString);

}

Print (L"Image Base   : %X\n", LoadedImage->ImageBase);

Print (L"Image Size   : %X\n", LoadedImage->ImageSize);

//

// Open the volume for the device where the EFI OS Loader was loaded from.

//

Status = BS->HandleProtocol (LoadedImage->DeviceHandle,

&FileSystemProtocol,

&Vol

);

if (EFI_ERROR(Status)) {

Print(L"Can not get a FileSystem handle for LoadedImage->DeviceHandle\n");

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

Status = Vol->OpenVolume (Vol, &RootFs);

if (EFI_ERROR(Status)) {

Print(L"Can not open the volume for the file system\n");

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

CurDir = RootFs;

//

// Open the file OSKERNEL.BIN in the same path as the EFI OS Loader.

//

DevicePathAsString = DevicePathToStr(LoadedImage->FilePath);

if (DevicePathAsString!=NULL) {

StrCpy(FileName,DevicePathAsString);

FreePool(DevicePathAsString);

}

for(i=StrLen(FileName);i>0 && FileName[i]!='\\';i--);

FileName[i] = 0;

StrCat(FileName,L"\\OSKERNEL.BIN");

Status = CurDir->Open (CurDir,

&FileHandle,

FileName,

EFI_FILE_MODE_READ,

0

);

if (EFI_ERROR(Status)) {

Print(L"Can not open the file %s\n",FileName);

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

Print(L"Opened %s\n",FileName);

//

// Allocate a 1MB buffer for OSKERNEL.BIN

//

Size = 0x00100000;

BS->AllocatePool(EfiLoaderData,

Size,

&OsKernelBuffer

);

if (OsKernelBuffer == NULL) {

Print(L"Can not allocate a buffer for the file %s\n",FileName);

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

//

// Load OSKERNEL.BIN into the allocated memory.

//

Status = FileHandle->Read(FileHandle,

&Size,

OsKernelBuffer

);

if (EFI_ERROR(Status)) {

Print(L"Can not read the file %s\n",FileName);

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

Print(L"%X bytes of OSKERNEL.BIN read into memory at %X\n",Size,OsKernelBuffer);

//

// Close OSKERNEL.BIN

//

Status = FileHandle->Close(FileHandle);

if (EFI_ERROR(Status)) {

Print(L"Can not close the file %s\n",FileName);

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

//

// Free the resources allocated from pool.

//

FreePool(OsKernelBuffer);

Print(L"\nPress [ENTER] to continue...\n");

Input(NULL,InputString,20);

//

// Get a list of all the BLOCK_IO devices

//

NoHandles = 0;

HandleBuffer = NULL;

Status = LibLocateHandle(ByProtocol,

&BlockIoProtocol,

NULL,

&NoHandles,

&HandleBuffer

);

if (EFI_ERROR(Status)) {

Print(L"Can not get the array of BLOCK_IO handles\n");

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

//

// Read the first block from each BLOCK_IO device and display it

//

for(i=0;i<NoHandles;i++) {

//

// Get the DEVICE_PATH Protocol Interface to the device

//

Status = BS->HandleProtocol (HandleBuffer[i],

&DevicePathProtocol,

&DevicePath

);

if (EFI_ERROR(Status) || DevicePath==NULL) {

Print(L"Can not get a DevicePath handle for HandleBuffer[%d]\n",i);

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

//

// Get the BLOCK_IO Protocol Interface to the device

//

Status = BS->HandleProtocol (HandleBuffer[i],

&BlockIoProtocol,

&BlkIo

);

if (EFI_ERROR(Status) || BlkIo==NULL) {

Print(L"Handle does not support the BLOCK_IO protocol\n");

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

//

// Allocate a buffer for the first block on the device.

//

Media = BlkIo->Media;

Block = AllocatePool (Media->BlockSize);

if (Block == NULL) {

Print(L"Can not allocate buffer for a block\n");

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

//

// Read block #0 from the device.

//

MediaId = Media->MediaId;

Status = BlkIo->ReadBlocks(BlkIo,

MediaId,

(EFI_LBA)0,

Media->BlockSize,

Block);

//

// Display block#0 from the device.

//

DevicePathAsString = DevicePathToStr(DevicePath);

if (DevicePathAsString != NULL) {

Print(L"\nBlock #0 of device %s\n",DevicePathAsString);

FreePool(DevicePathAsString);

}

DumpHex(0,0,Media->BlockSize,Block);

//

// Free the resources allocated from pool.

//

FreePool(Block);

Print(L"\nPress [ENTER] to continue...\n");

Input(NULL,InputString,20);

}

//

// Free the resources allocated from pool.

//

FreePool(HandleBuffer);

//

// Get System Configuration

//

Print(L"System Configuration Tables:\n\n");

Status = LibGetSystemConfigurationTable(&AcpiTableGuid,&AcpiTable);

if (!EFI_ERROR(Status)) {

Print(L"  ACPI Table is at address                   : %X\n",AcpiTable);

}

Status = LibGetSystemConfigurationTable(&SMBIOSTableGuid,&SMBIOSTable);

if (!EFI_ERROR(Status)) {

Print(L"  SMBIOS Table is at address                 : %X\n",SMBIOSTable);

}

Status = LibGetSystemConfigurationTable(&SalSystemTableGuid,&SalSystemTable);

if (!EFI_ERROR(Status)) {

Print(L"  Sal System Table is at address             : %X\n",SalSystemTable);

}

Status = LibGetSystemConfigurationTable(&MpsTableGuid,&MpsTable);

if (!EFI_ERROR(Status)) {

Print(L"  MPS Table is at address                    : %X\n",MpsTable);

}

Print(L"\nPress [ENTER] to continue...\n");

Input(NULL,InputString,20);

//

// Display the current Memory Map

//

MemoryMap = LibMemoryMap(&NoEntries,&MapKey,&DescriptorSize,&DescriptorVersion);

if (MemoryMap == NULL) {

Print(L"Can not retrieve the current memory map\n");

BS->Exit(ImageHandle,EFI_SUCCESS,0,NULL);

}

Print(L"Memory Descriptor List:\n\n");

Print(L"  Type        Start Address     End Address       Attributes      \n");

Print(L"  ==========  ================  ================  ================\n");

MemoryMapEntry = MemoryMap;

for(i=0;i<NoEntries;i++) {

Print(L"  %s  %lX  %lX  %lX\n",

OsLoaderMemoryTypeDesc[MemoryMapEntry->Type],

MemoryMapEntry->PhysicalStart,

MemoryMapEntry->PhysicalStart +

LShiftU64(MemoryMapEntry->NumberOfPages,PAGE_SHIFT)-1,

MemoryMapEntry->Attribute);

MemoryMapEntry = NextMemoryDescriptor(MemoryMapEntry, DescriptorSize);

}

//

// Free the resources allocated from pool.

//

FreePool(MemoryMap);

Print(L"\nPress [ENTER] to continue...\n");

Input(NULL,InputString,20);

//

// Display all the Environment Variables

//

Print(L"Environment Variable List:\n\n");

VariableName[0] = 0x0000;

VendorGuid = NullGuid;

Print(L"GUID                                Variable Name        Value\n");

Print(L"=================================== ==================== ========\n");

do {

VariableNameSize = 256;

Status = RT->GetNextVariableName(&VariableNameSize,

VariableName,

&VendorGuid

);

if (Status == EFI_SUCCESS) {

VariableValue = LibGetVariable(VariableName,&VendorGuid);

if (VariableValue != NULL) {

Print(L"%.-35g %.-20s %X\n",&VendorGuid,VariableName,VariableValue);

FreePool(VariableValue);

}

}

} while (Status == EFI_SUCCESS);

Print(L"\nPress [ENTER] to continue...\n");

Input(NULL,InputString,20);

//

// Get the most current memory map.

//

MemoryMap = LibMemoryMap(&NoEntries,&MapKey,&DescriptorSize,&DescriptorVersion);

//

// Transition from Boot Services to Run Time Services.

//

Print(L"Call ExitBootServices()\n");

//    BS->ExitBootServices(ImageHandle,MapKey);

Print(L"\nPress [ENTER] to continue...\n");

Input(NULL,InputString,20);

return EFI_SUCCESS;

}

Sample OS Loader Output

OS Loader application started

Date : 07/14/1999  Time : 14:15:45

Image device : Acpi(PNP0A03,0)/Pci(0|0)/Acpi(PNP0604,0)

Image file   : \osloader.efi

Image Base   : 07E68000

Image Size   : 00008FFF

Opened \OSKERNEL.BIN

00009000 bytes of OSKERNEL.BIN read into memory at 07D67008

Press [ENTER] to continue...

Block #0 of device

00000000: EB 3C 90 49 4E 54 45 4C-20 20 20 00 02 01 01 00  *.<.INTEL   .....*

00000010: 02 E0 00 40 0B F0 09 00-12 00 02 00 00 00 00 00  *...@............*

00000020: 00 00 00 00 00 01 29 20-20 20 20 45 46 49 20 46  *......)    EFI F*

00000030: 4C 4F 50 50 59 20 46 41-54 31 32 20 20 20 8C C8  *LOPPY FAT12   ..*

00000040: 8E D0 05 00 10 8E D8 BC-00 7C 8B EC B4 08 B2 00  *................*

00000050: CD 13 33 C0 8A C6 24 3F-FE C0 50 8A C1 24 3F 50  *..3...$?..P..$?P*

00000060: 81 BE FE 01 55 AA 0F 85-6F 01 80 BE 00 00 EB 0F  *....U...o.......*

00000070: 85 66 01 81 BE 0B 00 00-02 0F 85 5C 01 80 BE 0D  *.f.........\....*

00000080: 00 00 0F 84 53 01 83 BE-11 00 00 0F 84 4A 01 8B  *....S........J..*

00000090: 86 0E 00 3B 86 13 00 0F-8F 3E 01 33 C9 8D 36 03  *...;.....>.3..6.*

000000A0: 00 B1 08 E8 25 01 8D 36-2B 00 B1 0B E8 1C 01 81  *....%..6+.......*

000000B0: BE 36 00 46 41 0F 85 20-01 81 BE 38 00 54 31 0F  *.6.FA.. ...8.T1.*

000000C0: 85 16 01 B8 20 20 39 86-3B 00 0F 85 0B 01 39 86  *....  9.;.....9.*

000000D0: 3C 00 0F 85 03 01 80 BE-3A 00 32 74 0C 80 BE 3A  *<.......:.2t...:*

000000E0: 00 36 0F 84 F3 00 E9 F0-00 8B 8E 11 00 C1 E1 05  *.6..............*

000000F0: 8B D9 81 E3 FF 01 0F 85-DF 00 8B D9 C1 EB 09 BF  *................*

00000100: 00 00 8A 86 10 00 32 E4-F7 A6 16 00 03 86 0E 00  *......2.........*

00000110: 1E 07 E8 6D 00 03 C3 89-46 00 81 3D 45 46 75 27  *...m....F..=EFu'*

00000120: 81 7D 02 49 4C 75 20 81-7D 04 44 52 75 19 B8 20  *...ILu ...DRu.. *

00000130: 20 39 45 06 75 11 39 45-08 75 0C 39 45 09 75 07  * 9E.u.9E.u.9E.u.*

00000140: 8A 45 0B 24 58 74 0B 83-C7 20 83 E9 20 75 CB E9  *.E.$Xt... .. u..*

00000150: 87 00 8B 4D 1A 8C C8 05-00 20 8E C0 33 FF 8B C1  *...M..... ..3...*

00000160: 83 E8 02 32 FF 8A 9E 0D-00 F7 E3 03 46 00 32 FF  *...2........F.2.*

00000170: 8A 9E 0D 00 06 E8 0A 00-58 89 86 80 01 EA 00 00  *........X.......*

00000180: 00 20 60 8B F0 8B CB BD-FC 7B 8B C6 33 D2 F7 76  *. `.........3..v*

00000190: 00 42 8B 5E 00 2B DA 43-3B CB 7F 02 8B D9 51 8A  *.B.^.+.C;.....Q.*

000001A0: CA 33 D2 F7 76 02 53 8A-F2 B2 00 8A E8 8A C3 B4  *.3..v.S.........*

000001B0: 02 8B DF CD 13 5B 59 03-F3 2B CB 8C C0 C1 E3 05  *.....[Y..+......*

000001C0: 03 C3 8E C0 83 F9 00 75-BE 61 C3 80 3A 7F 7F 09  *.......u.a..:...*

000001D0: 80 3A 20 7C 04 46 E2 F3-C3 CC EB FD 00 00 00 00  *.: ..F..........*

000001E0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

000001F0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 55 AA  *..............U.*

Press [ENTER] to continue...

Block #0 of device

00000000: 33 C0 8E D0 BC 00 7C FB-50 07 50 1F FC BE 1B 7C  *3.......P.P.....*

00000010: BF 1B 06 50 57 B9 E5 01-F3 A4 CB BE BE 07 B1 04  *...PW...........*

00000020: 38 2C 7C 09 75 15 83 C6-10 E2 F5 CD 18 8B 14 8B  *8,..u...........*

00000030: EE 83 C6 10 49 74 16 38-2C 74 F6 BE 10 07 4E AC  *....It.8,t....N.*

00000040: 3C 00 74 FA BB 07 00 B4-0E CD 10 EB F2 89 46 25  *<.t...........F%*

00000050: 96 8A 46 04 B4 06 3C 0E-74 11 B4 0B 3C 0C 74 05  *..F...<.t...<.t.*

00000060: 3A C4 75 2B 40 C6 46 25-06 75 24 BB AA 55 50 B4  *:.u+@.F%.u$..UP.*

00000070: 41 CD 13 58 72 16 81 FB-55 AA 75 10 F6 C1 01 74  *A..Xr...U.u....t*

00000080: 0B 8A E0 88 56 24 C7 06-A1 06 EB 1E 88 66 04 BF  *....V$.......f..*

00000090: 0A 00 B8 01 02 8B DC 33-C9 83 FF 05 7F 03 8B 4E  *.......3.......N*

000000A0: 25 03 4E 02 CD 13 72 29-BE 75 07 81 3E FE 7D 55  *%.N...r).u..>..U*

000000B0: AA 74 5A 83 EF 05 7F DA-85 F6 75 83 BE 3F 07 EB  *.tZ.......u..?..*

000000C0: 8A 98 91 52 99 03 46 08-13 56 0A E8 12 00 5A EB  *...R..F..V....Z.*

000000D0: D5 4F 74 E4 33 C0 CD 13-EB B8 00 00 80 01 44 16  *.Ot.3.........D.*

000000E0: 56 33 F6 56 56 52 50 06-53 51 BE 10 00 56 8B F4  *V3.VVRP.SQ...V..*

000000F0: 50 52 B8 00 42 8A 56 24-CD 13 5A 58 8D 64 10 72  *PR..B.V$..ZX.d.r*

00000100: 0A 40 75 01 42 80 C7 02-E2 F7 F8 5E C3 EB 74 49  *.@u.B......^..tI*

00000110: 6E 76 61 6C 69 64 20 70-61 72 74 69 74 69 6F 6E  *nvalid partition*

00000120: 20 74 61 62 6C 65 2E 20-53 65 74 75 70 20 63 61  * table. Setup ca*

00000130: 6E 6E 6F 74 20 63 6F 6E-74 69 6E 75 65 2E 00 45  *nnot continue..E*

00000140: 72 72 6F 72 20 6C 6F 61-64 69 6E 67 20 6F 70 65  *rror loading ope*

00000150: 72 61 74 69 6E 67 20 73-79 73 74 65 6D 2E 20 53  *rating system. S*

00000160: 65 74 75 70 20 63 61 6E-6E 6F 74 20 63 6F 6E 74  *etup cannot cont*

00000170: 69 6E 75 65 2E 00 00 00-00 00 00 00 00 00 00 00  *inue............*

00000180: 00 00 00 8B FC 1E 57 8B-F5 CB 00 00 00 00 00 00  *......W.........*

00000190: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

000001A0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

000001B0: 00 00 00 00 00 00 00 00-A3 F4 00 00 00 00 80 01  *................*

000001C0: 01 00 0B 7F 7F EF 3F 00-00 00 C1 07 3D 00 00 00  *......?.....=...*

000001D0: 41 F0 05 7F FF DF 00 08-3D 00 00 08 3D 00 00 00  *A.......=...=...*

000001E0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

000001F0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 55 AA  *..............U.*

Press [ENTER] to continue...

Block #0 of device

00000000: EB 58 90 4D 53 57 49 4E-34 2E 31 00 02 08 20 00  *.X.MSWIN4.1... .*

00000010: 02 00 00 00 00 F8 00 00-3F 00 80 00 3F 00 00 00  *........?...?...*

00000020: C1 07 3D 00 3F 0F 00 00-00 00 00 00 02 00 00 00  *..=.?...........*

00000030: 01 00 06 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

00000040: 80 00 29 EB 17 22 1D 4E-4F 20 4E 41 4D 45 20 20  *..)..".NO NAME  *

00000050: 20 20 46 41 54 33 32 20-20 20 33 C9 8E D1 BC F4  *  FAT32   3.....*

00000060: 7B 8E C1 8E D9 BD 00 7C-88 4E 02 8A 56 40 B4 08  *.........N..V@..*

00000070: CD 13 73 05 B9 FF FF 8A-F1 66 0F B6 C6 40 66 0F  *..s......f...@f.*

00000080: B6 D1 80 E2 3F F7 E2 86-CD C0 ED 06 41 66 0F B7  *....?.......Af..*

00000090: C9 66 F7 E1 66 89 46 F8-83 7E 16 00 75 38 83 7E  *.f..f.F.....u8..*

000000A0: 2A 00 77 32 66 8B 46 1C-66 83 C0 0C BB 00 80 B9  **.w2f.F.f.......*

000000B0: 01 00 E8 2B 00 E9 48 03-A0 FA 7D B4 7D 8B F0 AC  *...+..H.........*

000000C0: 84 C0 74 17 3C FF 74 09-B4 0E BB 07 00 CD 10 EB  *..t.<.t.........*

000000D0: EE A0 FB 7D EB E5 A0 F9-7D EB E0 98 CD 16 CD 19  *................*

000000E0: 66 60 66 3B 46 F8 0F 82-4A 00 66 6A 00 66 50 06  *f`f;F...J.fj.fP.*

000000F0: 53 66 68 10 00 01 00 80-7E 02 00 0F 85 20 00 B4  *Sfh.......... ..*

00000100: 41 BB AA 55 8A 56 40 CD-13 0F 82 1C 00 81 FB 55  *A..U.V@........U*

00000110: AA 0F 85 14 00 F6 C1 01-0F 84 0D 00 FE 46 02 B4  *.............F..*

00000120: 42 8A 56 40 8B F4 CD 13-B0 F9 66 58 66 58 66 58  *B.V@......fXfXfX*

00000130: 66 58 EB 2A 66 33 D2 66-0F B7 4E 18 66 F7 F1 FE  *fX.*f3.f..N.f...*

00000140: C2 8A CA 66 8B D0 66 C1-EA 10 F7 76 1A 86 D6 8A  *...f..f....v....*

00000150: 56 40 8A E8 C0 E4 06 0A-CC B8 01 02 CD 13 66 61  *V@............fa*

00000160: 0F 82 54 FF 81 C3 00 02-66 40 49 0F 85 71 FF C3  *..T.....f@I..q..*

00000170: 4E 54 4C 44 52 20 20 20-20 20 20 0D 0A 4E 54 4C  *NTLDR      ..NTL*

00000180: 44 52 20 69 73 20 6D 69-73 73 69 6E 67 FF 0D 0A  *DR is missing...*

00000190: 44 69 73 6B 20 65 72 72-6F 72 FF 0D 0A 50 72 65  *Disk error...Pre*

000001A0: 73 73 20 61 6E 79 20 6B-65 79 20 74 6F 20 72 65  *ss any key to re*

000001B0: 73 74 61 72 74 0D 0A 00-00 00 00 00 00 00 00 00  *start...........*

000001C0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

000001D0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

000001E0: 00 00 00 00 00 00 00 00-00 00 00 00 00 00 00 00  *................*

000001F0: 00 00 00 00 00 00 00 00-00 7B 8E 9B 00 00 55 AA  *..............U.*

Press [ENTER] to continue...

Block #0 of device

00000000: EB 3C 90 4D 53 57 49 4E-34 2E 31 00 02 04 01 00  *.<.MSWIN4.1.....*

00000010: 02 00 02 00 00 F8 67 00-3F 00 80 00 3F 00 00 00  *......g.?...?...*

00000020: 41 99 01 00 80 00 29 E3-18 61 2D 4E 4F 20 4E 41  *A.....)..a-NO NA*

00000030: 4D 45 20 20 20 20 46 41-54 31 36 20 20 20 33 C9  *ME    FAT16   3.*

00000040: 8E D1 BC FC 7B 16 07 BD-78 00 C5 76 00 1E 56 16  *........x..v..V.*

00000050: 55 BF 22 05 89 7E 00 89-4E 02 B1 0B FC F3 A4 06  *U.".....N.......*

00000060: 1F BD 00 7C C6 45 FE 0F-38 4E 24 7D 20 8B C1 99  *.....E..8N$. ...*

00000070: E8 7E 01 83 EB 3A 66 A1-1C 7C 66 3B 07 8A 57 FC  *.....:f...f;..W.*

00000080: 75 06 80 CA 02 88 56 02-80 C3 10 73 ED 33 C9 FE  *u.....V....s.3..*

00000090: 06 D8 7D 8A 46 10 98 F7-66 16 03 46 1C 13 56 1E  *....F...f..F..V.*

000000A0: 03 46 0E 13 D1 8B 76 11-60 89 46 FC 89 56 FE B8  *.F....v.`.F..V..*

000000B0: 20 00 F7 E6 8B 5E 0B 03-C3 48 F7 F3 01 46 FC 11  * ....^...H...F..*

000000C0: 4E FE 61 BF 00 07 E8 28-01 72 3E 38 2D 74 17 60  *N.a....(.r>8-t.`*

000000D0: B1 0B BE D8 7D F3 A6 61-74 3D 4E 74 09 83 C7 20  *.......at=Nt... *

000000E0: 3B FB 72 E7 EB DD FE 0E-D8 7D 7B A7 BE 7F 7D AC  *;.r.............*

000000F0: 98 03 F0 AC 98 40 74 0C-48 74 13 B4 0E BB 07 00  *.....@t.Ht......*

00000100: CD 10 EB EF BE 82 7D EB-E6 BE 80 7D EB E1 CD 16  *................*

00000110: 5E 1F 66 8F 04 CD 19 BE-81 7D 8B 7D 1A 8D 45 FE  *^.f...........E.*

00000120: 8A 4E 0D F7 E1 03 46 FC-13 56 FE B1 04 E8 C2 00  *.N....F..V......*

00000130: 72 D7 EA 00 02 70 00 52-50 06 53 6A 01 6A 10 91  *r....p.RP.Sj.j..*

00000140: 8B 46 18 A2 26 05 96 92-33 D2 F7 F6 91 F7 F6 42  *.F..&...3......B*

00000150: 87 CA F7 76 1A 8A F2 8A-E8 C0 CC 02 0A CC B8 01  *...v............*

00000160: 02 80 7E 02 0E 75 04 B4-42 8B F4 8A 56 24 CD 13  *.....u..B...V$..*

00000170: 61 61 72 0A 40 75 01 42-03 5E 0B 49 75 77 C3 03  *aar.@u.B.^.Iuw..*

00000180: 18 01 27 0D 0A 49 6E 76-61 6C 69 64 20 73 79 73  *..'..Invalid sys*

00000190: 74 65 6D 20 64 69 73 6B-FF 0D 0A 44 69 73 6B 20  *tem disk...Disk *

000001A0: 49 2F 4F 20 65 72 72 6F-72 FF 0D 0A 52 65 70 6C  *I/O error...Repl*

000001B0: 61 63 65 20 74 68 65 20-64 69 73 6B 2C 20 61 6E  *ace the disk, an*

000001C0: 64 20 74 68 65 6E 20 70-72 65 73 73 20 61 6E 79  *d then press any*

000001D0: 20 6B 65 79 0D 0A 00 00-49 4F 20 20 20 20 20 20  * key....IO      *

000001E0: 53 59 53 4D 53 44 4F 53-20 20 20 53 59 53 7F 01  *SYSMSDOS   SYS..*

000001F0: 00 41 BB 00 07 60 66 6A-00 E9 3B FF 00 00 55 AA  *.A...`fj..;...U.*

Press [ENTER] to continue...

System Configuration Tables:

ACPI Table is at address                   : 00000000

SMBIOS Table is at address                 : 00000000

MPS Table is at address                    : 00000000

Press [ENTER] to continue...

Memory Descriptor List:

Type        Start Address     End Address       Attributes

==========  ================  ================  ================

BS_data     0000000000000000  0000000000000FFF  0000000000000008

available   0000000000001000  000000000001FFFF  0000000000000008

BS_data     0000000000020000  0000000000021FFF  0000000000000008

available   0000000000022000  0000000000089FFF  0000000000000008

BS_data     000000000008A000  000000000009AFFF  0000000000000008

BS_code     000000000009B000  000000000009EFFF  0000000000000008

BS_data     000000000009F000  000000000009FFFF  0000000000000008

BS_data     00000000000F0000  00000000000FFFFF  0000000000000008

available   0000000000100000  00000000001DFFFF  0000000000000008

BS_data     00000000001E0000  00000000001FFFFF  0000000000000008

available   0000000000200000  0000000000200FFF  0000000000000008

BS_code     0000000000201000  0000000000215FFF  0000000000000008

RT_code     0000000000216000  0000000000218FFF  8000000000000008

BS_data     0000000000219000  000000000021BFFF  0000000000000008

RT_data     000000000021C000  000000000021CFFF  8000000000000008

BS_data     000000000021D000  000000000021DFFF  0000000000000008

available   000000000021E000  0000000007E67FFF  0000000000000008

LoaderData  0000000007E68000  0000000007E68FFF  0000000000000008

LoaderCode  0000000007E69000  0000000007E6CFFF  0000000000000008

LoaderData  0000000007E6D000  0000000007E74FFF  0000000000000008

available   0000000007E75000  0000000007E7AFFF  0000000000000008

LoaderData  0000000007E7B000  0000000007E7BFFF  0000000000000008

BS_data     0000000007E7C000  0000000007E85FFF  0000000000000008

RT_data     0000000007E86000  0000000007E86FFF  8000000000000008

BS_data     0000000007E87000  0000000007E87FFF  0000000000000008

BS_code     0000000007E88000  0000000007E93FFF  0000000000000008

BS_data     0000000007E94000  0000000007E99FFF  0000000000000008

LoaderData  0000000007E9A000  0000000007E9BFFF  0000000000000008

BS_data     0000000007E9C000  0000000007E9CFFF  0000000000000008

LoaderData  0000000007E9D000  0000000007E9DFFF  0000000000000008

LoaderCode  0000000007E9E000  0000000007EA1FFF  0000000000000008

LoaderData  0000000007EA2000  0000000007EA4FFF  0000000000000008

BS_data     0000000007EA5000  0000000007FC6FFF  0000000000000008

RT_data     0000000007FC7000  0000000007FC8FFF  8000000000000008

BS_data     0000000007FC9000  0000000007FCEFFF  0000000000000008

RT_data     0000000007FCF000  0000000007FCFFFF  8000000000000008

BS_data     0000000007FD0000  0000000007FFFFFF  0000000000000008

BS_data     00000000FFFE0000  00000000FFFFFFFF  0000000000000008

Press [ENTER] to continue...

Environment Variable List:

GUID                                Variable Name        Value

=================================== ==================== ========

Efi                                 Lang                 07E9AF08

Efi                                 Timeout              07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 DevIo                07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 fs                   07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 diskio               07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 blkio                07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 txtin                07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 txtout               07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 load                 07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 image                07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 varstore             07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 dpath                07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 unicode              07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 pxe                  07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 ShellInt             07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 SEnv                 07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 ShellProtId          07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 ShellDevPathMap      07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 ShellAlias           07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 G0                   07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 Efi                  07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 GenFileInfo          07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 FileSysInfo          07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 PcAnsi               07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 Unknown Device       07E9AF08

47C7B227-C42A-11D2-8E57-00A0C969723 dir                  07E9AF08

47C7B227-C42A-11D2-8E57-00A0C969723 md                   07E9AF08

47C7B227-C42A-11D2-8E57-00A0C969723 rd                   07E9AF08

47C7B227-C42A-11D2-8E57-00A0C969723 del                  07E9AF08

47C7B227-C42A-11D2-8E57-00A0C969723 copy                 07E9AF08

47C7B226-C42A-11D2-8E57-00A0C969723 LegacyBoot           07E9AF08

47C7B225-C42A-11D2-8E57-00A0C969723 fs0                  07E9AF08

47C7B225-C42A-11D2-8E57-00A0C969723 fs1                  07E9AF08

47C7B225-C42A-11D2-8E57-00A0C969723 fs2                  07E7BF08

47C7B225-C42A-11D2-8E57-00A0C969723 fs3                  07E7BF08

47C7B225-C42A-11D2-8E57-00A0C969723 blk0                 07E9AF08

47C7B225-C42A-11D2-8E57-00A0C969723 blk1                 07E9AF08

47C7B225-C42A-11D2-8E57-00A0C969723 blk2                 07E9AF08

47C7B225-C42A-11D2-8E57-00A0C969723 blk3                 07E9AF08

47C7B225-C42A-11D2-8E57-00A0C969723 blk4                 07E7BF08

47C7B225-C42A-11D2-8E57-00A0C969723 blk5                 07E7BF08

47C7B225-C42A-11D2-8E57-00A0C969723 blk6                 07E7BF08

47C7B225-C42A-11D2-8E57-00A0C969723 blk7                 07E9AF08

47C7B225-C42A-11D2-8E57-00A0C969723 blk8                 07E9AF08

47C7B224-C42A-11D2-8E57-00A0C969723 path                 07E7BF08

Efi                                 LangCodes            07E9AF08

Press [ENTER] to continue...

Call ExitBootServices()

Press [ENTER] to continue...