Chicago File System Features - Tips & Issues

Attention:  Requires Chicago NDA

Revision:	0.98

Date:		April 22, 1994

Author:		Russ Arun

1.

Table of Contents

1. Overview

2. File System Details

3. End User Issues

3.1. Auto-generation of 8.3 names

3.2. Searches

3.3. Down Level Systems

3.4. Disk Utilities & Exclusive Volume Lock

3.5. Long File Name Format

3.6. Long File Names in the Root

4. ISV Issues

4.1. Limits in the Name

4.2. Auto-generation scheme

4.3. 32-bit Apps on Windows

4.4. 16-bit Apps on Chicago

4.5. 16-bit Apps & Down Level Systems

4.6. Character sets: APIs & on-disk names

4.6.1. 16 bit file APIs

4.6.2. 32 bit file APIs

4.6.3. On-Disk names

4.7. CreateProcess, WinExec & $exec functions and LFNs

4.8. Canonical API

4.9. Exclusive Volume API (specific to Chicago)

4.10. Keying off file names

4.11. Checking Directory Entries

4.12. Win32 & New INT 21 FindFirst/Next and FindClose

4.13. Time APIs

4.14. TSR and Apps that monitor INT 21 calls (INT 21 hookers)

4.15. File System "Compatibility" switch

4.16. "for" command in COMMAND.COM

4.17. Down level system idiosyncrasies

4.18. Long command lines

1.

1.	Overview

The FAT file system was the original file system that was part of MS-DOS.  This file system has hardly been modified since MS-DOS 2.0, but for the introduction of 16 bit FAT in MS-DOS 3.0.  Hence the enhancement of the FAT file system to support long file names will be the first major extension of this file system in quite a while.  Long file names are being introduced in the FAT file system in a backward compatible manner in the next version of Windows.

Any physical file on this extended FAT file system will logically be associated with two names: namely the (primary) file name and its (alternate name or) alias.  The alias will be in the standard MS-DOS 8.3 name format.  The alias will be generated automatically, if necessary.  Valid characters, as defined by MS-DOS for the 8.3 names, have been any combination of letters, digits or characters with ASCII codes greater than 127, blank (ASCII 20H), plus any of the following special characters:

$ % ' - _ @   ~ ` ! ( ) { } ^ # &

This is the same set of characters that is valid for the alias too.  The (long) file name can be up to 255 characters long.  Also the following additional characters, which are invalid in the alias (8.3 name), are valid in the (long) file name:

+ , ; = [ ]

2.	File System Details

In Chicago, the Long File name FAT, will be supported only when running Windows.  The regular MS-DOS real mode FAT file system (and not the Long File name FAT file system) will be the one that is supported in Single MS-DOS application mode (real mode).  This means that long names that are created in a Windows environment will not be visible when the user exits to Single MS-DOS application mode, though the names themselves are physically present on the media.  Only the alias (8.3 name) will be visible.  The same applies to any down level FAT file system, when a floppy media with long file names is transported to them.  On systems like MS-DOS 6.0, Win 3.1, Windows NT 3.1 and OS/2 2.11 only the alias (8.3 name) will be visible on the floppy, even if it contains long file names created on Chicago.

Chicago will be able to see the long file names on Windows NT’s NTFS, OS/2’s HPFS or Novell Netware’s file system, if there are long file names on the server.

As mentioned before, when a file is created, it logically has both a file name and an alias.  If the file name is 8.3 compliant then the file name and the alias are the same.  For the file name to be 8.3 compliant it has to use only the characters that are valid for an alias and it has to be all upper case.  This implies that a name that uses only characters that are valid for an alias and is 8.3 compliant as far as its format goes, is still not the same as the alias, if it contains lower case characters.  However in this case, the alias will just be the upper case version of the file name.  For example, if the file name of a file is Examples.Txt, then its corresponding alias will be EXAMPLES.TXT.  The case of the name is preserved in the file name.  Note that searches in the file system are case insensitive, so a search of the form examples.txt will find this file.

If the file name is not compliant with an 8.3 name either in format or in the characters it uses, then an alias will be auto-generated.   The user or an application cannot control the name created by the auto-generation process.  For example, a (long) file name of the form ThisIsALongFileName will be associated with an auto-generated alias of the form THISISAL.  In the case of alias (8.3) name collisions, this alias could easily be of the form THISIS~1 or THISI~19.

The requests to extend the FAT file system to support long file names have poured in over time.  It is a difficult balancing act extending a widely used file system, such as the FAT file system, in a backward compatible manner.  Further the long file name scheme that is being introduced is compatible with the Win32 file naming scheme.  The accrued benefits due to the existence of long file names should be obvious.  Its popularity and acceptance will be determined by how fast and how well applications support this feature, and how many of such applications find their way on to the user's machine.  A user who chooses to use the older 8.3 names, will not see much of a difference in the system, due to the long file names.    To be sure there are some issues and subtleties introduced by this feature and they are discussed below.

The rest of this paper dwells on issues that end users will see while using the long file name extensions in the FAT file system, and on tips for ISVs who develop applications and utilities.

3.	End User Issues

3.1.	Auto-generation of 8.3 names

The auto-generation of the alias has some side effects. Since the system auto-generates the alias name on every create, the following idiosyncrasies will be observed by users.

Operations on a long file name, can potentially change the alias name.  In particular operations such as copy, edit, backup & restore might change the 8.3 name associated with the file.  For example, if a file with the name LongFileName is associated with an alias LONGFI~2, and this file is copied to a different directory using:

copy LongFileName  \TMP\LongFileName

then the alias associated with this file can become LONGFILE, if such an alias (8.3 name) is not present in the target directory.  The (long) file name is of course preserved in this case.

Operations on the alias (the 8.3 name) will destroy the long file name.  In particular operations such as copy, with older versions of utilities that have not been updated to support long file names, can destroy the long file name associated with the file that is operated upon.  For example, if a file with a file name LongFileName.Txt is associated with an alias LONGFI~1.TXT, and this file is copied to a different directory using an older version of copy that is not aware of long file names then:

oldcopy LONGFI~1.TXT \TMP\LONGFI~1.TXT

will cause the destination file in the target directory to be associated only with the file name and alias of LONGFI~1.TXT.  In other words the destination file will not have the file name LongFileName.Txt.   Of course Chicago's COMMAND.COM has been updated to support long file names as part of all of its commands, including COPY.

A similar problem can occur on older versions of backup and restore.  If one backs up the entire system, using an old version of a backup utility that does not support long file names, and then restores the entire system at some point later, then all the long file names in the system will be lost.  Note that the alias (which will also be the newer file name) and the data of the file will be preserved.

A utility called LFNBK has been posted on Compuserve.  The user can preserve the (long) file names in this case by doing the following:

·	Preserve the (long) file name to (8.3) alias name association, by running LFNBK /b <drive letter>, where <drive letter> is the drive the user plans to backup

·	Backup this drive (specified as the drive letter in the previous line) using an old backup program that will not be aware of long file names.

·	Restore the backed up files to a drive, when necessary at some point later, using the old restore program that will not be aware of long file names

·	Restore the long file names on this drive, by running LFNBK /r <drive letter>, where drive letter is the drive where the files were restored to.

Note that the (8.3) alias name might be different from what was backed up in some cases, but the (long) file name will match what was backed up.

Chicago will provide a feature, called tunneling, to preserve the (long) file names when using older editors.  These older editors will only operate on the (alias) 8.3 name because they are not aware of (long) file names.  Tunneling will be turned on by default in Chicago, but the user can choose to turn it off.  Tunneling aims to preserve the (long) file name on editors that use the following scheme:

·	Normal file open and editing “creates” a temporary file

·	A “save and/or close” operation, saves the temporary file, deletes or renames the original file, renames the temporary file just edited to be the original file

Most editors use the above scheme.

A user who chooses to use only 8.3 compliant names (ignoring case) or sets the file system in Win 3.1 compatible mode will not see these idiosyncrasies.

*	LFNBK productizing decisions have not been made yet.

3.2.	Searches

Searches of file names apply to both the file name and its alias.  The system presents a single unified name space.  This is done so that the single physical view of the file is preserved.  However if the result of the search shows only the file name, it could be confusing to the user.  Consider a set of files in a directory, where the file names and aliases are as follows:

LongFileName			LONGFI~1

MyFile				MYFILE

Problems.Txt			PROBLEMS.TXT

AnotherFile			ANOTHERF

File-1				FILE-1

A search of the form DIR *1 will display:

LONGFI~1		123	08-11-93	15:26	LongFileName

FILE-1			352	08-11-93	16:01	File-1

Note that DIR displays the alias first for compatibility with the older DIR format.  However another utility, that is aware of long file names and displays only the file name, will display both the files LongFileName and File-1.  This could be confusing at first glance because the file LongFileName does not have the number 1 as part of the name (which was specified in the search criteria).  The file was matched by the search pattern because its alias contains the number 1.

The wildcard searches have been made more flexible in Chicago (if the file system is not in Win 3.1 compatible mode - see below for a definition of this file system mode).  Note that in the above search *1 was a valid specification.  It is acceptable to search for all files contain the words mid somewhere in the file name with a specification such as *mid*.  In the old search semantics, the first * encountered ignored all other character specifications.

3.3.	Down Level Systems

Down Level Systems are systems that support the old MS-DOS FAT file system.  Examples of such systems include MS-DOS 6.0, Windows 3.1, OS/2 2.11, Windows NT 1.0, etc.  These systems are not aware of the long file name extensions to the FAT file system.  If you were to take a floppy containing files that sport a long file name to the down level system, only the alias (8.3 name) will be visible on the down level system.  You can view the file using the alias name on the down level system.  If you take  the floppy back to the newer Windows release or to the newer Windows NT release, the long file name will be visible.

If you copy the file from the floppy to the hard disk on the down level system, the long file name associated with the file is not copied over.  This is not problematic because the down level system cannot see the long file name anyway.  However if you edit the file on the floppy using the alias, and then save a new copy back on the floppy on the down level system, the long file name associated with the file will be lost (if the editor uses the save, delete, rename cycle mentioned before).  If you take this floppy back to the newer Windows system, only the alias name will be associated with the file.   This is due to the fact that the down level system is not aware of the long file name and hence will not preserve it.

3.4.	Disk Utilities & Exclusive Volume Lock

Previously reserved fields in the file system directory entry are used for storing Last Access Date and Creation Date/Time.  A file with a long file name, which is longer than 5 characters,  will also cause the system to use previously reserved fields in the directory entry.   In previous versions of MS-DOS and Windows, these reserved entries were zero. Some Disk Utilities, especially disk repair and checking utilities, might display errors about the disk because of the usage of these reserved entries, though there are no real errors on the disk.  In the pathological case, a disk repair utility could destroy all these entries since it mistakenly thinks they are corrupted entries.  The end result of destroying these entries is different between the long file name case and last access date  & creation date/time case.  In the long file name case, the long file name is lost, but the alias (8.3 name) and the data in the file are still present.  It will just be difficult to find the file, without the associated long file name.  In the last access date & creation date/time case, the alias and the data will also be lost, because crucial information about the file (apart from the name) is also lost!

For this reason, Windows is setup to fail such utilities on default.  This feature is called Exclusive Volume Lock.  A newer version of the utility that will understand the newer on-disk file system structures, will take an exclusive volume lock and do the right thing.  Older versions of the utilities, that do not understand the newer disk structures, will not take the exclusive volume lock and will be failed when the utility tries to do direct disk writes.  The user will have to run some sort of wrapper utility that will take the Exclusive Volume lock on behalf of the app and execute the app.  COMMAND.COM will provide a switch, of the form lock <volume>:, that takes the Exclusive Volume lock on behalf of the app, if the file system is in Win 3.1 compatible mode (see below).  This COMMAND.COM switch will not be functional when the file system is in the default Chicago mode (that is the file system is not in Win 3.1 compatible mode).  If a user does use a third party wrapper for this purpose when the file system is in Chicago mode it can be risky, because an older version of a utility might potentially destroy long file names and in the worst case destroy data, while trying to repair what it thinks is a corrupted disk.

The user can set the file system in Windows 3.1 compatible mode, through the system folder in the Control Panel.  This is a setting in which none of the new file system features, such as long file names, last access date and creation date/time will be available.  The user will have to pass through a set of dialog boxes warning the user about the dire consequences of setting the file system in Win 3.1 compatible mode, if it was not previously set.  Once the file system is in Win 3.1 compatible mode, any existing long file names, last access date and creation date/time in the system will be deleted.  This forces the on-disk structures in the file system to match the ones on older versions of DOS and Windows.  When in this mode, older versions of the utilities can be safely run because there is no new information on the file system that the utility will interpret incorrectly.  However the system will still enforce the Exclusive Volume Lock to preserve internal system data consistency.  The user can safely use a COMMAND.COM switch or a third party wrapper, that would take the exclusive volume lock on behalf of the utility,  to run a utility in this case.

Even in Single MS-DOS application mode, the direct disk writes (specifically INT 26H) will be failed if the file system is in Chicago mode.  These direct disk writes will not be failed in Single MS-DOS app mode, if the file system is in Win 3.1 compatible mode.  The COMMAND.COM switch described above can be used in Single MS-DOS application mode too.

*	The decision about the form of the wrapper has not been finalized yet.  It might become a switch elsewhere in the system.

3.5.	Long File Name Format

As mentioned before, long file names preserve the case of the name.  Hence a user who creates a directory by typing mkdir examples is actually creating a directory name of examples and an alias of EXAMPLES.  However searches are case insensitive.

Period (the character .) is just another character in a (long) file name. Leading periods are allowed in a (long) file name, but trailing periods are stripped.  A file can have multiple periods as part of its name.  For example, MyFile.081293.Document is a valid file name, though its alias will probably be MYFILE08.DOC.  The first three characters after the last period in the file name are used as the extension for the alias, as long as the last period is not a leading period.  A file name of .login is also valid, though its alias will probably be LOGIN.

3.6.	Long File Names in the Root

Any file is best stored in a directory below the root in general.  This is especially true for files with long file names.  Files with long file names use up more directory entries than files with just an 8.3 name.  Since the number of entries in the root is limited, the root directory will be "filled up" with fewer files that have long file names.  In the above example, a long directory name of examples and an alias of EXAMPLES will be created.  In essence two entries will be used up and this causes the root directory to fill up faster.

4.	ISV Issues

4.1.	Limits in the Name

The maximum size of the file name component on Long File name FAT file systems is 255 characters (or 256 characters including the NULL).  The maximum path length is 260 characters (including the NULL).  These limits are the same as the ones in Win32.  The API GetVolumeInformation returns this information.  This API is supported both as a Win32 (32 bit) and an INT 21 (16 bit) API.  This API returns other useful information, such as the name of the file system.  Using the GetVolumeInformation API to determine these limits and allocate buffers, is the preferred way to deal with these limits for a logical volume.  If static buffers need to be allocated then the maximum buffer sizes defined by the Win32 API should be used.  The Win32 API defines 256 characters (including the NULL) as the maximum file name component length and 260 characters (including the NULL) as the maximum path length.  The maximum path length is 260 characters (including the NULL) even if the path is an UNC path name.

4.2.	Auto-generation scheme

The (alias) 8.3 name is auto-generated for a file name, if necessary.  No assumption should be made about the auto-generation scheme itself.  This auto-generation scheme could change  between different revisions of the operating system.

4.3.	32-bit Apps on Windows

Using the Win32 API is the preferred way of developing new applications.  The Win32 API allows portability of the application across multiple Windows systems.  Further more any of the idiosyncrasies of the underlying system or new features in the system, such as long file names, are taken care off by the Win32 API.  Lastly Win32 apps run in separate address spaces and are preemptible.

4.4.	16-bit Apps on Chicago

Most of the Win16 APIs that require the application to pass in a file name have been updated to support long file names being passed in.  These include LoadLibrary(), WinExec(), Profile APIs, _lopen() and _lcreate().  However APIs that return file names will return only 8.3 names to older versions of Windows apps for compatibility reasons.  OpenFile is an exception to these general statements about Win16 APIs.  The Win16 OpenFile API will only take an 8.3 format file name as its parameter and will return the fully enumerated path in 8.3 name format.

DOS applications generally use the INT 21 API.  The older INT 21 APIs have not changed.  All long file name INT 21 APIs have been introduced as INT 21, Function 71XX.  Any DOS application that is interested in using long file names will have to be revved to use the newer INT 21s.

The new INT 21H calls will be supported on all file systems, to the extent possible, on Chicago.  Some file systems might not support long file names.  Examples of such file systems include MSCDEX, Flash, real mode network redirectors etc.  In these cases the system will translate the newer INT 21 calls to the older INT 21 calls automatically, as long as the parameters are valid.  For example, in the FileOpen (INT 21, Func 716C) system call, the file name has to be a valid 8.3 name, for file systems that do not support long file names.  The file system will take care of the relevant translation to the older FileOpen (INT 21, Func 6C).  The GetVolumeInformation API gives information on the capabilities of the underlying file system that supports the volume in question.

* The OpenFile() support might change before ship.

4.5.	16-bit Apps & Down Level Systems

It might be necessary to develop a 16-bit application that works both on Windows releases that support long file names and on Windows or MS-DOS releases that do not support long file names.  The main code fragment of interest to deal with can be characterized as:

STC					; Set Carry for error flag

<new INT 21H call, Func 71H>		; Perform the newer INT 21H equivalent

JNC	SUCCESS			; Call succeeded, continue processing

CMP 	AX, 7100H			; See if the call is really not

; supported.  When the call is not

; supported then:  AL is set to 0;

; AH & Carry are preserved. This is

; true even in down level MS-DOS versions.

JNE	Call_Failed			; The call is supported, but something

; about this call failed

<old INT 21H call>			; Perform the older INT 21 call

Invariably the newer INT 21H calls will succeed on newer releases of Windows.

An alternative would be to use the GetVolumeInformation API as the trigger to figure out which version of the INT 21H call to use.  If the API succeeds, then use the newer INT 21H long file name calls (that are all sub-functions of Func 71H).  Otherwise use the older INT 21H calls.  As mentioned above, the GetVolumeInformation API will succeed on newer Windows releases even on file systems that do not support long file names or if the file system is in Windows 3.1 compatibility mode.  Please be sure to pass in a name that is valid for the logical volume you are operating on.  Even when calling the GetVolumeInformation API, please remember to use a code fragment such as the one above. There is no equivalent "old INT 21H call" for the GetVolumeInformation API.  It is important for you to Set the Carry flag on the newer calls, so that you can check the error return correctly on down level MS-DOS systems. The GetVolumeInformation API does not access the disk.

Note that Chicago’s Single MS-DOS Application mode behaves like a down level MS-DOS system for the case of the newer INT 21, 71xx APIs.  In this case, the Single MS-DOS application mode returns AX=7100H, without affecting the carry flag passed into the API.  So the above code fragment needs to be used for apps that need to run in Chicago’s Single MS-DOS application mode too.

4.6.	Character sets: APIs & on-disk names

4.6.1.	16 bit file APIs

All 16 bit file APIs, namely new and old INT 21 file APIs and Win 16 file APIs, will still present the OEM character set to 16 bit apps.  Since this has not changed, the 16 bit apps will continue to deal with file APIs in the same manner from a character set point of view.

4.6.2.	32 bit file APIs

The Win32 API supports both the ANSI and Unicode form of the API.  In Windows NT, both of these API forms are supported.  In Chicago, only the ANSI form of  the Win32 API is supported.  Hence Win32 apps using the file system APIs need to pass characters in the ANSI code page under Chicago.  The Win32 SetFileApisToOEM API will not be supported in Chicago.

4.6.3.	On-Disk names

Any application using the regular file system APIs, need not worry about the character set of the names on the disk.  The APIs do the right translation on behalf of the application.  However disk utilities that directly read the disk will have to contend with the character set on the disk.  The alias (8.3 names) are stored using characters from the OEM code page for compatibility reasons.  The (long) file names are stored in Unicode on the disk.

4.7.	CreateProcess, WinExec & $exec functions and LFNs

The Win32 CreateProcess & WinExec and the Win16 WinExec functions will all support long file name arguments. A DOS app using the $exec function (INT 21H, 4BH) will be restricted to the execution of 8.3 names for compatibility.  Any newer DOS app using the 16-bit $exec function (INT 21H, 4BH) and dealing with long file name executables, should translate the executable names to the equivalent 8.3 names using the Canonical API.  COMMAND.COM and the Shell VxD would support long file name execution by doing the necessary translations on behalf of the user.

4.8.	Canonical API

The Win32 GetFullPathName can be used to get a fully enumerated path name, where traversals such as "." and ".." are expanded.  A parallel 16-bit GetFullPathName function (INT 21H, 7160H, CX=0) will provide a similar facility for 16 bit apps.  In addition this 16 bit API will also expand SUBST-ed drives.  Another subfunction of this 16-bit API (INT 21H, 7160H, CX=1) will provide support for a GetShortPathName (16 bit only) API, which will allow an application to get a pure 8.3 name.  Setup applications need to use this API if they have to load files from CONFIG.SYS or AUTOEXEC.BAT.  Note that long file names are not present at boot up time and in Single MS-DOS application mode.

4.9.	Exclusive Volume API (specific to Chicago)

New 16-bit volume locking IOCTLs (MS-DOS IOCTL: INT 21, Func 440D, Major Code 08, Minor Code 4A, 4B, 6A, 6B etc.) will be supported in the next release of Windows.  Any utility that needs exclusive volume access to perform direct disk writes (INT 26H or INT 13H), should use these 16 bit Exclusive Volume IOCTLs, before performing direct disk writes.  Please refer to the Exclusive Volume API specification for more information on the locking levels that are relevant to this API.  This API will be documented in the SDK.

A Win32 app can use the DeviceIoControl function to communicate with the VWIN32 VxD and perform drive letter based (INT 21, 44OD) IOCTLs.  The same mechanism can also be used to perform direct disk reads and writes (INT 25, INT 26 & INT 13) from a Win32 app.  These DeviceIoControls will not be supported on Windows NT at this time.  Please refer to the documentation on DeviceIoControl in the SDK for more information.

* 	The above mentioned Win32 DeviceIoControls will not be supported on Windows NT.

4.10.	Keying off file names

When an application keys off file names, it should be aware of the following:

Using the alias (8.3 name) instead of the file name could break the association with the file because operations such as editing the file could potentially change the alias.  For example, consider the server side of the network which uses the file name to store information related to the file (like access permissions).  If the server side uses the alias (8.3 name) as opposed to the long name of the client file to store such information, it will be more susceptible to lose the association of permissions with the file.  If the user edits the file on the client side, the alias (8.3 name) could potentially change, and when it changes the server side will lose the associated information.

When an app caches the absolute path to the file name, the path itself could be a mixture of file names and aliases.  If there are n such name components in the path, then there are possibly 2**n such combinations.  Hence apps should store a canonical form of the absolute path, if the path needs to be stored at all.  The API provided to canonicalize the path should be used for this purpose.  The same is true for apps that use full path names to see if two files are the same.  Alternatively such apps can use the “index” field in GetFileInfoByHandle to verify whether it is the same file.  The “index” field of the GetFileInfoByHandle API might not be supported on real mode file systems, such as MSCDEX or real mode networks.

A setup program that needs to enter information into configuration files, such as CONFIG.SYS, should make sure it uses paths qualified with aliases (8.3 name components), since the long file names will not be visible at boot up time when files such as CONFIG.SYS and AUTOEXEC.BAT are processed.  The GetShortPathName API should be used for this purpose.

4.11.	Checking Directory Entries

A disk utility that is checking for directory entry coherence, should only check the valid entries.  Specifically reserved locations should either be not checked against zero values or such checks should be combined with MS-DOS version checks.  Otherwise the utility will malfunction when the entries are extended by using the reserved locations.

Values in bit fields should be checked by masking the bits of interest and then comparing it against a desired value.  Direct comparisons against a value, without masking the bits of interest, will cause the utility to break if reserved bits in the field are used in future revs of the operating system.

4.12.	Win32 & New INT 21 FindFirst/Next and FindClose

The Win32 and new INT 21 FindFirst return a handle.  The user is expected to use this handle in subsequent FindNext calls.  It is necessary that an app return this handle to the system by calling FindClose, when the app no longer needs the handle.  This is different from the 16-bit old INT 21 FindFirst and FindNext calls.  The older 16 bit INT 21 equivalents of these APIs did not require such a close operation.

The new FindFirst/Next calls return time in Coordinated Universal Time (UTC or FileTime) defined by Windows NT.  Please see the Time APIs section in this document and other relevant API specification documents for more information.

File systems, such as HPFS, may support only one name space.  If there is only one name associated with the file, it is returned as the (primary) FileName in the FindFirst/Next structure irrespective of whether the only visible name is a long file name or an 8.3 name.  In this case, the AlternateFileName is NULL.  Applications should be coded to handle this case.  The same is true for a file that has a name in 8.3 format.

As noted above, multiple periods and leading periods are allowed in a (long) file name.  Consider some parsing code running on Chicago that ends up using the updated FindFirst and FindNext calls.  If this parsing code ignores all files that start with a . character, with the intent of filtering out . and .. directories, it will end up ignoring file names such as .login.

4.13.	Time APIs

Coordinated Universal Time (UTC or FileTime) is supported across the network.  The FAT file system stamps local time in the directory entry for compatibility reasons.  At this point a bias is not stamped to allow translation of this time across different time zones. The new Win32 FindFirst/Next APIs return time in UTC (or FileTime) format.  The equivalent 16 bit (INT 21, 714E and 714F) FindFirst/Next APIs return time either in DOS date/time format or in UTC (or FileTime) format, depending on a parameter passed in by the app, as part of the API.

FileTimeToDosDateTime and DosDateTimeToFileTime will be supported both as Win32 and 16-bit APIs.  Please use the relevant functions if you need to convert the FileTime returned by the new FindFirst/Next functions to MS-DOS date/time format.  The rest of the Time APIs will be supported only as Win32 APIs.

The FAT file system now sports Creation date/time and Last Access date, in addition to the existing Last Modified date/time.  The new Creation time for a file is a more precise time than the existing Last Modified time in the FAT file system. The Creation time includes the "number of ten milliseconds in the 2 second interval”.  Hence the accuracy of the Creation time is ten milliseconds.  The new Last Access date/time is actually only a date.  There is no Last Access time.  Hence the proper assumption is that the Last Access time is always 0 (and that is what is returned in the Win32 APIs).

4.14.	TSR and Apps that monitor INT 21 calls (INT 21 hookers)

On default all INT 21 interrupts, except file API INT 21s, are passed down to any hooker present in the system.  The file API INT 21s are just passed to VM (local) hookers, but not to global (AUTOEXEC.BAT) type hookers.  This is done because there are new file APIs (new INT 21s) that support long file names for delete, rename and so on that an older hooker won't understand anyway.   Further more not all file API calls are INT 21 calls.  Specifically server calls and swapper calls to the file system are not INT 21 calls.

If the user forces the file system into Win 3.1 compatible mode, then none of the new features in the file system are turned on.  In the Win 3.1 compatible mode the file system will not support long file names, last access date and creation date/time.  In this case all the INT 21s, including the file API INT 21s, are passed to any hooker (whether they are global or local).   Before a relevant file API INT 21 is passed to a global or local hooker, the newer file API INT 21 is mapped to the equivalent older file API INT 21.  For name based new file API INT 21s, the name has to be 8.3 format conformant. If the name is not 8.3 format conformant the newer name or path based file API INT 21 call is failed.

Good citizens of Chicago will use the FileHook API to monitor file activity.  This entails writing a Ring 0 VxD.  Doing this will avoid unnecessary Ring 3 transitions which is a performance win and will allow the software to see all file I/O.  Please refer to the IFS Manager specification for information on the FileHook API.

As with Windows 3.1, software interrupts are first passed through the Ring 0 protect mode components (VxDs), then through the Ring 3 protect mode components and lastly through any relevant Virtual 8086 components (TSRs and the like).  If any of the earlier components consume the interrupt then the subsequent components do not see the interrupt.  This is very similar to the behavior seen by existing software interrupt hookers.

Any VxD that uses the FileHook API should use the FSD_Init_Order field defined in VMM.H.  This will ensure that this VxD loads in the right order.

4.15.	File System "Compatibility" switch

On default the file system in Chicago sports a whole set of new features in the file system.  The relevant ones here are long file names, last access date and creation date/time.  The user can force the file system into Win 3.1 compatible mode through a check box in the System Folder of the Control Panel.  When the user sets the file system in this mode, the disk is purged of all long file names, last access date and creation date/time, thus ensuring that the disk structure is compatible with Win 3.1.  Long file names, last access date and creation date/time are not supported while the file system is in Win 3.1 compatible mode.  Further all INT 21s are passed down to any hookers, thus ensuring that the system in this compatible mode will support existing TSRs.  When the file system is in Win 3.1 compatible mode the registry is stamped with the following setting:

Key: HKEY_LOCAL_MACHINE\SYSTEM\CurrentControlSet\Control\FileSystem

Win31FileSystem=1

On default Win31FileSystem=0.

Note that direct disk writes are still failed in Chicago, even if the file system is in Win 3.1 compatible mode.  This is needed to protect cached data in the file system.   A COMMAND.COM switch needs to be set to run older versions of utilities that perform direct disk writes.  These direct disk writes are not failed in Single MS-DOS application mode, if the file system is in Win 3.1 compatible mode.

Lastly the Shell uses the Creation Date/time for link tracking purposes.  When the file system is in Win 3.1 compatibility mode, the shell link tracking won’t function optimally.

* 	The Win31FileSystem key might become a volume based bitmap before ship.

4.16.	"for" command in COMMAND.COM

The for command in COMMAND.COM is modal.  The default will be LFNFOR=OFF. This will cause the for command to use the old INT 21s.  This implies that only aliases (8.3 names) can be used in the for command.  If LFNFOR=ON is set, then the for command uses the new INT 21s, and (long) file names can be used as part of the for command.  The default was chosen for compatibility with existing batch files.

4.17.	Down level system idiosyncrasies

The source of a copy can be from a file system that supports long file names, while the target of the copy can be to a file system that supports only the old 8.3 name.  An application that supports a “copy” type feature has to make a conscious choice about the semantics of the copy command in this case.  For example consider a copy of the form:

copy c:ThisIsALongFileName d:

One possibility is to emulate COMMAND.COM copy semantics.  In this case, COMMAND.COM uses the alias (8.3) name of the source as the primary name for the target.

Single MS-DOS application mode behaves like a down level MS-DOS system for all APIs, except for direct disk writes (INT 26H).  Direct disk writes are failed in Single MS-DOS application mode unless the application takes an exclusive volume lock (see above).

4.18.	Long command lines

COMMAND.COM now sports a 1024 character limit for environment variables and batch file lines.    This is the default in Chicago, which can be overridden by the user.  However the keyboard buffer is still limited to 128 characters on default.  This can also be overridden by the user.

Command lines passed to Windows applications (both Win32 and Win16 applications) had no inherent limit.  If these applications are invoked from the MS-DOS box, which is also the Win32 console, through batch files or through environment variables that expand to command lines longer than 128 characters, the applications will still see and be able to work with these long command lines without revving.

However MS-DOS applications will have to rev to see the longer command lines.  MS-DOS applications invariably pick up the command line from the PSP.  The command tail in the PSP is limited to 128 characters, including the leading length field and the trailing Carriage Return.  If a command tail passed to a DOS program is less than 126 actual characters, the command tail is still set in the PSP as before.  This is done for the sake of compatibility.  If a command tail passed to a DOS program is greater than 126 actual characters, then the entire command line is actually set in the environment variable CMDLINE.  The PSP itself will just contain a Carriage Return, which is a null command tail.   Note that language vendors that provide compiler run time routines have to update their MS-DOS tools to pick up the command line from the correct location.

* 	With the current scheme, users of INT 21, 4B ($exec call) will have to set the CMDLINE environment variable appropriately.  This will mostly be DOS apps.  Win16 and Win32 apps will be taken care of by the appropriate APIs.  This onus on INT 21, 4B will almost definitely change before ship time.  Either an API will be provided to get a command line or the INT 21, 4B call will be enhanced and/or an INT 21, 714B call will be added that will handle long command lines.  So any users of INT 21, 4B should watch for the final solution and use that.