# Managed Code Exception Handling

In this document, funclets are any of the exception handling sub-routines viz. filter, catch, fault, and finally. Framelets are the regions on the stack (ESP-relative) specific to the funclet, as opposed to the method’s base stack frame (EBP-based). Framelets have the return address for the nesting level, localloced region for that nesting level, and pushed arguments. The base method frame has the shadow ESP slots (explained below), the method’s locals, callee-saved registers, etc. Nesting level of any IL offset is the number of framlets surrounding that offset. Nesting level of a funclet corresponds with the nesting level of the start offset. So the nesting level on entry to a method is 0, the nesting level at the start of the first funclet, say a catch, is 1, the nesting level of an inner funclet is 2, etc. Note that the try’s do not contribute to the nesting level at all as they are executed simply, and not as a sub-routines.

We have the following requirements for a managed method with exception handling:

- Handlers are invoked using the original EBP frame, but ESP will not be reset to the original as unwinding isnt guranteed to have been done.

- Support nested handlers. This implies mulitple framelets may be present on the stack.

- Be able to (virtually or actually) unwind/crawl the call-stack at any point. Note that the funclets will have their own framelet with their own return addresses, and multiple framelets of the same method invocation will exist at different points in the call-stack.

- Be able to determine the ESP for any of the nesting levels that are currently active. This is needed if an exception is thrown from an inner nesting level and is caught by a try at an outer nesting level.

- Support asynchronous exceptions. This means that for fully interruptible methods, an exception could be triggered at almost any point. Ian is considering allowing this for partially-interruptible methods too.

These requirements are more than that of today's traditional, unmanaged code because :

- Unmanaged code doesn’t need to do a virtual unwind (stack crawl).

- Unmanaged code doesn’t support nested EH.

If an exception is thrown from an inner nesting level and is caught by a try at an outer nesting level, the EE will need to reset the ESP to the value for that outer nesting level. The possible solutions are:

- Keep a list of ESP values for each nesting level.

- Keep on unwinding the call-stack until the method is question has been visited curNestingLevel-catchNestingLevel times. This is more involved. We also would need to visit a function for every active finally even though that finally may have been called locally by the corresponding try block. Determining if a finally has been locally called will again involve keeping some state, which will correspond with the above scheme.

We have chosen the first option.

### Why do we need to have the start and end ranges of handlers?

When an exception thrown from a nested handler is caught by an outer try block, we need to know the ESP of the outer nesting level. For this, we need to be able to determine its exact nesting level. This is not possible with just the start offsets of handlers. The possible solutions are:

- The handlers specify the start and end offset. This lets us determine the nesting level of any offset within the code.

- The handlers specify their own nesting level. This information can be deduced from the above and hence has lesser power than the above.

- We would also have to have markers or special instructions in code to specify the end of the handlers so that the verifier could ensure that the nesting levels specified were accurate.

- It is possible to omit the nesting level and just have the start offset of handlers and end markers in code. This approach is equivalent but needs work to be done to calculate the nesting level, even for trusted code.

- Note that the markers may be lexical (all code lexically between the start offset and the corresponding marker is part of the funclet) or semantic (all paths starting from the start offset have to eventually reach a marker, and all such paths are part of the funclet).

- In either case, the code needs to be scanned to determine the extent of funclets. This is unreasonable for simple compilers. Determining the extent of funclets and the nesting level of a given offset in code is required while performing a leave to determine if the leave changes the nesting level or not.

### Problems with fully interruptible code and asynchronous exceptions

The URT supports async exceptions. Also, fully interruptible code can be interrupted at any point. The combination of this leads to the case where a thread executing fully interruptible code could be exposed to an exception at any point. This would typically be a ThreadAbortException thrown by another thread. What this implies is that any mechanism for exception support has to keep itself in a consistent state at all points in managed code where it could be interrupted. Note that for fully interruptible methods, this is all code except the prolog and the epilog. It is conceivable to mark specific regions of the method as not fully interruptible, but we have currently not chosen to do so.

We have instead chosen to have the unmanaged part of the URT help out by storing the ESP into the method's frame before invoking the funclet

### Problems with filters

It should be noted that when any funclet, except a filter called as part of the first pass, is executing (at the top of the stack), all frames between that funclet and the method which will handle the exception are dead. First-pass filters are therefore special as all the frames on the stack are potentially live as they could be activated during the second pass.

### Problems with localloc in handlers

ESP is needed to get to the return address of the funclet. Executing a localloc adjusts ESP. Hence, we need to keep track of the original ESP on entry to the funclet (for every active nesting level). These are currently not supported but might be implemented during Beta 2.

## Implementation

- All methods with exception clauses have EBP-frames.

- The method reserves n+f+1 contiguous DWORDs in its frame for storing the ESPs for every active funclet. We will call them the shadow ESP slots.

  - n is the max nesting level in the method

  - f=1 if there are any filters in the method, and 0 otherwise.

- These slots are treated as 0-terminated list of ESPs for every active nesting level.

- The method has to zero out the first of these slots in the method's prolog.

There are essentially three scenarios:

- catch/fault/finally called by the EE. When these funclets are called, no inner nesting level can be active (though we may subsequently enter inner nesting levels).

- Filter called by the EE. During the first pass, inner funclets may already be active and any such finallys will be activated during the second pass.

- Finally called in the fall-through case at the end of the try.

The first case involves the all the basic concepts used and we will see how that works first. The other two scenarios use variations and refinements to this general approach.

### catch/fault/finally called by the EE

- Before invoking the funclet, the EE calls ICodeManager::FixContext() which returns a pointer to the shadow ESP slot corresponding to the nesting level about to be invoked (and also zeroes out the next slot to maintain the 0-termination property).

- The EE writes the ESP that the funclet will be invoked with to the pointed slot. Hence, on entry to the funclet, the current ESP is already in the corresponding DWORD.

- If a stack-crawl happens at any point inside of the funclet, the CodeManager can examine the slots to determine the nesting level, and also the ESP for each nesting level.

- After the funclet terminates, the EE zeroes out the slot.

- In the case of a catch, the EE then unwinds the stack to the ESP of the outer nesting level, and resumes control in the managed code at that outer nesting level.

### Filter called by the EE

Filters have to be handled specially as an outer filter may be executed in the first pass, and then any inner finally will get executed in the second pass.

- It is not possible for filters to use the slot corresponding to their nesting level. Instead, we make filters use the first available slot. We can do this as long as filters cannot have any exception clauses nested inside of them.

- We need to be able to determine if a nesting level corresponds to a filter as opposed to the other funclet types. Therefore, the EE writes (ESP | 0x01) to the slot. The stack crawler can then inspect the lower bit to see if the funclet is a filter or not.

### Locally-called finallys

Locally-called finallys have to be handled differently as we are always in managed code, and a stack-unwind might happen at any time. The series of operations is as follows:

- Write a special marker (0xFC) instead of ESP to the slot corresponding to the nesting level of the finally about to be invoked.

- Push the address of the target of the leave.

- Jump to the start of the finally. The push+jmp combination is effectively like a call since it pushes a return address on the stack and transfers control to another location. The reason this is used instead of a call is that the finally can directly "return" to the leave target, which will be lexically outside the region protected by the "try" block. This is needed for the async exception + fully interruptible code combination.

- At the end of the finally, it just does a return (actually a "pop reg; jmp reg" to keep the # calls and # returns in sync).

- The leave target zeroes out the slot to which we had written the special marker (0xFC)

- Note that the in this case, there are places where the code may get interrupted where we would have written a value to the slot but not adjusted the stack and vice versa. However, due to the use of the special value, and the fact that a locally called finally pushes 1 DWORD on the stack, it is possible to correctly unwind the stack. Possible bug when leaving multiple finallys.

### Notes

- A method invocation can have multiple framelets simultaneously active on the stack active. GC reporting specifies that a pointer may not be reported multiple times (though different pointers with the same value have to be reported individually). This issue is addressed by reporting the method’s GC locals only from the outermost nesting level during the stack-walk.

This does not affect the liveness encoding, as any pointer active at the resumption target in the outer level will be live across the funclet at the inner level. So the funclet at the innermost level will naturally report all live pointers of the outer levels.

Filters

### Problems with the approach

- Supporting nesting levels with this approach (and any similar approaches) places restrictions on where the try and funclet code can be placed. Currently they have to be kept together at the same nesting level, and different try’s cannot share funclets.

- Longer code sequence while locally calling a finally. This will be the common non-exception path which needs to be as fast as possible.

### Why filters cannot have exception clauses nested inside of them?

- We have chosen to not specify the end offsets of filters for reducing size. Hence determining nesting level would be difficult inside of filters.

- Since a filter uses the topmost shadow ESP slot available, if inner funclets were allowed, they would use the slot corresponding to their nesting level which might be the one being used by the filter.