Compound File Binary Format

3 January, 1997

This document describes the on-disk format of the Compound File, used as the underpinnings of the structured storage support for OLE 2.0.

1. Overview

2. Sector Types

2.1 Header

2.2 Fat Sectors

2.3 MiniFat Sectors

2.4 DIF Sectors

2.5 Directory Sectors

2.6 Storage Sectors

3. Examples

3.1 Sector 0: Header

3.2 SECT 0: First (Only) FAT Sector

3.3 SECT 1: First (Only) Directory Sector

3.4 SECT 3: MiniFat Sector

3.5 SECT 4: MiniStream (Data of “Stream 1”)

Note: This document is meant to accompany the Microsoft Structured Storage Reference Implementation, heretoafter referred to as the “software”. Some of the information in this documentation may be inaccurate or may not be an accurate representation of the actual functionality of the software. When this document and the functionality of the software conflict, The actual functionality of the software represents the correct functionality. Microsoft assumes no responsibility for any damages that might occur either directly or indirectly from these discrepencies or inaccuracies. Microsoft may have trademarks, copyrights, patents or pending patent applications, or other intellectual property rights covering subject matter in this document and in the software. The furnishing of this document does not give you a license to these trademarks, copyrights, patents, or other intellectual property rights.

1.	Overview

A Compound File is made up of a number of virtual streamvirtual streams.  These are collections of data that behave as a linear stream, although their on-disk format may be fragmented.  Virtual streams can be user data, or they can be control structures used to maintain the file.  Note that the file itself can also be considered a virtual stream.

All allocations of space within a Compound File are done in units called sectorsectors.  The size of a sector is definable at creation time of a Compound File, but for the purposes of this document will be 512 bytes.  A virtual stream is made up of a sequence of sectors.

The Compound File uses several different types of sector:  Fat, Directory, Minifat, DIF, and Storage. A separate type of 'sector' is a Header, the primary difference being that a Header is always 512 bytes long (regardless of the sector size of the rest of the file) and is always located at offset zero (0).  With the exception of the header, sectors of any type can be placed anywhere within the file.  The function of the various sector types is discussed below.

In the discussion below, the term SECTSECT is used to describe the location of a sector within a virtual stream (in most cases this virtual stream is the file itself).  Internally, a SECT is represented as a ULONG.

2.	Sector Types

[4 bytes]		typedef unsigned long ULONG;

[2 bytes]		typedef unsigned short USHORT;

[2 bytes]		typedef short OFFSETOFFSET;

[4 bytes]		typedef ULONG SECTSECT;

[4 bytes]		typedef ULONG FSINDEXFSINDEX;

[2 bytes]		typedef USHORT FSOFFSETFSOFFSET;

[4 bytes]		typedef ULONG DFSIGNATUREDFSIGNATURE;

[1 byte]		typedef unsigned char BYTE;

[2 bytes]		typedef unsigned short WORD;

[4 bytes]		typedef unsigned long DWORD;

[2 bytes]		typedef WORD DFPROPTYPEDFPROPTYPE;

[4 bytes]		typedef ULONG SIDSID;

[16 bytes]		typedef CLSID GUID;

[8 bytes]		typedef struct tagFILETIME {

DWORD dwLowDateTime;

DWORD dwHighDateTime;

} FILETIME, TIME_T;

[4 bytes]		const SECT DIFSECTDIFSECT		= 0xFFFFFFFC;

[4 bytes]		const SECT FATSECTFATSECT		= 0xFFFFFFFD;

[4 bytes]		const SECT ENDOFCHAINENDOFCHAIN	= 0xFFFFFFFE;

[4 bytes]		const SECT FREESECTFREESECT		= 0xFFFFFFFF;

2.1	Header

struct StructuredStorageHeader {		// [offset from start in bytes, length in bytes]

BYTE		_abSig[8];		// [000H,08] {0xd0, 0xcf, 0x11, 0xe0, 0xa1, 0xb1, 0x1a, 0xe1} for current version,

// was {0x0e, 0x11, 0xfc, 0x0d, 0xd0, 0xcf, 0x11, 0xe0} on old, beta 2 files (late ’92)

// which are also supported by the reference implementation

CLSID		_clid;			// [008H,16] class id (set with WriteClassStg, retrieved with GetClassFile/ReadClassStg)

USHORT		_uMinorVersion;	// [018H,02] minor version of the format: 33 is written by reference implementation

USHORT		_uDllVersion;		// [01AH,02] major version of the dll/format: 3 is written by reference implementation

USHORT		_uByteOrder;		// [01CH,02] 0xFFFE: indicates Intel byte-ordering

USHORT		_uSectorShift;		// [01EH,02] size of sectors in power-of-two (typically 9, indicating 512-byte sectors)

USHORT		_uMiniSectorShift;	// [020H,02] size of mini-sectors in power-of-two (typically 6, indicating 64-byte mini-sectors)

USHORT		_usReserved;		// [022H,02] reserved, must be zero

ULONG		_ulReserved1;		// [024H,04] reserved, must be zero

ULONG		_ulReserved2;		// [028H,04] reserved, must be zero

FSINDEX		_csectFat;		// [02CH,04] number of SECTs in the FAT chain

SECT		_sectDirStart;		// [030H,04] first SECT in the Directory chain

DFSIGNATURE	_signature;	// [034H,04] signature used for transactionin: must be zero. The reference implementation

// does not support transactioning

ULONG		_ulMiniSectorCutoff;	// [038H,04] maximum size for mini-streams: typically 4096 bytes

SECT		_sectMiniFatStart;	// [03CH,04] first SECT in the mini-FAT chain

FSINDEX		_csectMiniFat;		// [040H,04] number of SECTs in the mini-FAT chain

SECT		_sectDifStart;		// [044H,04] first SECT in the DIF chain

FSINDEX		_csectDif;			// [048H,04] number of SECTs in the DIF chain

SECT		_sectFat[109];		// [04CH,436] the SECTs of the first 109 FAT sectors

};

The Header contains vital information for the instantiation of a Compound File.  Its total length is 512 bytes.  There is exactly one Header in any Compound File, and it is always located beginning at offset zero in the file.

2.2	Fat Sectors

The FatFat is the main allocator for space within a Compound File.  Every sector in the file is represented within the Fat in some fashion, including those sectors that are unallocated (free).  The Fat is a virtual stream made up of  one or more Fat Sectors.

Fat sectors are arrays of SECTs that represent the allocation of space within the file.  Each stream is represented in the Fat by a chainchain, in much the same fashion as a DOS file-allocation-table (FAT).  To elaborate, the set of Fat Sectors can be considered together to be a single array -- each cell in that array contains the SECT of the next sector in the chain, and this SECT can be used as an index into the Fat array to continue along the chain.  Special values are reserved for chain terminators (ENDOFCHAIN = 0xFFFFFFFE), free sectors (FREESECT = 0xFFFFFFFF), and sectors that contain storage for Fat Sectors (FATSECT = 0xFFFFFFFD)  or DIF Sectors (DIFSECT = 0xFFFFFFC), which are not chained in the same way as the others.

The locations of Fat Sectors are read from the DIF (Double-indirect Fat), which is described below.  The Fat is represented in itself, but not by a chain – a special reserved SECT value (FATSECT = 0xFFFFFFFD) is used to mark sectors allocated to the Fat.

A SECT can be converted into a byte offset into the file by using the following formula:  SECT << ssheader._uSectorShift + sizeof(ssheader).  This implies that sector 0 of the file begins at byte offset 512, not at 0.

2.3	MiniFat Sectors

Since space for streams is always allocated in sector-sized blocks, there can be considerable waste when storing objects much smaller than sectors (typically 512 bytes).  As a solution to this problem, we introduced the concept of the MiniFatMiniFat.  The MiniFat is structurally equivalent to the Fat, but is used in a different way.  The virtual sector size for objects represented in the Minifat is 1 << ssheader._uMiniSectorShift (typically 64 bytes) instead of 1 << ssheader._uSectorShift (typically 512 bytes).  The storage for these objects comes from a virtual stream within the Multistream (called the MinistreamMinistream).

The locations for MiniFat sectors are stored in a standard chain in the Fat, with the beginning of the chain stored in the header.

A Minifat sector number can be converted into a byte offset into the ministream by using the following formula:  SECT << ssheader._uMiniSectorShift.  (This formula is different from the formula used to convert a SECT into a byte offset in the file, since no header is stored in the Ministream)

The Ministream is chained within the Fat in exactly the same fashion as any normal stream.  It is referenced by the first Directory Entry (SID 0).

2.4	DIF Sectors

The Double-Indirect FatDouble-Indirect FatDIF is used to represent storage of the Fat.  The DIF is also represented by an array of SECTs, and is chained by the terminating cell in each sector array (see the diagram above).  As an optimization, the first 109 Fat Sectors are represented within the header itself, so no DIF sectors will be found in a small (< 7 MB) Compound File.

The DIF represents the Fat in a different manner than the Fat represents a chain.    A given index into the DIF will contain the SECT of the Fat Sector found at that offset in the Fat virtual stream.  For instance, index 3 in the DIF would contain the SECT for Sector #3 of the Fat.

The storage for DIF Sectors is reserved in the Fat, but is not chained there (space for it is reserved by a special SECT value , DIFSECT=0xFFFFFFFC).  The location of the first DIF sector is stored in the header.

A value of ENDOFCHAIN=0xFFFFFFFE is stored in the pointer to the next DIF sector of the last DIF sector.

2.5	Directory Sectors

typedef enum tagSTGTY {

STGTY_INVALID		= 0,

STGTY_STORAGE		= 1,

STGTY_STREAM		= 2,

STGTY_LOCKBYTES	= 3,

STGTY_PROPERTY	= 4,

STGTY_ROOT		= 5,

} STGTYSTGTY;

typedef enum tagDECOLOR {

DE_RED				= 0,

DE_BLACK			= 1,

} DECOLORDECOLOR;

struct StructuredStorageDirectoryEntry {			// [offset from start in bytes, length in bytes]

BYTE		_ab[32*sizeof(WCHAR)];		// [000H,64] 64 bytes. The Element name in Unicode, padded with zeros to

//  fill this byte array

WORD		_cb;						// [040H,02] Length of the Element name in characters, not bytes

BYTE		_mse;					// [042H,01] Type of object: value taken from the STGTY enumeration

BYTE		_bflags;					// [043H,01] Value taken from DECOLOR enumeration.

SID			_sidLeftSib;				// [044H,04] SID of the left-sibling of this entry in the directory tree

SID			_sidRightSib;				// [048H,04] SID of the right-sibling of this entry in the directory tree

SID			_sidChild;					// [04CH,04] SID of the child acting as the root of all the children of this

//  element (if _mse=STGTY_STORAGE)

GUID		_clsId;					// [050H,16] CLSID of this storage (if _mse=STGTY_STORAGE)

DWORD		_dwUserFlags;				// [060H,04] User flags of this storage (if _mse=STGTY_STORAGE)

TIME_T		_time[2];					// [064H,16] Create/Modify time-stamps (if _mse=STGTY_STORAGE)

SECT		_sectStart;				// [074H,04] starting SECT of the stream (if _mse=STGTY_STREAM)

ULONG		_ulSize;					// [078H,04] size of stream in bytes (if _mse=STGTY_STREAM)

DFPROPTYPE	_dptPropType;			// [07CH,02] Reserved for future use. Must be zero.

};

The DirectoryDirectory is a structure used to contain per-stream information about the streams in a Compound File, as well as to maintain a tree-styled containment structure.  It is a virtual stream made up of one or more Directory Sectors.  The Directory is represented as a standard chain of sectors within the Fat. The first sector of the Directory chain (the Root Directory Entry)

Each level of the containment hierarchy (i.e. each set of siblings) is represented as a red-black tree.  The parent of this set of sibilings will have a pointer to the top of this tree.  This red-black tree must maintain the following conditions in order for it to be valid:

1.	The root node must always be black. Since the root directory (see below) does not have siblings, it's color is irrelevant and may therefore be either red or black.

2.	No two consecutive nodes may both be red.

3.	The left child must always be less than the right child.  This relationship is defined as:

A node with a shorter name is less than a node with a longer name (i.e. compare length of the name)

For nodes with the same length names, compare the two names.

The simplest implementation of the above invariants would be to mark every node as black, in which case the tree is simply a binary tree.

A Directory Sector is an array of Directory Entries, a structure represented in the diagram below.  Each user stream within a Compound File is represented by a single Directory Entry.  The Directory is considered as a large array of Directory Entries.  It is useful to note that the Directory Entry for a stream remains at the same index in the Directory array for the life of the stream – thus, this index (called an SIDSID) can be used to readily identify a given stream.

The directory entry is then padded out with zeros to make a total size of 128 bytes.

Directory entries are grouped into blocks of four to form Directory Sectors.

2.5.1	Root Directory Entry

The first sector of the Directory chain (also referred to as the first element of the Directory array, or SID 0) is known as the Root Directory EntryRoot Directory Entry and is reserved for two purposes:  First, it provides a root parent for all objects stationed at the root of the multi-stream.  Second, its function is overloaded to store the size and starting sector for the Mini-stream.

The Root Directory Entry behaves as both a stream and a storage.  All of the fields in the Directory Entry are valid for the root. The Root Directory Entry’s Name field typically contains the string “RootEntry” in Unicode, although some versions of structured storage (particularly the preliminary reference implementation and the Macintosh version) store only the first letter of this string, “R” in the name. This string is always ignored, since the Root Directory Entry is known by its position at SID 0 rather than by its name, and its name is not otherwise used. New implementations should write “RootEntry” properly in the Root Directory Entry for consistency and support manipulating files created with only the “R” name.

2.5.2	Other Directory Entries

Non-root directory entries are marked as either stream (STGTY_STREAM) or storage (STGTY_STORAGE) elements. Storage elements have a _clsid, _time[], and _sidChild values; stream elements may not. Stream elements have valid _sectStart and _ulSize members, whereas these fields are set to zero for storage elements (except as noted above for the Root Directory Entry).

To determine the physical file location of actual stream data from a stream directory entry, it is necessary to determine which FAT (normal or mini) the stream exists within. Streams whose _ulSize member is less than the _ulMiniSectorCutoff value for the file exist in the ministream, and so the _startSect is used as an index into the MiniFat (which starts at _sectMiniFatStart) to track the chain of mini-sectors through the mini-stream (which is, as noted earlier, the standard (non-mini) stream referred to by the Root Directory Entry’s _sectStart value). Streams whose _ulSize member is greater than the _ulMiniSectorCutoff value for the file exist as standard streams – their _sectStart value is used as an index into the standard FAT which describes the chain of full sectors containing their data).

2.6	Storage Sectors

Storage sectors are simply collections of arbitrary bytes.  They are the building blocks of user streams, and no restrictions are imposed on their contents.  Storage sectors are represented as chains in the Fat, and each storage chain (stream) will have a single Directory Entry associated with it.

3.	Examples

This section contains a hexadecimal dump of an example structured storage file to clarify the binary file format.

3.1	Sector 0: Header

_abSig					= DOCF 11E0 A1B1 1AE1

_clid					= 0000 0000 0000 0000 0000 0000 0000 0000

_uMinorVersion			= 003B

_uDllVersion			= 3

_uByteOrder			= FFFE (Intel byte order)

_uSectorShift			= 9 (512 bytes)

_uMiniSectorShift		= 6 (64 bytes)

_usReserved			= 0000

_ulReserved1			= 00000000

_ulReserved2			= 00000000

_csectFat				= 00000001

_sectDirStart			= 00000001

_signature				= 00000000

_ulMiniSectorCutoff	= 00001000 (4096 bytes)

_sectMiniFatStart		= 00000002

_csectMiniFat			= 00000001

_sectDifStart			= FFFFFFFE (no DIF, file is < 7Mb)

_csectDIF				= 00000000

_sectFat[]				= 00000000 FFFFFFFF . . . (continues with FFFFFFFF)

000000:  D0CF 11E0 A1B1 1AE1  0000 0000 0000 0000   ................

000010:  0000 0000 0000 0000  3B00 0300 FEFF 0900   ........;.......

000020:  0600 0000 0000 0000  0000 0000 0100 0000   ................

000030:  0100 0000 0000 0000  0010 0000 0200 0000   ................

000040:  0100 0000 FEFF FFFF  0000 0000 0000 0000   ................

000050:  FFFF FFFF FFFF FFFF  FFFF FFFF FFFF FFFF   ................

. . .

0001F0:  FFFF FFFF FFFF FFFF  FFFF FFFF FFFF FFFF   ................

3.2	SECT 0: First (Only) FAT Sector

SECT 0: FFFFFFFD = FATSECT: marks this sector as a FAT sector.

Referred to in header by _sectFat[0]

SECT 1: FFFFFFFE = ENDOFCHAIN: marks the end of the directory chain,

referred to in header by _sectDirStart

SECT 2: FFFFFFFE = ENDOFCHAIN: marks the end of the mini-fat, referred to

in header by _sectMiniFatStart

SECT 3: 00000004 = pointer to the next sector in the “Stream 1” data. This sector is

the first sector of “Stream 1”, it is referred to by the Directory Entry

SECT 4: ENDOFCHAIN (0xFFFFFFFE): marks the end of the “Stream 1” stream data.

Further Entries are empty (FREESECT = 0xFFFFFFFF)

000200:  FDFF FFFF FEFF FFFF  FEFF FFFF 0400 0000   ................

000210:  FEFF FFFF FFFF FFFF  FFFF FFFF FFFF FFFF   ................

. . .

0003F0:  FFFF FFFF FFFF FFFF  FFFF FFFF FFFF FFFF   ................

3.3	SECT 1: First (Only) Directory Sector

SID 0: Root SID: Root Name = "R"

SID 1: Element 1 SID: Name = "Storage 1"

SID 2: Element 2 SID: Name = "Stream 1"

SID 3: Unused

3.3.1	SID 0: Root Directory Entry

_ab          = ("R") (this should be “Root Entry”)

_cb          = 0004 (4 bytes, includes double-null terminator)

_mse         = 05 (STGTY_ROOT)

_bflags      = 00 (DE_RED)

_sidLeftSib  = FFFFFFFF (none)

_sidRightSib = FFFFFFFF (none)

_sidChild    = 00000001 (SID 1: “Storage 1”)

_clsid       = 0067 6156 54C1 CE11 8553 00AA 00A1 F95B

_dwUserFlags = 00000000 (n/a for STGTY_ROOT)

_time[0]     = CreateTime   = 0000 0000 0000 0000 (none set)

_time[1]     = ModifyTime   = 801E 9213 4BB4 BA01 (??)

_sectStart   = 00000003 (starting sector of MiniStream)

_ulSize      = 00000240 (length of MiniStream in bytes)

_dptPropType = 0000 (n/a)

000400:  0052 0000 0000 0000  0000 0000 0000 0000   .R..............

000410:  0000 0000 0000 0000  0000 0000 0000 0000   ................

000420:  0000 0000 0000 0000  0000 0000 0000 0000   ................

000430:  0000 0000 0000 0000  0000 0000 0000 0000   ................

000440:  0400 0500 FFFF FFFF  FFFF FFFF 0100 0000   ................

000450:  0067 6156 54C1 CE11  8553 00AA 00A1 F95B   .gaVT....S.....[

000460:  0000 0000 0000 0000  0000 0000 801E 9213   ................

000470:  4BB4 BA01 0300 0000  4002 0000 0000 0000   K.......@.......

3.3.2	SID 1: “Storage 1”

_ab          = ("Storage 1")

_cb          = 0014 (20 bytes, including double-null terminator)

_mse         = 01 (STGTY_STORAGE)

_bflags      = 01 (DE_BLACK)

_sidLeftSib  = FFFFFFFF (none)

_sidRightSib = FFFFFFFF (none)

_sidChild    = 00000002 (SID 2: “Stream 1”)

_clsid       = 0000 0000 0000 0000 0000 0000 0000 0000 (none set)

_dwUserFlags = 00000000 (none set)

_time[0]     = CreateTime   = 00000000 00000000 (none set)

_time[1]     = ModifyTime   = 00000000 00000000 (none set)

_sectStart   = 00000000 (n/a)

_ulSize      = 00000000 (n/a)

_dptPropType = 0000 (n/a)

000480:  5300 7400 6F00 7200  6100 6700 6500 2000   S.t.o.r.a.g.e. .

000490:  3100 0000 0000 0000  0000 0000 0000 0000   1...............

0004A0:  0000 0000 0000 0000  0000 0000 0000 0000   ................

0004B0:  0000 0000 0000 0000  0000 0000 0000 0000   ................

0004C0:  1400 0101 FFFF FFFF  FFFF FFFF 0200 0000   ................

0004D0:  0061 6156 54C1 CE11  8553 00AA 00A1 F95B   .aaVT....S.....[

0004E0:  0000 0000 0088 F912  4BB4 BA01 801E 9213   ........K.......

0004F0:  4BB4 BA01 0000 0000  0000 0000 0000 0000   K...............

3.3.3	SID 2: “Stream 1”

_ab          = ("Stream 1")

_cb          = 0012 (18 bytes, including double-null terminator)

_mse         = 02 (STGTY_STREAM)

_bflags      = 01 (DE_BLACK)

_sidLeftSib  = FFFFFFFF (none)

_sidRightSib = FFFFFFFF (none)

_sidChild    = FFFFFFFF (n/a for STGTY_STREAM)

_clsid       = 0000 0000 0000 0000 0000 0000 0000 0000 (n/a)

_dwUserFlags = 00000000 (n/a)

_time[0]     = CreateTime   = 00000000 00000000 (n/a)

_time[1]     = ModifyTime   = 00000000 00000000 (n/a)

_startSect   = 00000000 (SECT in mini-fat, since _ulSize is smaller than _ulMiniSectorCutoff)

_ulSize      = 00000220 (< ssheader._ulMiniSectorCutoff, so _sectStart is in Mini)

_dptPropType = 0000 (n/a)

000500:  5300 7400 7200 6500  6100 6D00 2000 3100   S.t.r.e.a.m. .1.

000510:  0000 0000 0000 0000  0000 0000 0000 0000   ................

000520:  0000 0000 0000 0000  0000 0000 0000 0000   ................

000530:  0000 0000 0000 0000  0000 0000 0000 0000   ................

000540:  1200 0201 FFFF FFFF  FFFF FFFF FFFF FFFF   ................

000550:  0000 0000 0000 0000  0000 0000 0000 0000   ................

000560:  0000 0000 0000 0000  0000 0000 0000 0000   ................

000570:  0000 0000 0000 0000  2002 0000 0000 0000   ........ .......

000580:  0000 0000 0000 0000  0000 0000 0000 0000   ................

3.3.4	SID 3: Unused

000590:  0000 0000 0000 0000  0000 0000 0000 0000   ................

0005A0:  0000 0000 0000 0000  0000 0000 0000 0000   ................

0005B0:  0000 0000 0000 0000  0000 0000 0000 0000   ................

0005C0:  0000 0000 FFFF FFFF  FFFF FFFF FFFF FFFF   ................

0005D0:  0000 0000 0000 0000  0000 0000 0000 0000   ................

0005E0:  0000 0000 0000 0000  0000 0000 0000 0000   ................

0005F0:  0000 0000 0000 0000  0000 0000 0000 0000   ................

3.4	SECT 3: MiniFat Sector

SECT 0: 00000001: pointer to the second sector in the “Stream 1” data. This sector is

the first sector of “Stream 1”, it is referred to by _sectStart of SID 2

SECT 1: 00000002: pointer to the third sector in the “Stream 1” data. This sector is

the second sector of “Stream 1”, it is referred to in MiniFat SECT 0, above.

. . .

SECT 8: FFFFFFFE = ENDOFCHAIN: marks the end of the “Stream 1” data.

Further Entries are empty (FREESECT = 0xFFFFFFFF)

000600:  0100 0000 0200 0000  0300 0000 0400 0000   ................

000610:  0500 0000 0600 0000  0700 0000 0800 0000   ................

000620:  FEFF FFFF FFFF FFFF  FFFF FFFF FFFF FFFF   ................

. . .

0007F0:  FFFF FFFF FFFF FFFF  FFFF FFFF FFFF FFFF   ................

3.5	SECT 4: MiniStream (Data of “Stream 1”)

// referred to by SECTs in MiniFat of SECT 3, above

000800:  4461 7461 2066 6F72  2073 7472 6561 6D20   Data for stream

000810:  3144 6174 6120 666F  7220 7374 7265 616D   1Data for stream

000820:  2031 4461 7461 2066  6F72 2073 7472 6561    1Data for strea

. . .

000A00:  7461 2066 6F72 2073  7472 6561 6D20 3144   ta for stream 1D

000A10:  6174 6120 666F 7220  7374 7265 616D 2031   ata for stream 1

// data ends at 000A1F, MiniSector is filled to the end with known data (a copy of the header or

// FFFFFFF to prevent random disk or memory contents from contaminating the file on-disk.

000A20:  0000 0000 0000 0000  3B00 03FF FE00 0900   ........;.......

000A30:  0600 0000 0000 0000  0000 0000 0000 0100   ................

000A40:  D0CF 11E0 A1B1 1AE1  0000 0000 0000 0000   ................

000A50:  0000 0000 0000 0000  003B 0003 FFFE 0009   .........;......

000A60:  0006 0000 0000 0000  0000 0000 0000 0001   ................

000A70:  0000 0001 0000 0000  0000 1000 0000 0002   ................

000A80:  0000 0001 FFFF FFFE  0000 0000 0000 0000   ................

000A90:  FFFF FFFF FFFF FFFF  FFFF FFFF FFFF FFFF   ................

. . .

000BF0:  FFFF FFFF FFFF FFFF  FFFF FFFF FFFF FFFF   ................

Index

C

chain, 2

D

DECOLOR, 3

DFPROPTYPE, 1

DFSIGNATURE, 1

DIF, 3

DIFSECT, 1

Directory, 3

Double-Indirect Fat, 3

E

ENDOFCHAIN, 1

F

Fat, 2

FATSECT, 1

FREESECT, 1

FSINDEX, 1

FSOFFSET, 1

M

MiniFat, 2

Ministream, 2

O

OFFSET, 1

R

Root Directory Entry, 4

S

SECT, 1

sector, 1

SID, 1, 4

STGTY, 3

V

virtual stream, 1