Microsoft®
Memphis Beta Device Driver Kit

I82930
USB Device Sample Minidriver Design Notes

This document is for informational purposes only. MICROSOFT MAKES NO WARRANTIES, EXPRESS OR IMPLIED, IN THIS DOCUMENT.

Microsoft Corporation may have patents or pending patent applications, trademarks, copyrights, or other intellectual property rights covering subject matter in this document. The furnishing of this document does not give you any license to the patents, trademarks, copyrights, or other intellectual property rights except as expressly provided in any written license agreement from Microsoft Corporation.

Microsoft does not make any representation or warranty regarding specifications in this document or any product or item developed based on these specifications. Microsoft disclaims all express and implied warranties, including but not limited to the implied warranties or merchantability, fitness for a particular purpose and freedom from infringement. Without limiting the generality of the foregoing, Microsoft does not make any warranty of any kind that any item developed based on these specifications, or any portion of a specification, will not infringe any copyright, patent, trade secret or other intellectual property right of any person or entity in any country. It is your responsibility to seek licenses for such intellectual property rights where appropriate. Microsoft shall not be liable for any damages arising out of or in connection with the use of these specifications, including liability for lost profit, business interruption, or any other damages whatsoever. Some states do not allow the exclusion or limitation of liability or consequential or incidental damages; the above limitation may not apply to you.

ActiveMovie, ActiveVRML, ActiveX, BackOffice, Developer Studio, Direct3D, DirectDraw, DirectInput, DirectMusic, DirectPlay, DirectSound, DirectX, Microsoft, NetMeeting, OpenType, Visual Basic, Visual C++, Win32, Windows, and Windows NT are trademarks or registered trademarks of Microsoft Corporation in the United States and/or other countries. Other product and company names mentioned herein may be the trademarks of their respective owners.

© 1997 Microsoft Corporation. All rights reserved.

Revision History

| Date | Description |
| --- | --- |
| 1/6/97 | January 97 Preview draft |

Contents

Overview	3

Background Notes	3

Notes on Writing USB Device Minidrivers	4

Anatomy of the Sample Minidriver	4

Event-driven Walkthrough of the Sample Minidriver	6

References	6

LIST THEM HERE	6

Reference to Other Microsoft-supplied Samples	6

Overview

The purpose of this Design Note is to document I82930, which is a sample USB device minidriver that is provided by Microsoft, in source-code form, to give the user assistance in writing their own minidriver. To be of maximum value, this document requires the user to have the following additional materials close at hand.

·	USB Driver and Minidriver Design Notes and Reference, which is another of the documents in the Memphis DDK. All USB device driver-provided function calls made by this sample minidriver are documented here.

·	WDM Design Notes and Reference, which is another of the documents in the Memphis DDK. References for I/O Request Packets (IRPs) that are used by this sample minidriver are documented here.

·	The I82930 source-code files. After you install the WDM DDK, these source code files can be located at [path to be determined].

I82930 is a driver for the Intel 82930 USB test board. This sample demonstrates how a minidriver gets loaded, and how it submits requests to the USB Driver Interface (USBDI).

There are additional device-specific sample minidrivers located on this Memphis DDK. See the section titled “Reference to Other Microsoft-provided Samples” for a list of additional sample minidrivers provided by Microsoft to give the user assistance in writing their own minidriver. The focus of this Design Note is on the USB device sample minidriver. No attempt is made here to explain the USB Driver Interface -- a “and then a miracle occurs” attitude is taken with regard to USBDI.

This Design Note is organized as follows:

Background Notes

Provides important information relevant to writing USB device minidrivers.
Clarifies the minidriver’s role in a layered architecture, by showing what lives above and below it.
Describes the nature of resources available to the minidriver.

Anatomy of the Sample Minidriver

Provides a table that illustrates the anatomy of this sample minidriver.

Event-driven Walkthrough of the Sample Minidriver

Provides helpful commentary on the sample source code.
Identifies those portions of the minidriver that the user needs to adapt to meet their particular device requirements.

References

References to material helpful toward understanding this sample minidriver.
A reference to other Microsoft-provided sample minidrivers.

Background Notes

A minidriver is a hardware-specific DLL that uses a Microsoft-provided class driver to accomplish most actions through function calls, and provides only device-specific controls. Under WDM, the minidriver registers each adapter with the class driver, and the class driver creates a device object to represent each adapter that registers. The registration process is described in WDM Design Notes and Reference. The minidriver uses the class driver’s device object to make system calls.

A WDM USB device driver communicates with a WDM USB stack through an IRP interface. There are two ways to call DDIs:

·	The client device driver passes USB Request Block (URB) structures to the next-lower driver as a parameter in an IRP with Irp->MajorFunction set to IRP_MJ_INTERNAL_DEVICE_CONTROL and the next IRP stack location Parameters.DeviceIoControl.IoControlCode field set to IOCTL_INTERNAL_USB_SUBMIT_URB.

·	The client device driver passes an IRP with Irp->Majorfunction set to IRP_MJ_INTERNAL_DEVICE_CONTROL, and the next IRP stack location Parameters.DeviceIoControl.IoControlCode field set to one of the other IOCTL_INTERNAL_USB_ function codes.

The client device driver and bus driver share information in the common structures USBD_INTERFACE_INFORMATION and USBD_PIPE_INFORMATION.

I/O Request Packet (IRP) Transfers. IRPs are passed to the next lower driver by using the WDM function IoCallDriver with the device object of the next lower driver as a parameter.The device object of the next lower driver for all USB client device drivers is the DeviceObject returned from the call to IoAttachDeviceToStack.

USB Request Block (URB) Transfers. Clients send these requests to the bus by including them in an IRP a pointer to a URB structure; a function code within the URB identifies the specific request. For transfer requests, multiple URB structures may be linked and passed in with a single IRP. The USB driver stack components assume all URB structures passed to them are allocated from the nonpaged pool.

Common URB Header Structure. Different URB structures are defined for each function. However, every URB has a common header, _URB_HEADER. The header portion of a URB must always be initialized with the input parameters Length and Function, and will always return the output parameter Status.

Bandwidth Allocation. Bandwidth allocation occurs through the process of selecting a configuration or interface and acquiring open pipe handles. While a driver holds an open handle for a specific pipe, the bandwidth necessary to transfer data on that pipe (based on maximum packet size and service interval) is reserved.

IOCTL Codes. For a discussion of the IOCTL codes that a USB client device driver must use, see USB Driver and Minidriver Design Notes and Reference.

URB Transfer Requests. For a discussion of URB transfer requests: transfer flags, status codes, halt/stall behavior, and linked URBs, see USB Driver and Minidriver Design Notes and Reference.

Notes on Writing USB Device Minidrivers

·	[need notes???]

This section has described general issues relevant to writing USB device minidrivers. Now you are ready to start looking at the SONYDCR source code. The following section is an “anatomy” of the sample minidriver code in terms of C modules and driver entry points.

Anatomy of the Sample Minidriver

After you install the WDM DDK, the following source code files can be located at [path to be determined].

| I82930.c | Shows how a driver gets loaded, and how it submits requests to the USB Driver Interface. |
| --- | --- |

After you install the WDM DDK, the following header files can be located at [path to be determined].

| I82930.h | Contains structures that are samples of information that could be used in a device extension structure. |
| --- | --- |

These sample files are heavily commented, to aid the user in understanding their purpose and their relationship to the stream class driver. Documentation for the DDIs referenced below may be found in USB Driver and Minidriver Design Notes and Reference, in WDM Design Notes and Reference, or in the source code files for the sample minidriver, listed above. Documentation for the class driver DDIs can be quickly found by looking to the Table of Contents for these documents. When DDIs are part of the sample minidriver source code, their file locations are noted in parentheses.

| Minidriver DDI | Description |
| --- | --- |
| NTSTATUS DriverEntry( IN PDRIVER_OBJECT DriverObject, IN PUNICODE_STRING RegistryPath ); | Installable driver initialization entry point. This entry point is called directly by the I/O system. |
| NTSTATUS I82930_Dispatch( IN PDEVICE_OBJECT DeviceObject, IN PIRP Irp ); | Process the IRPs sent to this device. |
| VOID I82930_Unload( IN PDRIVER_OBJECT DriverObject ); | Free allocated resources. |
| NTSTATUS I82930_StartDevice( IN PDEVICE_OBJECT DeviceObject ); | Initializes a given instance of the device on the USB. The device descriptor is obtained and stored. |
| NTSTATUS I82930_RemoveDevice( IN PDEVICE_OBJECT DeviceObject ); | Stops a given instance of an 82930 device on the USB. |
| NTSTATUS I82930_StopDevice( IN PDEVICE_OBJECT DeviceObject ); | Stops a given instance of an 82930 device on the USB. |
| NTSTATUS I82930_PnPAddDevice( IN PDRIVER_OBJECT DriverObject, IN PDEVICE_OBJECT PhysicalDeviceObject ); | Creates a new instance of the device. |
| NTSTATUS I82930_CreateDeviceObject( IN PDRIVER_OBJECT DriverObject, IN PDEVICE_OBJECT *DeviceObject, LONG Instance ); | Creates a FunctionalDeviceObject. |
| NTSTATUS I82930_CallUSBD( IN PDEVICE_OBJECT DeviceObject, IN PURB Urb ); | Passes a URB to the USBD class driver. |
| NTSTATUS I82930_ConfigureDevice( IN PDEVICE_OBJECT DeviceObject ); | Initializes a given instance of the device on the USB and selects the configuration. |
| NTSTATUS I82930_SelectInterface( IN PDEVICE_OBJECT DeviceObject, IN PUSB_CONFIGURATION_DESCRIPTOR ConfigurationDescriptor, PUSB_INTERFACE_INFORMATION Interface ); | Initializes an 82930 with multiple interfaces. |
| VOID I82930_Cleanup( PDEVICE_OBJECT DeviceObject (; | ??? |
| NTSTATUS I82930_BuildPipeList( IN PDEVICE_OBJECT DeviceObject ); | ??? |
| NTSTATUS I82930_ResetPipe( IN PDEVICE_OBJECT DeviceObject, IN PI82930_PIPE Pipe ); | Reset both pipes associated with a video channel on the camera. |
| VOID I82930_DecrementIoCount( IN PDEVICE_OBJECT DeviceObject ); | ??? |
| VOID I82930_IncrementIoCount( IN PDEVICE_OBJECT DeviceObject ); | ??? |

Event-driven Walkthrough of the Sample Minidriver

The following steps briefly describe ??????????????????? for the sample USB device minidriver. The sample minidriver routines mentioned here are described in greater detail in the comments of the sample source code and in routine-specific notes that follow.

1.	[need event-driven walkthrough]

References

Documentation for the class driver DDIs can be quickly found by looking to the Table of Contents for WDM Design Notes and Reference, or USB Driver and Minidriver Design Notes and Reference. However, some DDIs need additional documentation when viewed in the context of this sample minidriver.

LIST THEM HERE

Reference to Other Microsoft-supplied Samples

The following Microsoft-supplied minidrivers are available as part of this Memphis DDK.

SCSAMPLE: Stream Class Sample Minidriver Design Notes documents the SCSAMPLE sample minidriver. The location of the sample source code is given in that document. (need info on demonstration value of this minidriver)