ipseccmd.exe 
IP Security Policy Configuration Tool

#### Contents

Introduction

Command-line Syntax

Tips and Examples for Using IPSECCMD

Notes and Caveats

Feedback

# Introduction

IPSECCMD  is a command line tool used to configure IP Security policies in the Directory Service, or in a local or remote registry.  It does almost everything that the

IP Security MMC snap-in does, and is even modeled after the snap-in.

In addition, it can query IPSec Security Policies Database (SPD) and display the current state of IPSec Services

IPSECCMD has three mutually exclusive modes: static, dynamic, and query

Dynamic mode will plumb policy into the IPSec Services Security Policies Database. The policy will be persisted, ie. it will stay after a reboot.  The benefit of dynamic mode is that the policy can co-exist with DS based policies, which overrides any local policy not plumbed by ipseccmd.

To delete all dynamic policies, execute "ipseccmd -u" command

When the tool is used in static mode, it creates or modifies stored policy.

This policy can be used again and will last the lifetime of the store.  This is the mode that the IP Security MMC snap-in uses.

In query mode, the tool queries IPSec Security Policies Database.

WHY WOULD YOU WANT TO USE IPSECCMD?

*  You have a large and/or complex IPSec policy that you want to

configure.  IPSECCMD can help you by providing a scriptable way to

create that policy.  Just put your IPSECCMD commands into a batch file.

This also provides a backup in case you lose the DS or registry that

the policy is stored in.  Just re-run the batch file.

*   IPSECCMD facilitates just in time policy with it's batch ability.

If someone wants a secured channel with your server, simply send them

the tool binaries and the command line or batch file to run.

*   Your machine is using DS policy and you want to add rules

that will allow you to speak IPSec to machines not covered in the

DS policy.  Dynamic mode of IPSECCMD will achieve this for you.

*   You prefer command line tools to GUI apps.

For a more thorough explanation of IP Security policy terminology, see the online Help for the IP Security MMC snap-in.

# Command Reference

USAGE:

ipseccmd \\machinename -f FilterList -n NegotiationPolicyList -t TunnelAddr

-a AuthMethodList -1s SecurityMethodList -1k Phase1RekeyAfter -1p

-1f MMFilterList -1e SoftSAExpirationTime -soft -confirm

[-dialup OR -lan]

{-w TYPE:DOMAIN -p PolicyName:PollInterval -r RuleName -x -y -o}

ipseccmd \\\\machinename show filters policies auth stats sas all

BATCH MODE:

ipseccmd -file filename

File must contain regular ipseccmd commands,

all these commands will be executed in one shot.

ipseccmd has three mutually exclusive modes: static, dynamic, and query.

The default mode is dynamic.

Dynamic mode will plumb policy directly into the IPSec Services Security Policies Database. The policy will be persisted, i.e. it will stay after a reboot. The benefit of dynamic policy is that it can co-exist with DS based policy.

To delete all dynamic policies, execute "ipseccmd -u" command

When the tool is used in static mode,

it creates or modifies stored policy.  This policy can be used again and

will last the lifetime of the store. Static mode is indicated by the -w

flag.  The flags in the {} braces are only valid for static mode.  The usage

for static mode is an extension of dynamic mode, so please read through

the dynamic mode section.

In query mode, the tool queries IPSec Security Policies Database.

NOTE: references to SHA in ipseccmd are referring to the SHA1 algorithm.

QUERY MODE

The tool displays requested type of data from IPSec Security Policies Database

filters   - shows main mode and quick mode filters

policies  - shows main mode and quick mode policies

auth      - shows main mode authentication methods

stats     - shows Internet Key Exchange (IKE) and IPSec statistics

sas       - shows main mode and quick mode Security Associations

all       - shows all of the above data

It is possible to combine several flags

EXAMPLE: ipseccmd show filters policies

DYNAMIC MODE

Each execution of the tool sets an IPSec rule, an IKE policy,

or both.  When setting the IPSec policy,  think of it as setting an "IP Security Rule" in the UI.  So, if you need to set up a tunnel policy, you will need

to execute  the tool twice, once for the outbound filters and outgoing tunnel

endpoint, and once for the inbound filters and incoming tunnel endpoint.

OPTIONS:

\\machinename sets policies on that machine.  If not included, the

local machine is assumed.

NOTE: that if you use this it must be the first argument AND

you MUST have administrative privileges on that machine.

-confirm will ask you to confirm before setting policy

can be abbreviated to -c

*OPTIONAL, DYNAMIC MODE ONLY*

The following flags deal with IPSec policy. If omitted, a default value

is used where specified.

-f FilterList

where FilterList is one or more space separated filterspecs

a filterspec is of the format:

A.B.C.D/mask:port=A.B.C.D/mask:port:protocol

you can also specify DEFAULT to create default response rule

The Source address is always on the left of the '=' and the Destination

address is always on the right.

MIRRORING: If you replace the '=' with a '+' two filters will be created,

one in each direction.

mask and port are optional.  If omitted, Any port and

mask 255.255.255.255 will be used for the filter.

You can replace A.B.C.D/mask with the following for

special meaning:

0 means My address(es)

* means Any address

a DNS name (NOTE: multiple resolutions are ignored)

a GUID of the local network interface in the form

{12345678-1234-1234-1234-123456789ABC}

GUIDs are NOT supported for static mode

protocol is optional, if omitted, Any protocol is assumed.  If you

indicate a protocol, a port must precede it or :: must preceded it.

NOTE BENE: if protocol is specified, it must be the last item in

the filter spec.

Examples:

Machine1+Machine2::6 will filter TCP traffic between Machine1 and Machine2

172.31.0.0/255.255.0.0:80=157.0.0.0/255.0.0.0:80:TCP will filter

all TCP traffic from the first subnet, port 80 to the second subnet,

port 80

PASSTHRU and DROP filters: By surrounding a filter specification with (),

the filter will be a passthru filter.  If you surround it with [], the

filter will be a blocking, or drop, filter.

Example: (0+128.2.1.1) will create 2 filters (it's mirrored) that will

be exempted from policy.

You can use the following protocol symbols: ICMP UDP RAW TCP

Star notation:

If you're subnet masks are along octet boundaries, then you

can use the star notation to wildcard subnets.

Examples:

128.*.*.* is same as 128.0.0.0/255.0.0.0

128.*.* is the same as above

128.* is the same as above

144.92.*.* is same as 144.92.0.0/255.255.0.0

There is no DEFAULT, -f is required

-n NegotiationPolicyList

where NegotiationPolicyList is one or more space separated

IPSec policies in the one of the following forms:

ESP[ConfAlg,AuthAlg]RekeyPFS[Group]

AH[HashAlg]

AH[HashAlg]+ESP[ConfAlg,AuthAlg]

where ConfAlg can be NONE, DES, or 3DES

and AuthAlg can be NONE, MD5, or SHA

and HashAlg is MD5 or SHA

NOTE: ESP[NONE,NONE] is not a supported config

NOTE: SHA refers the SHA1 hash algorithm

Rekey is number of KBytes or number of seconds to rekey

put K or S after the number to indicate KBytes or seconds, respectively

Example: 3600S will rekey after 1 hour

To use both, separate with a slash.

Example: 3600S/5000K will rekey every hour and 5 MB.

REKEY PARAMETERS ARE OPTIONAL

PFS this is OPTIONAL, if it is present it will enable phase 2 perfect

forward secrecy.  You may use just P for short.

It is also possible to specify which PFS Group to use:

PFS1 or P1, PFS2 or P2

By Default, PFS Group value will be taken from current Main Mode settings

DEFAULT: ESP[3DES,SHA] ESP[3DES,MD5] ESP[DES,SHA]

ESP[DES,MD5]

-t tunnel address in one of the following forms:

A.B.C.D

DNS name

DEFAULT: omission of tunnel address assumes transport mode

-a AuthMethodList

A list of space separated auth methods of the form:

PRESHARE:"preshared key string"

KERBEROS

CERT:"CA Info"

The strings provided to preshared key and CA info ARE case sensitive.

You can abbreviate the method with the first letter, ie. P, K, or C.

DEFAULT: KERBEROS

-soft will allow soft associations

DEFAULT: don't allow soft SAs

-lan will set policy only for lan adapters

-dialup will set policy only for dialup adapters

*BOTH ARE OPTIONAL, if not specified, All adapters are used*

DEFAULT: All adapters

The following deal with IKE phase 1 policy.  An easy way to remember

is that all IKE phase 1 parameters are passed with a 1 in the flag.

If no IKE flags are specified, the current IKE policy

will be used.  If there is no current IKE policy, the defaults

specified below will be used.

-1s SecurityMethodList

where SecurityMethodList is one or more space separated SecurityMethods

in the form:

ConfAlg-HashAlg-GroupNum

where ConfAlg can be DES or 3DES

and HashAlg is MD5 or SHA

and GroupNum is:

1 (Low)

2 (Med)

Example: DES-SHA-1

DEFAULT: 3DES-SHA-2 3DES-MD5-2 DES-SHA-1 DES-MD5-1

-1p enable PFS for phase 1

DEFAULT: not enabled

-1k number of Quick Modes or number of seconds to rekey for phase 1

put Q or S after the number to indicate Quick Modes or seconds,

respectively

Example: 10Q will rekey after 10 quick modes

To use both, separate with a slash.

Example: 10Q/3600S will rekey every hour and 10 quick modes

*OPTIONAL*

DEFAULT: no QM limit, 480 min lifetime

-1e SoftSAExpirationTime

set Soft SA expiration time attribute of the main mode policy

value is specified in seconds

DEFAULT: not set if Soft SA is not allowed

set to 300 seconds if Soft SA is allowed

-1f MMFilterList

set specific main mode filters. Syntax is the same as for -f option

except that you cannot specify passthru, block filters, ports and protocols

DEFAULT: filters are generated automatically based on quick mode filters

STATIC MODE

Static mode uses most of the dynamic mode syntax, but adds a few flags

that enable it work at a policy level as well.  Remember, dynamic mode

just lets you add anonymous rules to the policy agent.  Static mode

allows you to create named policies and named rules.  It also has some

functionality to modify existing policies and rules, provided they were

originally created with ipseccmd.

Static mode is supposed to provide most of the functionality of the IPSec UI

in a command line tool, so there are references here to the UI.

First, there is one change to the dynamic mode usage that static mode

requires.  In static mode, pass through and block filters are indicated

in the NegotiationPolicyList that is specified by -n.  There are three

items you can pass in the NegotiationPolicyList that have special meaning:

BLOCK will ignore the rest of the policies in NegotiationPolicyList and

will make all of the filters blocking or drop filters.

This is the same as checking the "Block" radio button

in the UI

PASS  will ignore the rest of the policies in NegotiationPolicyList and

will make all of the filters pass through filters.

This is the same as checking the "Permit"

radio button in the UI

INPASS will plumb any inbound filters as pass through.

This is the same as checking the "Allow unsecured communication,

but always respond using IPSEC" check box in the UI

Static Mode flags:

All flags are REQUIRED unless otherwise indicated.

-w Write the policy to storage indicated by TYPE:LOCATION

TYPE can be either REG for registry or DS for Directory Storage

if \\machinename was specified and TYPE is REG, will be written

to the remote machine's registry

DOMAIN for the DS case only. Indicates the domain name of the

DS to write to. If omitted, use the domain the local machine is in.

OPTIONAL

-p PolicyName:PollInterval

Name the policy with this string.  If a policy with this name is

already in storage, this rule will be added to the policy.

Otherwise a new policy will be created.  If PollInterval is specified,

the polling interval for the policy will be set.

-r RuleName

Name the rule with this string.  If a rule with that name already exists,

that rule is modified to reflect the information supplied to ipseccmd.

For example, if only -f is specified and the rule exists,

only the filters of that rule will be replaced.

-x will set the policy active in the LOCAL registry case OPTIONAL

-y will set the policy inactive in the LOCAL registry case OPTIONAL

-o will delete the policy specified by -p OPTIONAL

(NOTE: this will delete all aspects of the specified policy

don't use if you have other policies pointing to the objects in that policy)

# Tips and Examples for Using IPSECCMD

At the bare minimum,  you need is to specify at least one flag, otherwise the help kicks in. There are defaults for all flags except -f.  Typically you will always provide –f to specify what filters to apply the policy to.  An exception is for the –y or –x or –u flags, which delete policies or rules.

For tunnel policies, specify your tunnel endpoint with -t.

REMEMBER: each time you run ipseccmd you are plumbing a "rule" into

ipsec.  So for tunnel policies, you'll have to run the tool twice, once for

the inbound and once for the outbound.

DON'T USE MIRRORING (the plus symbol) IN YOUR TUNNEL FILTERS!

Example 1:

Dynamic mode for all traffic from this host to any other host.

ipseccmd -f 0+* -n ah[md5]

will set a mirrored filter of me to any using AH md5.  Uses Kerberos for

oakley auth ON THE LOCAL MACHINE

Example 2:

Setting dynamic policy on a remote machine

ipseccmd \\foobar0 -f foobar+foobar0 -n esp[des,sha]+ah[md5]

-apreshare:tooltime -c

mirrored filter between the two machines named foobar and foobar0,

using and AND proposal and

a preshared key.  SETS POLICY ON \\foobar0

Example 3:

Tunnel Policy

ipseccmd -f 128.2.1.1=128.2.1.13 -t 128.2.1.13 -n ah[sha]

-apreshare:tooltime -1s des40-md5-3 -1p -c

ipseccmd -f 128.2.1.13=128.2.1.1 -t 128.2.1.1 -n ah[sha]

-apreshare:tooltime -1s des40-md5-3 -1p -c

AH tunnel between the two specified IP addresses.  Note the phase 1

security method is set with PFS.  Also uses -confirm, abbriviated.

Example 4:

Using static mode

ipseccmd -w DS -p "Default Domain Policy":30 -r "Secured Servers" -f 0+SecuredServer1

0+SecuredServer2 -n ESP[MD5,DES] AH[MD5] -a KERBEROS P:ace -lan

this would set up a policy in the Directory Service for the domain that the machine

running this command is in.  It sets up a DS based policy for clients

to two secured servers.  Both ESP and AH are sent as security offers and the machines

negotiate which one they will use. Note the use of abbreviation in the authentication methods

(KERBEROS could have been abbreviated as a K) and that this rule is only for LAN interfaces.

Example 5:

Using static mode

ipseccmd -w REG -r "Me to Anyone" -p "Secure My Traffic" -f 0+*

-n AH[MD5] -a P:ace -x

this would set up a local policy that would negotiate properly with the

policy from example 4, so it would be run on SecuredServer1 or SecuredServer2.

Note the use of -x to make the policy active.

Example 6:

Using query  mode

ipseccmd \\RemoteMachine show filters policies

this would show IPSec filters and policies information from the RemoteMachine. You must have administrative rights on RemoteMachine for this command to complete successfully.

Example 7:

Using query  mode

ipseccmd show all

this would show all information from IPSec Security Policies Database (SPD), or the complete IPSec state of the local machine.

# Notes

Important

You must have specific privileges for both dynamic and static mode.  For static mode, you must have read/write access to the storage that you write to in static mode.  For dynamic mode, you must have Administrator privleges on the machine that you are plumbing the dynamic policy to.

For static mode, authorized users can modify the ACLs of the storage to give you access.  IP Security policy objects are stored in:

HKEY_LOCAL_MACHINE\Software\Policies\Microsoft\Windows\IPSec\\Policy\Local

for the local/remote machine case AND

CN=IP Security,CN=System,DC=YourDCName,DC=ParentDCName,DC=TopLevelDC

ie, the IP Security container under the System container

for the Directory Service case.

CAVEATS

- In dynamic mode, if you use a DNS name that resolves to multiple addresses only the first address in the list is used.  This is not a problem in static mode.

- Read the filter spec help carefully, it is the most difficult and easiest to confuse.  In particular, pay attention to how a protocol is specified.