Microsoft WindowsXP
RSNIFF

User Guide

Author: Anthony Leibovitz (tonyle@microsoft.com)

Version 8.1

May 15, 2001

© Copyright Microsoft Corporation, 2001. All Rights Reserved

# Introduction

RSNIFF is a Windows NT service that enables remote users to obtain server-side, on-demand network diagnostic information when using an appropriate RSNIFF client (such as RASDIAG). The information collected includes link-layer Microsoft Network Monitor captures for all enabled interfaces on the host machine and pre-/post- snapshot of various IP-related network configuration values (ie., routing table, ip addresses, etc).

# RSNIFF Service Installation – How to

Prior to installation, please make sure rsniff has not already been installed on your machine. If it has, be sure to ‘net stop rsniff’ prior to re-installing or upgrading.

- Create a directory called C:\RSNIFF

- Copy RNIFF.EXE and RSNIFF.PDB to C:\RSNIFF

- Issue the following command to install RSNIFF: RSNIFF.EXE –i. (If rsniff was previously installed, you must uninstall prior to upgrade. To do this, type ‘rsniff.exe –u’ to uninstall and then ‘rsniff.exe –I’ to re-install.

- To start the server, type ‘net start rsniff’

# How to obtain Network Monitor captures and logs from RSNIFF

- Make sure RSNIFF is installed and ensure that the RSNIFF service is started (ie., ‘net start rsniff’).

- Start the RSNIFF client application (ie., RASDIAG), specifying the IP address of the machine where the RSNIFF service is running. The RSNIFF client application is typically a RAS client / Demand-dial Router that has existing network connectivity (Internet). The RSNIFF service is typically running on the RAS server / Router.

- Once the RSNIFF client has completed it’s work, captures and logs will be stored in a directory under C:\RSNIFF that is designated as: YYYYMMDDHHMMSS-<CLIENT_NAME>-SID_nnn (ie., 0514143648-RASCLIENT2-SID_001).

# RSNIFF Log

The RSNIFF log file is located in C:\RSNIFF. This file contains information on all clients that have attempted a connection to the RSNIFF service as well as details regarding the client’s requests.

# RSNIFF Service Removal – How to

Prior to removal, make sure the service has stopped (‘net stop rsniff’)

- Change to the C:\RSNIFF directory

- Type: ‘rsniff.exe –u’

# Other Options

The following table can be obtained by issuing the command: ‘rsniff.exe -?’. The number in parenthesis below (8.1) represents the internal version number of this tool.

------------------------------------------------

RSNIFF - RAS REMOTE SNIFFING AGENT SERVICE (8.1)

------------------------------------------------

-i         Install RSNIFF service

-u         Uninstall RSNIFF service

-?         This menu

/?         This menu

------------------------------------------------

# Design / General Algorithm Information

To provide the above functionality, RNIFF principally relies on Microsoft’s TCP/IP Winsock API and the IDelaydC COM interface exposed by Microsoft’s Network Monitor Agent Packet Provider. The following pseudo-code outlines the general algorithm for RSNIFF.

- while(accept() != INVALID_SOCKET) // wait for a TCP caller to connect on TCP Port 2222.

- dwCallerID++; // increment unique caller id

- recv(&rc_v5) // receive a structure of sizeof(REMOTE_CAPTURE_V5) bytes; this is the first supported version of RSNIFF

- Determine the version of the incoming client from rc_v5.dwVer and, based on this information, retrieve additional bytes containing information about the client (subsequent structures describing REMOTE_CAPTURE information are larger).

- Convert the received structure to a struct of type REMOTE_CAPTURE

- Write a log file entry indicating that client, pRc5->szMachine has connected and is making a request.

- Create a directory in the install_root called <date>-<clientname>-SID_<dwCallerID>

- if(rc.dwOpt1 & RSNIFF_OPT1_DOSNIFF) ; // enumerate all active network interfaces and start capturing network traffic. Write a log entry indicating a request for a sniff.

- if(rc.dwOpt1 & RSNIFF_OPT1_GETSRVROUTINGINFO) ; // obtain a pre-repro snapshot of the server’s routing information. Store the acquired information in a file called ROUTINGINFO.TXT. This file is stored in the directory created above. Write a log entry indicating a request for routing info.

- recv(1 byte) ; //wait for a single byte to arrive – it never will b/c we’re really waiting for the socket to be closed from the client-side (recv() will return 0). During this time, it is expected that the remote client will do a repro of the problem. Once the repro has occurred, the remote client will close the socket and thus indicate to the RSNIFF server that capturing can be terminated.

- closesocket(s) ; // close the socket that was created.

- if(rc.dwOpt1 & RSNIFF_OPT1_GETSRVROUTINGINFO) ; // obtain a pre-repro snapshot of the server’s routing information. Store the acquired information in a file called ROUTINGINFO.TXT. This file is stored in the directory created above. This is the post-repro version.

- if(rc.dwOpt1 & RSNIFF_OPT1_DOSNIFF) ; // stop capturing network traffic, rename capture files to <orig_capture_name>__rc.szMachine_SID_<dwCallerID>.CAP. Move all captures to the directory created above.

- Write a log entry indicating request is completed.